## Slide 1: Logic Gates
June 2025

## Slide 2: Digital devices vs linear devices
Linear devices are designed for linear response
Digital devices are designed so that the output is one of two values
  Output is proportional to the input
  Output is “on” or “off”
  Output is “high” or “low”
  Output is “1” or “0”

## Slide 3: Digital devices vs linear devices
A brief digression to Linear Electronics

## Slide 4: Common Emitter Amplifier Circuit
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 5V
First calculate the base current
Use the transistor β to calculate the collector current
IC = β IB
Find the voltage drop across the collector resistor
Vdrop = IC RC
Vout = Vcc - Vdrop
What if Vin < VBE,on

## Slide 5: Common Emitter Amplifier Circuit
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
First calculate the base current
= 5V
What if Vin < VBE,on
A) The base current flows in the opposite direction of the arrow.
B) The base current can be calculated using the Shockley equation.
C) The base current flow is zero.
Would you say that:
D) The base current cannot be calculated.
The previous equations are only good for the forward active region.
very small.

## Slide 6: Common Emitter Amplifier Circuit
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 5V
First calculate the base current
Use the transistor β to calculate the collector current
IC = β IB
Find the voltage drop across the collector resistor
Vdrop = IC RC
Vout = Vcc - Vdrop
Vin < VBE,on is the cutoff region.
IB ≈ 0
IC ≈ 0
Vout ≈ VCC
Having an input that is close to 0 V results in an output that is close to the supply voltage.

## Slide 7: Common Emitter Amplifier Circuit
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 5V
First calculate the base current
Use the transistor β to calculate the collector current
IC = β IB
Find the voltage drop across the collector resistor
Vdrop = IC RC
Vout = Vcc - Vdrop
What if Vin ≈ VCC
The transistor is in saturation!
Assume Vin = 4.7 V
IB = 40 μA
IC = 4 mA
Vdrop = 24.8 V ???
Vout = 0.2 V
Having an input that is close to the supply voltage results in an output that is close to 0 V.

## Slide 8: Common Emitter Amplifier Circuit
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 5V
In linear electronics we tried to avoid putting transistors into the cutoff state or the saturation state.
In digital electronics having the transistors in the cutoff state or the saturation state is normal.

## Slide 9: Common Emitter Amplifier Circuit
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 5V
What would happen if we hooked two of these together, using the output from the first stage as the input to the second stage?

## Slide 10: Common Emitter Amplifier Circuit
= 5V
If the input to the first stage is close to 0 V, that transistor will be cut off and the output of that stage will be close to 5 V.
0 V
5 V
That 5V now becomes the input to the second stage, forcing that second transistor into the saturated region and making the output of that stage close to 0 V.
0.2 V

## Slide 11: Common Emitter Amplifier Circuit
= 5V
If the input to the first stage is close to 5 V, that transistor will be saturated and the output of that stage will be close to 0 V.
5 V
0.2 V
That low voltage becomes the input to the second stage, forcing that second transistor into the cut off region and making the output of that stage close to 5 V.
5 V

## Slide 12: Common Emitter Amplifier Circuit
= 5V
This is a (not great) example of a digital logic gate called a NOT gate
A better example of a NOT gate would use more transistors.
The additional transistors would prevent the circuit’s operation from being affected by the current demands of the input and output.

## Slide 13: Types of Digital Devices
Digital devices can be made using different types of transistors and with different arrangements
The most common types of digital logic are TTL (transistor-transistor-logic), CMOS (complementary metal oxide semiconductor), and ECL (Emitter Coupled Logic)
TTL and ECL use bipolar junction transistors (BJTs)

## Slide 14: Choosing a Type of Digital Devices
TTL, CMOS, and ECL each have advantages
Considerations for choosing a device type
  Robustness (static electricity, temperature fluctuations)
  Power dissipation
  Switching speed (propagation delay)
  Noise immunity
  Fanout (how many devices can be connected to it)
  cost

## Slide 15: A CMOS NOT Gate

## Slide 16: A CMOS NOT Gate
.
When the transistor is active, holes (positive charges) conduct the current.
.
When the transistor is active, electrons (negative charges) conduct the current.

## Slide 17: A CMOS NOT Gate

## Slide 18: A CMOS NOT Gate

## Slide 19: A CMOS NOT Gate

## Slide 20: A CMOS NOT Gate

## Slide 21: A CMOS NOT Gate

## Slide 22: A CMOS NOT Gate

## Slide 23: A CMOS NOT Gate

## Slide 24: A CMOS NOT Gate
0

## Slide 25: A CMOS NOT Gate
The inner details of how a CMOS NOT gate (inverter) works are different than the inner details of how a TTL NOT gate (inverter) works.
From an external perspective the circuits act the same – an input near the supply voltage causes an output near zero, and an input near zero causes an output near the supply voltage.
What is meant by “near the supply voltage” and “near zero” will be different for the different types of digital logic gates.

## Slide 26: Comparing “High” and “Low” for TTL and CMOS
0.8 V
0.5 V
2.0 V
2.7 V
0.0 V
5.0 V
low noise margin
high noise margin
TTL
Acceptable Input Signal Levels
Acceptable Output Signal Levels
noise margin – the amount of noise that can be added to an acceptable output signal with the signal still being recognizable by the next stage.

## Slide 27: Comparing “High” and “Low” for TTL and CMOS
0.8 V
0.5 V
2.0 V
2.7 V
0.0 V
5.0 V
low noise margin
high noise margin
TTL Stage 1
Acceptable Input Signal Levels
Acceptable Output Signal Levels
0.8 V
0.5 V
2.0 V
2.7 V
0.0 V
5.0 V
low noise margin
high noise margin
TTL Stage 2
Acceptable Input Signal Levels
Acceptable Output Signal Levels
input


## Slide 28: Comparing “High” and “Low” for TTL and CMOS
CMOS
(5 V Supply)
1.5 V
0.05 V
3.5 V
4.95 V
0.0 V
5.0 V
low noise margin
high noise margin
Acceptable Input Signal Levels
Acceptable Output Signal Levels
Acceptable Output Signal Levels
Acceptable Input Signal Levels
CMOS
(5 V Supply)
1.5 V
0.05 V
3.5 V
4.95 V
0.0 V
5.0 V
low noise margin
high noise margin

## Slide 29: Comparing “High” and “Low” for TTL and CMOS
0.8 V
0.5 V
2.0 V
2.7 V
0.0 V
5.0 V
low noise margin
high noise margin
TTL
CMOS
(5 V Supply)
1.5 V
0.05 V
3.5 V
4.95 V
0.0 V
5.0 V
low noise margin
high noise margin
Acceptable Input Signal Levels
Acceptable Output Signal Levels
Acceptable Output Signal Levels
Acceptable Input Signal Levels
An acceptable output from TTL might not be an acceptable input signal for CMOS

## Slide 30
In general, we don’t need to know the differences between logic types.
We need to know that there ARE differences between logic types so that we don’t cause problems with mixing them.

## Slide 31: Boolean Algebra
Boolean algebra only uses two values.
We can also ignore the details of what the exact voltages are in the circuit
If the inputs and outputs follow the rules of Boolean algebra and if we don’t mix logic types, the intermediate details are not critical
By using Boolean algebra, we can ignore the details of exactly what voltages constitute “true” and “false”
True
False

## Slide 32: TTL AND Gate
= 5V

## Slide 33: TTL AND Gate Using Boolean Algebra
x1
x2
output

## Slide 34: Inputs and Outputs
Most logic gates will have multiple (usually two) input signals and one output signal.
The inputs and the outputs are treated as binary digits.
1 = “high”
0 = “low”
1 ≠ 1 Volt
  Exception: The NOT gate only has one input.

## Slide 35: Basic Logic Gates
June 2025

## Slide 36: Basic Logic Gates
NOT
AND
OR
XOR

## Slide 37: NOT Logic Gates
x1
output
The output is the opposite of the input
Truth Table
x1 | output
0 | 1
1 | 0
Also called an inverter.
Also called forming a complement
symbol
1 does not mean 1 volt. It means a value that is close to the supply voltage.

## Slide 38: AND Logic Gates
x1
x2
output
The output is TRUE only if both of the inputs are TRUE
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Every possible combination of logical inputs.
TRUE = 1

## Slide 39: 3 input AND Logic Gate
x1
x2
output
The output is TRUE only if all of the inputs are TRUE
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
x3
Every possible combination of logical inputs.

## Slide 40: Equivalent Circuit for 3 input AND Logic Gate
The output is TRUE only if all of the inputs are TRUE
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
x1
x2
output
x3
x1 | x2 | output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
For every combination of inputs here, there are two rows here.

## Slide 41: OR Logic Gates
x1
x2
output
The output is TRUE if at least one input is TRUE
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 42: 3 input OR Logic Gate
x1
x2
output
The output is TRUE if at least one input is TRUE
Truth Table
x3
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1

## Slide 43: Equivalent Circuit for 3 input OR Logic Gate
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x1
x2
output
x3
The output is TRUE if at least one input is TRUE

## Slide 44: XOR Logic Gates
x1
x2
output
The output is TRUE if an odd number of inputs are TRUE
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 45: Odd and Even Numbers
A number is odd if there is a remainder when you divide the number by 2
1
2
3
4
5
6
7
8
9
A number is even if there is no remainder when you divide the number by 2

## Slide 46: XOR Logic Gates
The output is TRUE if an odd number of inputs are TRUE
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x1
x2
output

## Slide 47: XOR Logic Gates
The output is TRUE if one and only one input is TRUE ???
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x1
x2
output
The output is TRUE if an odd number of inputs are TRUE
Are these equivalent?
We said:
Some people say:
For a two input XOR gate, they are equivalent.

## Slide 48: 3 input XOR Logic Gate
x1
x2
output
Truth Table
x3
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1
The output is TRUE if an odd number of inputs are TRUE
The output is TRUE if one and only one input is TRUE ???
The bottom statement is not true for XOR gates with more than two inputs

## Slide 49: 3 input XOR Logic Gate
The output is TRUE if an odd number of inputs are TRUE
The output is TRUE if one and only one input is TRUE ???
Be careful when you use XOR gates with more than two inputs.
All commercial devices that I have seen use this.
I have heard that some emulation software uses this.

## Slide 50: Equivalent Circuit for 3 input XOR Logic Gate
The output is TRUE only if an odd number of the inputs are TRUE
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x1
x2
output
x3

## Slide 51: More Logic Gates
NAND
NOR
XNOR
Equivalent to AND followed by NOT
Equivalent to XOR followed by NOT
Equivalent to OR followed by NOT

## Slide 52: NAND Logic Gates
The output is FALSE only if both of the inputs are TRUE
Truth Table
x1 | x2 | AND output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1
x2
output
x1 | x2 | AND output | NAND output
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
x1
x2
output
Equivalent Circuit

## Slide 53: NOR Logic Gates
The output is FALSE if at least one input is TRUE
Truth Table
x1 | x2 | OR output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x1
x2
output
x1 | x2 | OR output | NOR output
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
x1
x2
output
Equivalent Circuit

## Slide 54: XNOR Logic Gates
Truth Table
x1 | x2 | XOR output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
The output is FALSE if an odd number of inputs are TRUE
x1
x2
output
x1
x2
output
Equivalent Circuit
x1 | x2 | XOR output | XNOR output
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 55: XNOR Logic Gates
Truth Table
x1 | x2 | XOR output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
The output is TRUE if an even number of inputs are TRUE
x1
x2
output
x1
x2
output
Equivalent Circuit
x1 | x2 | XOR output | XNOR output
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 56: Review of the Gates

## Slide 57: Basic Logic Gates
NOT
AND
OR
XOR
x1 | output
0 | 1
1 | 0
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x1 | x2 | output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 58: The Other Logic Gates
NAND
NOR
XNOR
x1 | x2 | output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x1 | x2 | output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x1 | x2 | output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 59: Combinational Circuits
June 2025

## Slide 60: Analysis of Digital Circuits
A truth table can describe the operation of a digital logic circuit
Truth Table
x1 | x2 | output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x1
x2
output

## Slide 61: Analysis of Digital Circuits
Sometimes it is useful to put intermediate results in our truth table.
Truth Table
x1 | x2 | A | B | output
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
x1
x2
A
B
output
1
1
0
0
0
0
0
1
1
1
0
1

## Slide 62
Let’s look at a different Circuit

## Slide 63: Analysis of Digital Circuits
What is the truth table to describe the operation of this circuit?
x1
x2
A
output
Truth Table
x1 | x2 | A | output
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
1
1
0
0
1
1
0
1

## Slide 64: Functionally Equivalent Circuits
x1
x2
A
B
output
x1
x2
A
output
Two circuits are functionally equivalent if they have the same output for every combination of inputs

## Slide 65
Using simpler circuits that do the same job saves money.
One way to find simpler equivalent circuits is to use Boolean algebra.

## Slide 66: Boolean Algebra
Boolean algebra deals with variables that can only have one of two values
True
False
Various axioms and theorems are used to manipulate the variables to find equivalent Boolean expressions
Complex circuits can be designed and analyzed using Boolean algebra
1
0
Normal Math
2 x 4 = 8
2 + 3 = 5
Boolean Algebra
1 x 1 = 1
0 + 1 = 1
rules

## Slide 67: Boolean Algebra Tables
Multiplication
x1 | x2 | x1*x2
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Addition
x1 | x2 | x1+x2
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Negation
(Complement)
x1 | x1
0 | 
1 | 
The line over top means negation or complement
What truth table is the equivalent of this one?
0
0
0
1
0
1
1
1
1
0

## Slide 68: The AND Gate is Equivalent to Boolean Multiplication
Equivalent Boolean expression: x1 * x2
x1
x2
output
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
This is often written with implied multiplication: x1 x2
x1 * x2

## Slide 69: Boolean Algebra Tables
Multiplication
x1 | x2 | x1*x2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Addition
x1 | x2 | x1+x2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Negation
(Complement)
x1 | x1
0 | 1
1 | 0
What truth table is the equivalent of this one?

## Slide 70: The OR Gate is Equivalent to Boolean Addition
Equivalent Boolean expression: x1 + x2
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x1 + x2
x1
x2
output

## Slide 71: Boolean Algebra Tables
Multiplication
x1 | x2 | x1*x2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Addition
x1 | x2 | x1+x2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Negation
(Complement)
x1 | x1
0 | 1
1 | 0
What truth table is the equivalent of this one?

## Slide 72: The NOT Gate is Equivalent to Boolean Negation (Complement)
Equivalent Boolean expression: x1
Truth Table
x1 | output
0 | 1
1 | 0
x1
output
x1
We say the variable name (including subscript) and then “bar”
Or we might say “NOT” and then the variable name

## Slide 73: XOR
The XOR gate does not have a single Boolean operation that is directly equivalent
We can form a compound expression that is equivalent of the XOR gate
We will postpone this until we talk about how to form a Boolean expression directly from a truth table

## Slide 74: Find the Boolean Expressions for the Functionally Equivalent Circuits
x1
x2
A
x
y
x1
x2
A
B
x
y
What are the Boolean expressions for each of these circuits?

## Slide 75: Find the Boolean Expressions for the Functionally Equivalent Circuits
x1
x2
x
y
x1
x2
x
y
x + y
x y
x
x + x y
x

## Slide 76
We can use Boolean algebra to reduce the complexity of the first circuit, finding a simpler equivalent circuit.
First we need to learn some Boolean algebra theorems.

## Slide 77: Boolean Algebra
There are three slides of theorems.
Some of these theorems will seem obvious because they are the same as normal algebra.
Some will not be obvious and will be more difficult.
Some are very important. I will point those out to you.

## Slide 78: Boolean Algebra
We will soon learn a graphical method of applying these theorems.
The graphical method will make it less important to know very many of the theorems.
Some you will rarely use. You can look them up if you need them.
I only list those (rarely used) theorems so that you will have a reference.

## Slide 79: Boolean Algebra Theorems for One Variable
x * 0 = 0
x + 1 = 1
x * 1 = x
x + 0 = x
x * x = x
x + x = x
x * x = 0
x + x = 1
x = x
x
0
0
x
1
x
x
x
x
x
1
1
x
0
x
x
x
x
For each theorem, if you replace every ‘*’ with a ‘+’, every ‘+’ with a ‘*’ (using appropriate parentheses), every ‘1’ with a ‘0’, and every ‘0’ with a ‘1’, the resulting statement will be true.
Duality:
x
x
0
x
x
1

## Slide 80: Boolean Algebra Theorems Using Multiple Variables
x*y = y*x
x + y = y + x
x * (y*z) = (x*y)*z
x * (y+z) = x*y + x*z
x + x * y = x
commutative
x + (y+z) = (x+y)+z
associative
x + (y*z) = (x+y)*(x+z)
distributive
x *(x + y)= x
absorption
x*y + x*y = x
(x+y) * (x+y) = x
combining

## Slide 81: More Boolean Algebra Theorems
DeMorgan’s
consensus
x*y = x + y
x + y = x * y
x + x * y = x + y
x *( x + y) = x * y
x*y + y*z+ x*z = x*y + x*z
(x+y) * (y+z) *(x + z) = (x+y)*(x + z)

## Slide 82
Putting it into practice

## Slide 83: Now use Boolean algebra to show that these are functionally equivalent circuits
x1
x2
A
B
x + x y
x
y
x1
x2
A
x
y
x + y
Simplify

## Slide 84
x + x * y = x + y
One of the Boolean theorems states:
This equation for the first circuit is
x + x y
We can make the first equation match the theorem by substituting z = x

## Slide 85
If we let z = x then z = x
x + x y
Now this is the same form as the theorem
= z + y
Substitute into the expression x + x y
= x + y
This is the same expression that we had for the second circuit.
Apply the theorem
Substitute
= x
x + x * y = x + y
Boolean theorem:
= z + z y

## Slide 86
If we let z = x then z = x
x + x y = z + z y
Now this is the same form as the theorem
= z + y
Substitute into the expression x + x y
= x + y
This is the same expression that we had for the second circuit.
Apply the theorem
Substitute
= x
x + x * y = x + y
Boolean theorem:

## Slide 87
We can find an expression for a function directly from the truth table
There are two different ways of finding a Boolean expression directly from the truth table.
Sum of Products (SOP)
Product of Sums (POS)

## Slide 88: Finding Logical Networks from the Truth Table
Sum of Products:
input variables
output
example:
f =x y z+ x y z + x y z
x
y
z
x
z
Sum
Products
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 89: Finding Logical Networks from the Truth Table
Sum of Products:
input variables
output
example:
f =x y z+ x y z + x y z
x
y
z
x
z
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 90: Finding Logical Network from Truth Table
Truth Table
x1 | x2 | output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Sum of Products:
This function is TRUE if these conditions are true
minterms describe the conditions of the variables for each line of the table
x1x2
x1x2
x1x2
x1x2
minterms
This function is TRUE if these conditions are true OR if these conditions are true
This function is TRUE if these conditions are true OR if these conditions are true OR if these conditions are true
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 91: Finding Logical Network from Truth Table
For each row that has a 1 for the output, form the minterm that is the product of the states of the variables
Truth Table
x1 | x2 | output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x1x2
x1x2
x1x2
minterms
We do not need to include this minterm, since in the truth table the output is zero.
f = x1x2 + x1x2 + x1x2
Now add (OR) the minterms together to get the function
Sum of Products:
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 92: An Implementation of the Function
x1
x2
f = x1x2 + x1x2 + x1x2
products
sum

## Slide 93: An Implementation of the Function
products
sum
x1
x2
f = x1x2 + x1x2 + x1x2
x1
x2
x1x2
x1x2
x1x2

## Slide 94: An Implementation of the Function
x1x2
x1x2
x1x2
x1
x2
f = x1x2 + x1x2 + x1x2
products
sum

## Slide 95: Finding Logical Network from Truth Table
f = x1x2 + x1x2 + x1x2
The SOP formulation will always allow you to develop a circuit, but it will likely not be the simplest circuit.
It would be better to use Boolean algebra to reduce the function first.

## Slide 96: Using Boolean Algebra to Reduce the Truth Table Function
f = x1x2 + x1x2 + x1x2
Using distributive law
f = x1x2 + (x1 + x1)x2
f = x1x2 + (1)x2
f = x1x2 + x2
since x + x * y = x + y
since x + x = 1
since 1 * x = x
f = x1 + x2
This is the equivalent expression (we have used the variables x1 and x2 instead of x and y)
x = x2
y = x1
f = yx + x
x = x2

## Slide 97: Implementation of the Original Function
x1x2
x1x2
x1x2
x1
x2
f = x1x2 + x1x2 + x1x2
f = x1x2 + x1x2 + x1x2

## Slide 98: Implementation of Reduced Function
f = x1 + x2
x1
x2

## Slide 99: Revisiting the example problem
Truth Table
x | y | z | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
This is the circuit that we drew before
f =x y z+ x y z + x y z
The same technique can be used for larger truth tables (more variables)

## Slide 100: Finding Logical Networks from the Truth Table
Sum of Products:
input variables
output
example:
f =x y z+ x y z + x y z
x
y
z
x
z
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 101: Revisiting the example problem
Truth Table
x | y | z | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
The function can be reduced with Boolean Algebra
f =x y z+ x y z + x y z
f =x y z+ x y( z + z)
f =x y z+ x y
f =(x z+ x )y
f =(z+ x )y
f = z y + x y

## Slide 102: Finding Logical Networks from the Truth Table
Sum of Products:
input variables
output
example:
f =x y z+ x y z + x y z
z
y
x
f = z y + x y
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 103: Summary of Sum of Products
Using the SOP technique allowed us to write a Boolean function directly from the truth table
Boolean algebra allowed us to simplify the expression
We can implement the function using logic gates.
  We could implement the function directly from the SOP
  We could implement the reduced function

## Slide 104: Boolean Logic for Other Gates
Now that we know how to write functions from truth tables, we can write expressions for the rest of the logic gates.

## Slide 105: XOR Gate Equivalent Expression
Equivalent Boolean expression: x1 x2 + x1 x2
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x1
x2
output

## Slide 106: NAND Logic Gates
Truth Table
x1 | x2 | NAND output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x1
x2
output
f = x1x2
f = x1x2 + x1x2 + x1x2
f = x1(x2 + x2) + x1x2
f = x1+ x1x2
f = x1+ x2

## Slide 107: NOR Logic Gates
Truth Table
x1 | x2 | NOR output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x1
x2
f = x1x2
output

## Slide 108: XNOR Logic Gates
Truth Table
x1 | x2 | XNOR output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x1
x2
f = x1x2+ x1x2
output

## Slide 109
NAND gates and NOR gates use fewer transistors than AND gates and OR gates
Any logic function can be synthesized using just NAND gates or just NOR gates

## Slide 110: Sum of Products can use just NAND Gates
Sum of Products:
output
inputs
Equivalent Sum of Products Using NAND Gates:
inputs
Replace AND gates with NAND gates
Replace OR gate with NAND gate
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.