## Slide 1: Product of Sums
June 2025

## Slide 2: Finding Logical Network from Truth Table
Truth Table
x1 | x2 | output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Sum of Products:
This function is TRUE if these conditions are true
What makes the function true?
x1x2
x1x2
x1x2
minterms
This function is TRUE if these conditions are true OR if these conditions are true
This function is TRUE if these conditions are true OR if these conditions are true OR if these conditions are true
f = x1x2 + x1x2 + x1x2
Product of Sums:
What makes the function false?
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 3: Finding Logical Networks from the Truth Table
Product of Sums:
input variables
example:
f =( x + y + z)*(x + y + z )
output
What it looks like
x
y
z
x
z
multiplication
AND
addition
OR
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 4: Understanding Product of Sums
Is Tony awake?
At the grocery store
At the movies
At a friend’s house
At the park
At the mall
Out for a walk
At work
At the library
In his bed
Laying on his couch
If Tony is awake, he would be:
If Tony is asleep, he would be:
or
or
or
or
or
or
or
or
asleep = awake

## Slide 5: Example
Truth Table
x | y | z | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
f =(x + y+ z)*(x +y + z)
If this is true
If the inputs do not match the first line with an output of 0
If this is true,
and
if the inputs do not match the second line with an output of 0,
the only options left are for the function to be true.
the inputs do not match
this line
the inputs do not match this line
All possible inputs

## Slide 6: Example – Proof that it works
Truth Table
x | y | z | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Find minterms that make function false
f = x y z + x y z
f = x y z + x y z
Negate both sides
DeMorgan’s Theorem
f = x y z · x y z
f = ( x + y + z )·( x + y + z )
DeMorgan’s Theorem
f = ( x + y + z )·( x + y + z )
Maxterms

## Slide 7: Finding Logical Networks from the Truth Table
Product of Sums:
input variables
example:
f =( x + y + z)*(x + y + z )
output
What it looks like
x
y
z
x
z
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 9: Example 2 Two or more of three bits are set
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
( x1+x2+x3)
( x1+x2+x3)
( x1+x2+x3)
Maxterms
Each Maxterm corresponds to the conditions that cause a line of the truth table to NOT be met.

## Slide 10: Example 2 Two or more of three bits are set
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
( x1+x2+x3)
( x1+x2+x3)
( x1+x2+x3)
Maxterms
Form the product of sums (POS) by multiplying all of the maxterms corresponding to the lines of the truth table for which the function equals zero

## Slide 11: Example 2 Two or more of three bits are set
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Product of Sums (POS)
f = (x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)
Form the product of sums (POS) by multiplying all of the maxterms corresponding to the lines of the truth table for which the function equals zero

## Slide 12: Example 2 Two or more of three bits are set
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
f = (x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)
This sum is TRUE if the conditions of the first line are NOT met
This sum is TRUE if the conditions of the second line are NOT met
This sum is TRUE if the conditions of the third line are NOT met
This sum is TRUE if the conditions of the fifth line are NOT met
This statement of the function is saying that the function is true if each of the conditions for being false is untrue.

## Slide 13: Example 2 Two or more of three bits are set
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
f = (x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)
We can build a circuit to implement this function, but it will not be the lowest cost. We can use Boolean algebra to reduce the complexity.

## Slide 14: Example 2
f = (x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)
First let’s design the circuit to show that it can be done
x3
x1
x2
x1
x2
x3
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)
(x1+x2+x3)

## Slide 15: Example 2
Now work on reducing the complexity.
Very soon we will learn other techniques that simplify this procedure. Just view this as a demonstration of the capabilities of Boolean algebra. Don’t worry about figuring out how to do this part by yourself.

## Slide 16: Example 2
f = (x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)*(x1+x2+x3)
Now work on reducing the complexity.
(x+y) * (x+y) = x
using theorem
f = (x1+x2)*(x1+x2+x3)*(x1+x2+x3)
distribute (x1+x2)
(x+y) * (x+y) = x
using theorem
f =[(x1+x2)*(x1+x2 ) + (x1+x2) x3] *(x1+x2+x3)
f =[x1+ (x1+x2) x3] *(x1+x2+x3)

## Slide 17: Example 2
distribute (x3)
(x+ xy) = x
using theorem
f =[x1+ (x1+x2) x3] *(x1+x2+x3)
f =[x1+ x1 x3 +x2 x3] *(x1+x2+x3)
f =[x1+ x2 x3] *(x1+x2+x3)
distribute
f =[x1x1 + x1 x2 x3 + x1 x2 + x2 x2 x3 +x1x3 + x2 x3 x3]

## Slide 18: Example 2
f =[x1x1 + x1 x2 x3 + x1 x2 + x2 x2 x3 + x2 x3 x3 +x1x3]
f =[ x1 x2 x3 + x1 x2 + x2 x3 + x2 x3 +x1x3]
(x x) = 0 and (x x) = x
using theorems
x + x = x
using theorem
f =[ x1 x2 x3 + x1 x2 + x2 x3 +x1x3]
f =[ x1 x2 x3 + x2 x3 + x1 x2 +x1x3]
commutative theorem
(x+ xy) = x
using theorem
f =[x2 x3 + x1 x2 +x1x3]

## Slide 19: Simplified Circuit
x1x2
x1
x2
x3
x2x3
x1x3
f = x2 x3 + x1 x2 +x1x3

## Slide 20: Important Points
The logic functions of truth tables can be implemented in either sum of products (SOP) or product of sums (POS) formats
SOP implementation uses possibly NOT gates and then AND gates followed by OR gates
POS implementation uses possibly NOT gates and then OR gates followed by AND gates
Either SOP or POS can be obtained directly by inspection of the truth table

## Slide 21: Important Points
Neither SOP or POS formats will likely be the smallest possible circuit
Circuit complexity can be reduced by using Boolean algebra
While the Boolean algebra reduction may be easy for small truth tables, for larger tables it becomes increasingly difficult
There is an easier method for larger truth tables. This method of Karnaugh maps will be covered next

## Slide 22
NAND gates and NOR gates use fewer transistors than AND gates and OR gates
Any logic function can be synthesized using just NAND gates or just NOR gates

## Slide 23: Product of Sums can use just NOR Gates
Product of Sums:
inputs
Equivalent Product of Sums Using NOR Gates:
inputs
output
Replace OR gates with NOR gates
Replace AND gate with NOR gate
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 24: Product of Sums can use just NOR Gates
Product of Sums:
inputs
Equivalent Product of Sums Using NOR Gates:
inputs
output
Replace OR gates with NOR gates
Replace AND gate with NOR gate
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 25: Example using NOR gates for POS
Product of Sums:
input variables
example:
f =( x + y + z)*(x + y + z )
output
x
y
z
x
z
f =( x + y + z) + (x + y + z )
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 26
Practice Problems

## Slide 27: Problem 1: Write the POS formulation for this truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Draw a circuit that implements the function using NOT gates, OR gates and an AND gate
Draw a circuit that implements the function using only NOT gates and NOR gates
Write the function as it is implemented by the second circuit

## Slide 28: Problem 2: Write the POS formulation for this truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Draw a circuit that implements the function using NOT gates, OR gates and an AND gate
Draw a circuit that implements the function using only NOT gates and NOR gates
Write the function as it is implemented by the second circuit

## Slide 29: Problem 3: Write the POS formulation for this truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Draw a circuit that implements the function using NOT gates, OR gates and an AND gate
Draw a circuit that implements the function using only NOT gates and NOR gates
Write the function as it is implemented by the second circuit

## Slide 30: Problem 4: Write the POS formulation for this truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Draw a circuit that implements the function using NOT gates, OR gates and an AND gate
Draw a circuit that implements the function using only NOT gates and NOR gates
Write the function as it is implemented by the second circuit