## Slide 1: Karnaugh Maps
June 2025

## Slide 2
A better gate minimization method.

## Slide 3: Karnaugh Maps
Karnaugh maps are a rearrangement of the truth table that allows us to graphically find the minimized logical circuit
Boolean Algebra made easy!

## Slide 4: Karnaugh Maps
The maps are arranged differently depending upon the number of input variables
Each cell in the Karnaugh map corresponds to one set of input values and one output

## Slide 5: Two Variable Karnaugh Map
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0
1
0
1
f = x2 x1 + x2 x1

## Slide 6: Two Variable Karnaugh Map
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
0
1
0
1
Look at the Karnaugh map to find groups of ‘1’s that are together
Circle groups that are multiples of two wide and/or multiples of two tall
Do this until all ‘1’s are circled, if necessary circling unpaired ‘1’s

## Slide 7: Two Variable Karnaugh Map
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
0
1
0
1
These groups allow us to reduce the complexity of the circuit
Write down the variable states that describe each circle, adding (OR) them together if there are multiple circles
f = x2
f = x2 x1 + x2 x1
f = x2 (x1 + x1)
f = x2 (1)
f = x2

## Slide 8: Three Variable Karnaugh Map
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
x1x2
x1x2

## Slide 9: Three Variable Karnaugh Map
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
Important:
For the reduction to work correctly, only one digit of the code can change at a time
11
1 0
Each cell in the Karnaugh map still corresponds to one set of x1x2x3 values and one output

## Slide 10: Three Variable Karnaugh Map
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
0
0
0
0
1
1
1
1

## Slide 11: Three Variable Karnaugh Map
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
0
0
0
0
1
1
1
1
Look at the Karnaugh map to find groups of ‘1’s that are together
Circle groups that are multiples of two wide and/or multiples of two long
Do this until all ‘1’s are circled, if necessary circling unpaired ‘1’s
It is OK to “double count” some ‘1’s

## Slide 12: Three Variable Karnaugh Map
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
0
0
0
0
1
1
1
1
Write down the variable states that describe each circle, adding (OR) them together if there are multiple circles
f = x1 x2 + x3 x2 + x1 x3
x1 x2
x3 x2
x1 x3

## Slide 13
An example with a different truth table will illustrate some additional important points

## Slide 14: Another Three Variable Karnaugh Map
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
1
0
0
1
1
1
1
1
x1
x2 x3
x2 x3
f = x1 + x2 x3 + x2 x3
You can loop from top to bottom or from side to side

## Slide 15: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
1
0
0
1
1
1
1
1
1
1
1
1
0
0
0
0

## Slide 16: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
1
0
0
1
1
1
1
1
1
1
1
1
0
0
0
0
x2x4
x1x3
x2x4
f = x1 x3 + x2 x4 + x2 x4

## Slide 17
We have used the Karnaugh map to determine the least cost SOP implementations
The Karnaugh map can also be used to determine the least cost POS implementations
This is done by grouping the zeros instead of the ones

## Slide 18: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
1
0
0
1
1
0
1
1
1
1
1
1
0
0
0
0
x2+x4
x2+x3+x4
x1+x2+x4
f = (x2+x4)(x2+x3+x4)(x1+x2+x4)

## Slide 19: Incompletely Specified Functions
Sometimes functions have bit combinations that will not occur
For the output corresponding to those bit combinations, we don’t care if it is a 0 or a 1. We don’t care because the combination will not occur.

## Slide 20: Incompletely Specified Functions
This is called an incompletely specified function
We put a ‘d’ for “don’t care” in the Karnaugh map.
We are free to specify either a 1 or a 0. We choose whichever makes our function simpler.

## Slide 21: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | d
1 | 0 | 1 | 1 | d
1 | 1 | 0 | 0 | d
1 | 1 | 0 | 1 | d
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | d
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
0
0
1
1
1
d
d
1
d
1
0
d
1
1
d
d

## Slide 22: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 1
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 1 | 1 | d | d
x1 x2
x3x4
x3x4
x2x3
x1
f = x1+x2x3 +x2x3 +x3x4
x2x3

## Slide 23: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 1
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 1 | 1 | d | d
x1 x2
x3x4
x1+x2+x3
f =(x2+x3+x4)(x1+x2+x3)
x2 + x3+x4

## Slide 24
Another example

## Slide 25: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | d
1 | 0 | 1 | 1 | d
1 | 1 | 0 | 0 | d
1 | 1 | 0 | 1 | d
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | d
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
0
0
1
0
1
d
d
1
d
0
0
d
1
0
d
d

## Slide 26: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 0
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 0 | 0 | d | d
x1 x2
x3x4
x2x3
x1x4
f = x1 x4+x2x3 +x2x3x4
x2x3x4
SOP

## Slide 27: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 0
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 0 | 0 | d | d
x1 x2
x3x4
x2 + x4
x1+ x2 + x3
f = (x2 + x3 ) (x2 + x4 )(x1 + x2 + x3 )
x2 + x3
POS

## Slide 28: Larger Karnaugh Maps
Karnaugh maps for 5 or 6 variables require three dimensional grids
More variables require envisioning more dimensions

## Slide 30: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 1
Find the minimized SOP function
Find the minimized POS function and draw the corresponding circuit

## Slide 31
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Generate the Karnaugh map corresponding to the truth table
Problem 2
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 32: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | d
0 | 0 | 1 | 1 | d
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | d
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 3
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 33: Generate the Karnaugh map corresponding to the truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | d
0 | 1 | 1 | d
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Problem 4
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 34: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | d
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | d
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 5
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 35: Generate the Karnaugh map corresponding to the truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Problem 6
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 36: Generate the Karnaugh map corresponding to the truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | d
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Problem 7
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 37: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | d
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | d
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 8
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit