## Slide 1: Karnaugh Maps
June 2025

## Slide 2
A better gate minimization method.

## Slide 3: Karnaugh Maps
Karnaugh maps are a rearrangement of the truth table that allows us to graphically find the minimized logical circuit
Boolean Algebra made easy!

## Slide 4: Karnaugh Maps
Karnaugh maps are a rearrangement of the truth table that allows us to graphically find the minimized logical circuit
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
x1 x2
x3
f = x1 x2 + x2 x3 + x1 x3
f = x1 x2 x3 + x1 x2 x3 + x1 x2 x3 + x1 x2 x3
Boolean Algebra made easy!

## Slide 5: Karnaugh Maps
The maps are arranged differently depending upon the number of input variables
Each cell in the Karnaugh map corresponds to one set of input values and one output
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
 | 00 | 01 | 11 | 10
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
 | 00 | 01 | 11 | 10
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
Two Inputs
Three Inputs
Four Inputs

## Slide 6: Two Variable Karnaugh Map
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
Truth Table
x1 | x2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0
1
0
1
f = x1 x2 + x1 x2

## Slide 7: Two Variable Karnaugh Map
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
0
1
0
1
Look at the Karnaugh map to find groups of ‘1’s that are together
Circle groups that are multiples of two wide and/or multiples of two tall
Do this until all ‘1’s are circled, if necessary circling unpaired ‘1’s

## Slide 8: Two Variable Karnaugh Map
 | 0 | 1
0 |  | 
1 |  | 
x1
x2
0
1
0
1
These groups allow us to reduce the complexity of the circuit
Write down the variable states that describe each circle, adding (OR) them together if there are multiple circles
f = x2
f = (x1 + x1) x2
f = (1) x2
f = x2
f = x1 x2 + x1 x2

## Slide 9: Three Variable Karnaugh Map
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
x1x2
x1x2

## Slide 10: Three Variable Karnaugh Map
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
Important:
For the reduction to work correctly, only one digit of the code can change at a time
11
1 0
Each cell in the Karnaugh map still corresponds to one set of x1x2x3 values and one output

## Slide 11: Three Variable Karnaugh Map
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
0
0
0
0
1
1
1
1

## Slide 12: Three Variable Karnaugh Map
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
0
0
0
0
1
1
1
1
Look at the Karnaugh map to find groups of ‘1’s that are together
Circle groups that are multiples of two wide and/or multiples of two long
Do this until all ‘1’s are circled, if necessary circling unpaired ‘1’s
It is OK to “double count” some ‘1’s

## Slide 13: Three Variable Karnaugh Map
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
0
0
0
0
1
1
1
1
Write down the variable states that describe each circle, adding (OR) them together if there are multiple circles
f = x1 x2 + x2 x3 + x1 x3
x1 x2
x2 x3
x1 x3

## Slide 14: Comparison of SOP and reduced functions
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
f = x1 x2 + x2 x3 + x1 x3
f = x1 x2 x3 + x1 x2 x3 + x1 x2 x3 + x1 x2 x3

## Slide 15: Finding Logical Networks from the Truth Table
output
Sum of Products:
Problem 3:
x1
x3
x2
x1
x2
f =x1x2x3 + x1x2x3 + x1x2x3 + x1x2x3
x3
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 16: Sum of Products Circuit
input variables
output
x1
x2
x3
x1
x3
x2
f = x1 x2 x3 + x1 x2 x3 + x1 x2 x3 + x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 17: Reduced Circuit
input variables
output
x1
x2
x3
x1
x3
x2
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3
f = x1 x2 + x2 x3 + x1 x3
x1 x2
x1 x3
x2 x3
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 18
An example with a different truth table will illustrate some additional important points

## Slide 19: Another Three Variable Karnaugh Map
0 |  |  |  | 
1 |  |  |  | 
x1 x2
x3
0 0
0 1
11
1 0
1
0
0
1
1
1
1
1
x1
x2 x3
x2 x3
f = x1 + x2 x3 + x2 x3
You can loop from top to bottom or from side to side

## Slide 20: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
1
0
0
1
1
1
1
1
1
1
1
1
0
0
0
0
Notice the order

## Slide 21: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
1
0
0
1
1
1
1
1
1
1
1
1
0
0
0
0
x2x4
x1x3
x2x4
f = x1 x3 + x2 x4 + x2 x4

## Slide 22
We have used the Karnaugh map to determine the least cost SOP implementations
The Karnaugh map can also be used to determine the least cost POS implementations
This is done by grouping the zeros instead of the ones

## Slide 23: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
1
0
0
1
1
0
1
1
1
1
1
1
0
0
0
0
x2+x4
x2+x3+x4
x1+x2+x4
f = (x2+x4)(x2+x3+x4)(x1+x2+x4)
x1x2x4

## Slide 24: Implementing the Circuit
input variables
output
x1
x2
x3
x4
x2
x3
x2+x3+x4
x4
f = (x2+x4)(x2+x3+x4)(x1+x2+x4)
x2+x4
x1+x2+x4
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 25: Incompletely Specified Functions
Sometimes functions have bit combinations that will not occur
For the output corresponding to those bit combinations, we don’t care if it is a 0 or a 1. We don’t care because the combination will not occur.

## Slide 26: Incompletely Specified Functions
This is called an incompletely specified function
We put a ‘d’ for “don’t care” in the Karnaugh map.
We are free to specify either a 1 or a 0. We choose whichever makes our function simpler.

## Slide 27: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | d
1 | 0 | 1 | 1 | d
1 | 1 | 0 | 0 | d
1 | 1 | 0 | 1 | d
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | d
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
0
0
1
1
1
d
d
1
d
1
0
d
1
1
d
d

## Slide 28: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 1
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 1 | 1 | d | d
x1 x2
x3x4
x3x4
x2x3
x1
f = x1+x2x3 +x2x3 +x3x4
x2x3

## Slide 29: Sum of Products Reduced Circuit
input variables
output
x4
x3
x2
x4
x2
x3
x3 x4
x2 x3
x2 x3
f = x1+x2x3 +x2x3 +x3x4
x1
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 30: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 1
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 1 | 1 | d | d
x1 x2
x3x4
x1+x2+x3
f =(x2+x3+x4)(x1+x2+x3)
x2 + x3+x4

## Slide 31: Product of Sums Reduced Circuit
input variables
output
x4
x3
x2
x4
x2
x3
x1 + x2 + x3
x1
f =(x2+x3+x4)(x1+x2+x3)
x2 + x3 + x4
Notes: The function is true if the first minterm is true OR if the second minterm is true OR if the last minterm is true.

## Slide 32
Another example

## Slide 33: Four Variable Karnaugh Map
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | d
1 | 0 | 1 | 1 | d
1 | 1 | 0 | 0 | d
1 | 1 | 0 | 1 | d
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | d
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
x1 x2
x3x4
0 0
0 1
11
1 0
0
0
1
0
1
d
d
1
d
0
0
d
1
0
d
d

## Slide 34: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 0
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 0 | 0 | d | d
x1 x2
x3x4
x2x3
x1x4
f = x1 x4+x2x3 +x2x3x4
x2x3x4
SOP

## Slide 35: Incompletely Specified Karnaugh Map
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 1 | d | 0
0 1 | 0 | 1 | d | 1
11 | 1 | 0 | d | d
1 0 | 0 | 0 | d | d
x1 x2
x3x4
x2 + x4
x1+ x2 + x3
f = (x2 + x3 ) (x2 + x4 )(x1 + x2 + x3 )
x2 + x3
POS

## Slide 36: Larger Karnaugh Maps
Karnaugh maps for 5 or 6 variables require three dimensional grids
More variables require envisioning more dimensions

## Slide 38: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 1
Find the minimized SOP function
Find the minimized POS function and draw the corresponding circuit

## Slide 39
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Generate the Karnaugh map corresponding to the truth table
Problem 2
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 40: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | d
0 | 0 | 1 | 1 | d
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | d
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 3
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 41: Generate the Karnaugh map corresponding to the truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | d
0 | 1 | 1 | d
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Problem 4
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 42: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | d
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | d
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 5
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 43: Generate the Karnaugh map corresponding to the truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Problem 6
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 44: Generate the Karnaugh map corresponding to the truth table
Truth Table
x1 | x2 | x3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | d
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Problem 7
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit

## Slide 45: Generate the Karnaugh map corresponding to the truth table
x1 | x2 | x3 | x4 | output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | d
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | d
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | d
1 | 1 | 1 | 1 | 0
0 0
0 1
11
1 0
Problem 8
Find the minimized SOP function and draw the corresponding circuit
Find the minimized POS function and draw the corresponding circuit