## Slide 1: Decoders
June 2025

## Slide 2: Decoder Basics
2-to-4 decoder
inputs
enable
A decoder has inputs that represent a binary number
The binary number selects an output line from the available lines
outputs
There is usually one or more enable lines that determine if chip functions or if it ignores the input.
2n outputs
n inputs

## Slide 3: Decoder Basics
2-to-4 decoder
inputs
enable
Some decoders set the selected line “high” and force all other outputs “low”
outputs
Other decoders, including the 74LS138, set the selected line “low” and force all other outputs “high”

## Slide 4: 2-to-4 Decoder
From the truth table we can see that
inputs |  | outputs |  |  | 
w1 | w0 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Truth Table
Note: This decoder sets the selected line high and all others low. This is different from the 74LS138.
y1 = w1w0
y3 = w1w0
y0 = w1w0
y2 = w1w0

## Slide 5: 2-to-4 Decoder Circuit
inputs |  | outputs |  |  | 
w1 | w0 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
y3 = w1w0
y2 = w1w0
y1 = w1w0
y0 = w1w0

## Slide 6: 2-to-4 Decoder – Check the Function
y0 = w1w0
y1 = w1w0
y2 = w1w0
y3 = w1w0
inputs |  | outputs |  |  | 
w1 | w0 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
0
0
1
1
1
1
1
1
0
0
1
0
0
0
0
0

## Slide 7: 2-to-4 Decoder
y0 = w1w0
y1 = w1w0
y2 = w1w0
y3 = w1w0
inputs |  | outputs |  |  | 
w1 | w0 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
1
0
0
1
0
0
1
1
1
1
0
0
0
1
0
0

## Slide 8: 2-to-4 Decoder
y0 = w1w0
y1 = w1w0
y2 = w1w0
y3 = w1w0
inputs |  | outputs |  |  | 
w1 | w0 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
0
1
1
0
0
1
0
0
0
0
1
1
1
0
1
0

## Slide 9: 2-to-4 Decoder
y0 = w1w0
y1 = w1w0
y2 = w1w0
y3 = w1w0
inputs |  | outputs |  |  | 
w1 | w0 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
1
1
0
0
0
0
0
0
1
0
0
1
0
1
1
1

## Slide 10: 2-to-4 Decoder with Enable
inputs |  |  | outputs |  |  | 
En | w1 | w0 | y3 | y2 | y1 | y0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0
0 | x | x | 0 | 0 | 0 | 0
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
An enable bit, if high, causes the circuit to function normally.
If it is low, all outputs are set to zero.
En

## Slide 11: 2-to-4 Decoder with Enable
inputs |  |  | outputs |  |  | 
En | w1 | w0 | y3 | y2 | y1 | y0
1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
0 | x | x | 1 | 1 | 1 | 1
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
If we changed the truth table to have the selected output low, how would we need to change the ciruit?
En

## Slide 12: 2-to-4 Decoder with Enable
inputs |  |  | outputs |  |  | 
En | w1 | w0 | y3 | y2 | y1 | y0
1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
0 | x | x | 1 | 1 | 1 | 1
Truth Table
w0
w1
w0
w1
y0
y1
y2
y3
We could just change the AND gates to NAND gates.
En

## Slide 13: 2-to-4 Decoder with Enable
w0
w1
inputs
y0
y3
y1
y2
En
outputs

## Slide 14: 3-to-8 Decoder Using 2-to-4 Decoders
w0
w1
y0
y3
y1
y2
En
w0
w1
y0
y3
y1
y2
En
w0
w1
w2
En
y0
y2
y1
y3
y4
y5
y6
y7

## Slide 15: 3-to-8 Decoder Using 2-to-4 Decoders
w0
w1
y0
y3
y1
y2
En
w0
w1
y0
y3
y1
y2
En
w0
w1
w2
En
y0
y2
y1
y3
y4
y5
y6
y7
0
0
0
0
0
Setting En = 0 disables both chips

## Slide 16: 3-to-8 Decoder Using 2-to-4 Decoders
w0
w1
y0
y3
y1
y2
En
w0
w1
y0
y3
y1
y2
En
w0
w1
w2
En
y0
y2
y1
y3
y4
y5
y6
y7
0
1
1
1
1
0
1
0
This works as before
This chip is disabled

## Slide 17: 3-to-8 Decoder Using 2-to-4 Decoders
w0
w1
y0
y3
y1
y2
En
w0
w1
y0
y3
y1
y2
En
w0
w1
w2
En
y0
y2
y1
y3
y4
y5
y6
y7
1
1
0
1
1
1
0
1
This works as the other one did before
This chip is disabled
w2 acts as the high order bit, selecting which chip is on

## Slide 18: 4-to-16 Decoder Using 2-to-4 Decoders
w0
w1
y0
y3
y1
y2
En
w0
w1
En
w0
w1
En
y0
y3
y1
y2
w0
w1
y0
y3
y1
y2
En
w0
w1
En
y0
y3
y1
y2
w0
w1
y0
y3
y1
y2
En
w3
w4
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
w4w3
w4w3
w4w3
w4w3
This decoder selects which chip to use for the second stage

## Slide 19: 74LS138 Enables
The 74LS138 has three different enable pins, pins 4, 5, and 6.
All outputs are high unless the proper voltages are on each of the enable pins.
To enable the chip, pins 4 and 5 should be grounded and pin 6 should be set to the “high” voltage (normally 5.0 volts).

## Slide 20: 74LS138 Inputs
The inputs that select which output pin becomes low are applied to pins 1, 2, and 3. The least significant bit is pin 1 (A0) and the most significant bit is pin 3 (A2).

## Slide 21: 74LS138 Outputs
The output pins are pin 7 and pins 9-15.
Y0 is set low if A2, A1, and A0 are all zeros.
Y1 is set low if A2, A1, and A0 are 0, 0, and 1 respectively.

## Slide 22: 74LS138 Function Based upon Motorola Data Sheets
Inputs |  |  |  |  |  | Outputs |  |  |  |  |  |  | 
Enable |  |  | Select |  |  |  |  |  |  |  |  |  | 
E1 | E2 | E3 | A2 | A1 | A0 | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
1 | X | X | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
X | 1 | X | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
X | X | 0 | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
chip is enabled
chip is disabled

## Slide 23: Reminder about Minterms
inputs |  |  | output
a | b | c | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Truth Table
0
0
0
1
0
1
1
1
Reminder: a minterm describes the state of the variables. There is a minterm corresponding to each row of a truth table.
Minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
m0 =
m1 =
m2 =
m3 =
m4 =
m5 =
m6 =
m7 =

## Slide 24: 74LS138 Function Based upon Motorola Data Sheets
Inputs |  |  |  |  |  | Outputs |  |  |  |  |  |  | 
Enable |  |  | Select |  |  |  |  |  |  |  |  |  | 
E1 | E2 | E3 | A2 | A1 | A0 | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
1 | X | X | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
X | 1 | X | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
X | X | 0 | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
When the chip is enabled, each of the outputs can be viewed as being the complement of the corresponding minterm.
chip is enabled
chip is disabled

## Slide 25: 74LS138 Function Based upon Motorola Data Sheets
Inputs |  |  |  |  |  | Outputs |  |  |  |  |  |  | 
Enable |  |  | Select |  |  |  |  |  |  |  |  |  | 
E1 | E2 | E3 | A2 | A1 | A0 | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
1 | X | X | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
X | 1 | X | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
X | X | 0 | X | X | X | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
chip is enabled
chip is disabled
m0
m1
m2
m3
m4
m5
m6
m7

## Slide 26: 74LS138 Outputs
The outputs can be viewed as the complement of the respective minterms.
We can use this to our advantage and use the 74LS138 to generate functions of three variables.

## Slide 27
Any function can be expressed in terms of its minterms. Some Boolean algebra may be required to get it into the proper form.
Example: f = abc + bc + ac + ab
While the first term of the sum is a minterm, the other terms are not.

## Slide 28
Example: f = abc + bc + ac + ab
We can convert the terms that are not minterms into the sums of minterms by multiplying the term by the sum of the variables that are missing from the minterm and the complement of the variables that are missing from the minterm.
We will first work on the term bc.

## Slide 29
Example: f = abc + bc + ac + ab
bc = bc ( a + a )
This is true since ( a + a ) = 1
bc = bca + bca
Distributive law
bc = abc + abc
Associative law
Now bc is expressed in terms of its minterms.

## Slide 30
Example: f = abc + bc + ac + ab
Distributive law
Now work on the term ac
ac = ac ( b + b )
This is true since ( b + b ) = 1
ac = acb + acb
ac = abc + abc
Associative law
Now ac is expressed in terms of its minterms.

## Slide 31
Example: f = abc + bc + ac + ab
Distributive law
Now work on the term ab
This is true since ( c + c ) = 1
ab = ab ( c + c )
ab = abc + abc
Now ab is expressed in terms of its minterms.

## Slide 32
Example: f = abc + bc + ac + ab
f = abc + abc + abc + abc + abc + abc + abc
f = abc + abc + abc + abc + abc
f = m7 + m3 + m5 + m2
f = abc + abc + abc + abc
f = m2 + m3 + m5 + m7
since x + x = x

## Slide 33
Example: f = abc + bc + ac + ab
f = m2 + m3 + m5 + m7
We now have the function in terms of its minterms. However, the output of the 74LS138 is the complements of the minterms. We need to do some more Boolean algebra to get the function in terms of its complements.

## Slide 34
Example: f = abc + bc + ac + ab
f = m2 + m3 + m5 + m7
Negate both sides
f = m2 m3 m5 m7
Negate both sides
DeMorgan’s theorem
f = m2 m3 m5 m7
These are outputs of the chip.
Put the appropriate outputs into a NAND gate to generate the function.

## Slide 35: 74LS138
The function will be generated once the chip is enabled and the inputs are applied to terminals 1 through 3.
f = m2 m3 m5 m7
0
0
1
inputs

## Slide 36: Shortcut Using Truth Table
Example: f = abc + bc + ac + ab
f = abc + abc + abc + abc + abc + abc + abc
inputs |  |  | output
a | b | c | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
For each term that is not a minterm
Find those values in the truth table
Write down all of the values of those minterms
m3
m7

## Slide 37: Shortcut Using Truth Table
Example: f = abc + bc + ac + ab
f = abc + abc + abc + abc + abc + abc + abc
inputs |  |  | output
a | b | c | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
For each term that is not a minterm
Find those values in the truth table
Write down all of the values of those minterms
m3
m5
m7

## Slide 38: Shortcut Using Truth Table
Example: f = abc + bc + ac + ab
f = abc + abc + abc + abc + abc + abc + abc
inputs |  |  | output
a | b | c | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
For each term that is not a minterm
Find those values in the truth table
Write down all of the values of those minterms
You will still need to remove the duplicate minterms
m2
m3
m5
m7
This list is good

## Slide 39: Example 2
Using the 74LS138 design a circuit that implements the following function:
f = abc + ab + abc

## Slide 40: Example 2
inputs |  |  | output
a | b | c | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example: f = abc + ab + abc
m7
m2
m3
m1
f = m1 + m2 + m3 + m7
f = m1 m2 m3 m7

## Slide 41: 74LS138
The function will be generated once the chip is enabled and the inputs are applied to terminals 1 through 3.
0
0
1
inputs
f = m1 m2 m3 m7

## Slide 43: Problem 1
Using the 74LS138 design a circuit that implements the following function:
f = ab + ac + abc

## Slide 44: Problem 2
Using the 74LS138 design a circuit that implements the following function:
f = x + yz

## Slide 45: Problem 3
Using the 74LS138 design a circuit that implements the following function:
f = abc + ac + bc

## Slide 46: Problem 4
Using the 74LS138 design a circuit that implements the following function:
f = xy

## Slide 47: Problem 5
Using the 74LS138 design a circuit that implements the following function:
f = xz + xy + xyz

## Slide 48: Problem 6
Using the 74LS138 design a circuit that implements the following function:
f = x1x2x3 + x1x2

## Slide 49: Problem 7
Using the 74LS138 design a circuit that implements the following function:
f = lmn + lm + ln

## Slide 50: Problem 8
Using the 74LS138 design a circuit that implements the following function:
f = bc + ab + ab

## Slide 51: Problem 9
Using the 74LS138 design a circuit that implements the following function:
f = ab + ab