## Slide 1
Encoders
June 2025

## Slide 2: Binary Encoders
A binary encoder has multiple inputs with one and only one input being “high”
The output of a binary encoder is a binary number that identifies which of the inputs is “high”
4-to-2 encoder
inputs
enable
outputs
2n inputs
n outputs

## Slide 3: 4-to2 Binary Encoder
From the truth table we can see that
y1 = w0w1w2w3 + w0w1w2w3
and
y0 = w0w1w2w3 + w0w1w2w3
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
However, since we are guaranteed that there is one and only one “high” input, this is equivalent to:
y1 = w2 + w3 and y0 = w1 + w3

## Slide 4: 4-to2 Binary Encoder
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
1
d
d
d
d
d
d
d
d
d
d
d
d

## Slide 5: Karnaugh Map for Encoder Output y0
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
1
d
d
d
d
d
d
d
d
d
d
d
d

## Slide 6: Karnaugh Map for Encoder Output y0
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
1
d
1
d
d
d
d
w1
1
1
1
1
1
1

## Slide 7: Karnaugh Map for Encoder Output y0
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
1
d
d
1
w1
w3
1
1
1
1
1
1
1
1
1
y0 = w1 + w3

## Slide 8: Karnaugh Map for Encoder Output y0
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
1
d
d
d
d
d
d
d
d
d
d
d
d

## Slide 9: Karnaugh Map for Encoder Output y0
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
1
1
0
0
0
0
1
0
0
0
0
0
0
w0w2
y0 = w0w2
This would require two NOT gates and an AND gate

## Slide 10: 4-to2 Binary Encoder
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y1
0
0
1
1
d
d
d
d
d
d
d
d
d
d
d
d

## Slide 11: Karnaugh Map for Encoder Output y0
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y1
0
0
1
1
d
d
d
d
d
d
d
d
d
d
d
d
w3
w2
y1 = w2 + w3

## Slide 12: 4-to2 Binary Encoder Circuit
w1
w3
w0
w2
y0
y1
y0 = w1 + w3
y1 = w2 + w3

## Slide 13: 8-to3 Binary Encoder
inputs |  |  |  |  |  |  |  | outputs |  | 
w7 | w6 | w5 | w4 | w3 | w2 | w1 | w0 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
Truth Table
y2 = w4 + w5 + w6 + w7
y1 = w2 + w3 + w6 + w7
y0 = w1 + w3 + w5 + w7

## Slide 14: 8-to3 Binary Encoder Circuit
y0
y1
y2
w0
w2
w1
w3
w4
w5
w6
w7
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 15: 2n-to-n Binary Encoder
.
.
.
w0
w2n-1
.
.
.
2n inputs
n outputs
y0
yn-1
.
.
.

## Slide 17: Priority Encoders
A priority encoder has multiple inputs like the binary encoder, but there is no guarantee about how many inputs will being “high”
The output of a priority encoder is a binary number that identifies the highest priority input that is “high”

## Slide 18: 4-to2 Priority Encoder
We can start by modifying the truth table for the binary encoder.
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
Highest Priority
Second Highest Priority
Third Highest Priority
Lowest Priority

## Slide 19: 4-to2 Priority Encoder
Our highest priority means what is most important to us.
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
Highest Priority
Second Highest Priority
Third Highest Priority
Lowest Priority
I have homework.
I am hungry.
I have a phone call.
The building is on fire.

## Slide 20: 4-to2 Priority Encoder
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
If w3 = 1, the output should be y1=1 and y0=1 regardless of the values of w2, w1, or w0.
Highest Priority
Second Highest Priority
Third Highest Priority
Lowest Priority
x
x
x
If the building is on fire, you will get out of the building and not worry about answering the phone or eating food or doing homework.
We put ‘x’ in these because it doesn’t matter what they are

## Slide 21: 4-to2 Priority Encoder
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
Highest Priority
Second Highest Priority
Third Highest Priority
Lowest Priority
x
x
x
If w3 = 0 and w2 = 1, the output should be y1=1 and y0=0 regardless of the values of w1, or w0.
x
x
If the building is not on fire and your phone is ringing, you will answer it even if you are hungry and have homework.
We put ‘x’ in these because it doesn’t matter what they are

## Slide 22: 4-to2 Priority Encoder
inputs |  |  |  | outputs | 
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
Truth Table
Highest Priority
Second Highest Priority
Third Highest Priority
Lowest Priority
x
x
x
x
x
If w3 = 0 and w2 = 0 and w1 = 1, the output should be y1=0 and y0=1 regardless of the value of w0.
x
If the building is not on fire and your phone is not ringing and you are hungry, you will eat even if you have homework.
We put ‘x’ here because it doesn’t matter what it is

## Slide 23: 4-to2 Priority Encoder
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | x | 0 | 1 | 1
0 | 1 | x | x | 1 | 0 | 1
1 | x | x | x | 1 | 1 | 1
Truth Table
The output z tells us when something needs our attention.
Let output z = you need to do something
Let input w0 = you have homework
Let input w1 = you are hungry
Let input w2 = the phone is ringing
Let input w3 = the building is on fire

## Slide 24: 4-to2 Priority Encoder
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | x | 0 | 1 | 1
0 | 1 | x | x | 1 | 0 | 1
1 | x | x | x | 1 | 1 | 1
Truth Table
We need to expand the truth table to get rid of the ‘x’s before we can find the circuit to implement the priority encoder.
What does the x in the highlighted row mean?
It means that there are really two different rows. Everything is the same in those two rows except for w0. For one of those rows w0 equals zero, and for the other row w0 equals one.

## Slide 25: 4-to2 Priority Encoder
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | x | x | 1 | 0 | 1
1 | x | x | x | 1 | 1 | 1
Truth Table
0 0 1 x

## Slide 26: 4-to2 Priority Encoder Truth Table
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
0 0 1 x
0 1 x x
1 x x x
0 0 0 1
0 0 0 0

## Slide 27: 4-to2 Priority Encoder Karnaugh Map
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output z
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
z = w0 + w1 + w2 + w3
w2
w1
w0
w3

## Slide 28: 4-to2 Priority Encoder Karnaugh Map
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y0
0
1
0
d
1
0
0
0
1
1
1
1
1
1
1
1
w3
w1w2
y0 = w1w2 + w3

## Slide 29: 4-to2 Priority Encoder Karnaugh Map
inputs |  |  |  | outputs |  | 
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0 0 | 0 1 | 1 1 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
w1w0
w3w2
Output y1
0
0
1
1
d
0
1
1
1
1
1
1
1
1
1
1
w3
w2
y1 = w2 + w3

## Slide 30: 4-to2 Priority Encoder Circuit
w1
w3
w0
w2
y0
y1
z
y1 = w2 + w3
z = w0 + w1 + w2 + w3
y0 = w1w2 + w3

## Slide 31: For the given inputs, find the outputs of a 4-to-1 priority encoder
y1
w2
w3
w0
w1
y0
z

## Slide 32: For the given inputs, find the outputs of a 4-to-1 priority encoder
y1
w2
w3
w0
w1
y0
z

## Slide 33: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 35: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 36
Practice Problems

## Slide 37: Problem 1: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 38: Problem 2: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 39: Problem 3: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 40: Problem 4: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 41: Problem 5: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 42: Problem 6: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z
w2

## Slide 43: Problem 7: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 44: Problem 8: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 45: Problem 9: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 46: Problem 10: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z

## Slide 47: Problem 11: For the given inputs, find the outputs of a 4-to-1 priority encoder
w2
w3
w0
w1
y1
y0
z