## Slide 1: Flip-Flops
June 2025

## Slide 2: Flip-flops
Latches
Gated Latches
Flip-flops

## Slide 3: Circuit for SR Latch
Qa
R
Qb
S
two inputs
Set
Reset
two outputs
The outputs are applied to the inputs of the NOR gates
This is called feedback

## Slide 4: Circuit for SR Latch
Qa
R
Qb
S
two inputs
Set
Reset
two outputs
The future outputs of the circuit can depend upon the current state of the circuit
This provides a type of memory

## Slide 5: Circuit for SR Latch
Qa
R
Qb
S
two inputs
Set
Reset
two outputs
Under certain conditions the outputs retain their previous values
The outputs can take a short time to “settle” into the new values

## Slide 6: Circuit for SR Latch
Qa
R
Qb
S
two inputs
Set
Reset
two outputs
When S and R are both zero, the outputs retain their previous values
When S is low and R is high, Qa is reset to zero and is Qb one
S | R | Qa | Qb
0 | 0 | Qa | Qb
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Characteristic Table
When S is high and R is low, Qa is set to one and is Qb becomes zero
Having both S and R high is considered an illegal input

## Slide 7: Circuit for SR Latch
Qa
R
Qb
S
two inputs
Set
Reset
two outputs
S | R | Qa | Qb
0 | 0 | Qa | Qb
0 | 1 | 0 | 1
1 | 0 | 1 | 0
Characteristic Table
For legal inputs, Qb = Qa

## Slide 8: Flip-flops
Latches
Gated Latches
Flip-flops

## Slide 9: Gated SR Latch
Q
Q
A gate is normally added to a latch. A gate only allows signals to get into the latch when we want them to.
Characteristic Table
R
S
Clk
R
S
R
S
clk | S | R | Q | Q
0 | x | x | Q | Q
1 | 0 | 0 | Q | Q
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
S | R | Q | Q
0 | 0 | Q | Q
0 | 1 | 0 | 1
1 | 0 | 1 | 0

## Slide 10: Example of Signals for Gated SR Latch
clk
R
S
Q
Q
input signals ignored
output can change multiple times

## Slide 11: Gated D Latch
Q
Q
S and R are always complements
R
S
Clk
R
S
When the clock is high, the data input, D, appears at the output, Q
one input
D

## Slide 12: Flip-flops
Latches
Gated Latches
Flip-flops

## Slide 13: Flip-flops
A flip-flop changes its output only at an edge of the clock signal.
Clock
Rising edge
Falling edge
Depending upon the design, it could be on the rising edge of the clock signal or on the falling edge of the clock signal.

## Slide 14: Flip-flops
A master-slave flip-flop consists of two latches with one latch being active while the other one is inactive.
A primary-subordinate flip-flop ensures that the output of a flip-flop does not change more than once during one clock cycle.
primary-subordinate

## Slide 15: Primary-subordinate D Flip-Flop
D
Clk
Q
Q
D
Clk
Q
Q
Q
D
Q
Clock
Primary Latch
Subordinate Latch
Qp
Symbol for Latch
Triggered on falling edge
Move NOT gate to here to trigger on rising edge

## Slide 16: Symbol for negative-edge-triggered Master-slave D Flip-Flop
D
>
Q
Q
The circle indicates that it is triggered on the falling edge
This symbol indicates that the flip-flop is edge triggered.
primary-subordinate

## Slide 17: Timing for Primary-Subordinate D Flip-flop -- Example 1
D
Clock
QP
Q
When the clock is high the primary follows the input, but the subordinate is disabled
When the clock goes low, the master stops following the input and the slave loads the intermediate output

## Slide 18: Timing for D Flip-flop -- Example 2
D
Clock
Q
Qp

## Slide 19: Positive-edge-triggered Primary-subordinate D Flip-Flop
D
Clk
Q
Q
D
Clk
Q
Q
Q
D
Q
Clock
Primary
Subordinate
Qp

## Slide 20: Symbol for positive-edge-triggered D Flip-Flop
D
>
Q
Q

## Slide 21: Symbol for negative-edge-triggered D Flip-Flop with Clear and Preset
D
>
Q
Q
Preset_n
Clear_n
The circle indicates that a low voltage causes the preset
The circle indicates that a low voltage causes the clear
The clear and the preset occur asynchronously -- without waiting for the next clock edge.

## Slide 22: Timing for D Flip-flop -- Example 3
D
Clock
Q
Qp
Clear_n
Preset_n

## Slide 23: Adding a Synchronous Clear to a D Flip-Flop
D
>
Q
Q
Clear_n
D
Clock

## Slide 24: T Flip-Flop
D
>
Q
Q
T
Clock

## Slide 25: T Flip-Flop
D
>
Q
Q
T
Clock
What is the logic function here?
What is the logic function here?
What is the value of D?

## Slide 26: T Flip-Flop
D
>
Q
Q
T
Clock
TQ
TQ
TQ+TQ
If T = 0, the output always stays the same.
If T = 1, the output always changes.

## Slide 27: Symbol for T Flip-Flop
T
>
Q
Q

## Slide 28: Timing for T Flip-flop -- Example 1
T
Clock
Q
Triggered
Since T is high, the output is inverted
Triggered
Since T is low, the output stays the same
Triggered
Since T is high, the output is inverted

## Slide 29: Timing for D Flip-flop -- Example 2
T
Clock
Q
Triggered
Since T is high, the output is inverted
Triggered
Since T is high, the output is inverted
Triggered
Since T is high, the output is inverted

## Slide 30: JK Flip-Flop
D
>
Q
Q
J
Clock
K

## Slide 31: JK Flip-Flop
D
>
Q
Q
J
Clock
K
D = JQ + KQ
What is the logic function here?
What is the logic function here?
What is the value of D?

## Slide 32: JK Flip-Flop
D = JQ + KQ
J | K | Q(t+1)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Characteristic Table
D = 0Q + 1Q
D = 0Q + 0Q
D = 1Q + 1Q
= Q + Q = 1
D = 1Q + 0Q
0
Q(t)
1
Q(t)

## Slide 33: JK Flip-Flop
J | K | Q(t+1)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Characteristic Table
0
Q(t)
1
Q(t)
For these three combinations of inputs, the JK flip-flop acts like an SR flip-flop
For J=1 and K=1, the JK flip-flop acts like a T flip-flop

## Slide 34: Frequency Divide By Two
Flip-flops can be easily used to divide the clock frequency by a factor of two
T
>
Q
Q
Clock
Input held “high”
Output
Clock
Output

## Slide 35: Summary Flip-flops
Flip-flops only change on a clock edge
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | 
JK Flip-flop Characteristic Table
Q(t)
T | Q(t+1)
0 | Q(t)
1 | 
T Flip-flop Characteristic Table
Q(t)
D | Q(t+1)
0 | 0
1 | 1
D Flip-flop Characteristic Table