## Slide 1: Counters
June 2025

## Slide 2: Four Bit Counters
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
T flip-flops changes every clock cycle if the T input is 1
The output of the T flip-flops will divide the clock frequency by 2

## Slide 3: Four Bit Counter
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
Clock
1
Q0
Q1
Q2
Q3
Clock
Q0
Q1
Q2
Q3
Down
>
1
1
1
1
0
1
1
1
1
0
1
1
0
0
1
1
1
1
0
1
0
1
0
1
1
0
0
1
0
0
0
1
15
14
13
12
11
10
9
8

## Slide 4: Four Bit Counter
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
Clock
1
Q0
Q1
Q2
Q3
Clock
Q0
Q1
Q2
Q3
1
0
0
0
0
1
0
0
1
1
0
0
0
0
1
0
Up
>
There is still a problem

## Slide 5: Four Bit Counter
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
Clock
1
Q0
Q1
Q2
Q3
Clock
Q0
Q1
Q2
Q3
Down
>
There is a delay before the last bit is established

## Slide 6
We would prefer a synchronous counter.
Synchronous sequential circuits
at the same time
one after another
Things happen one after another, but when changes occur everything changes at the same time
example: counting
we go from one number to the next (such as from seven to eight)
when the number changes from seven to eight, all of the binary digits change at the same time
a clock signal synchronizes the changes

## Slide 7: Next State Table
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Each variable represents a flip-flop
For every state
Indicate what the next state should be
How the state table is used depends upon what type of flip-flops are being used.
First, we will use T flip-flops.
The next state says what the state of the flip-flops should be after the next clock cycle
After that we will redesign using D flip-flops.
The present state of each flip-flop (y3, y2, y1, and y0) act like the inputs

## Slide 8: Four Bit Counter Using T Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
We will make a Karnaugh map to determine what connections need to be made between the outputs of the flip-flops and the inputs of the flip-flops
With T flip-flops, the value of T should be one if the variable changes values in going to the next state. The value should be zero if the variable stays the same.
We will compare the values of the next state to those of the present state

## Slide 9: Four Bit Counter Using T Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map for Y3
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
There is no change, so a 0 goes here
0
0
0
0
0
0
1
0
0
0
0
1
0
0
0
0
Find the first change
There are no other changes

## Slide 10: Four Bit Counter Using T Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map for T3
 | 0 0 | 0 1 | 11 | 1 0
0 0 | 0 | 0 | 0 | 0
0 1 | 0 | 0 | 1 | 0
11 | 0 | 0 | 1 | 0
1 0 | 0 | 0 | 0 | 0
y1 y0
y3y2
T3 = y0 y1 y2
T3 = Q0 Q1 Q2

## Slide 11: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map for T2
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
T2 = y1 y0
0
0
0
0
0
1
1
0
0
0
0
1
0
0
1
0
T2 = Q1 Q0

## Slide 12: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map for T1
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
T1 = y0
0
0
1
0
1
1
1
0
0
0
1
1
0
1
1
0
T1 = Q0

## Slide 13: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map for T0
 | 0 0 | 0 1 | 11 | 1 0
0 0 | 1 | 1 | 1 | 1
0 1 | 1 | 1 | 1 | 1
11 | 1 | 1 | 1 | 1
1 0 | 1 | 1 | 1 | 1
y1 y0
y3y2
T0 = 1

## Slide 14
T0 = 1
T1 = y0
T2 = y1 y0
T3 = y0 y1 y2
T0 = 1
T1 = Q0
T2 = Q1 Q0
T3 = Q0 Q1 Q2

## Slide 15: Four Bit Synchronous Counter
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
Clock
1
Q0
Clock
Q0
Q1
Q2
Q3
Q1
Q2
Q3
Q0
Q1
Q1
Q0
Q2
y0
y1
y2
y3
1
0
0
0
0
1
0
0
1
1
0
0
0
0
1
0
1
0
1
0
0
1
1
0
1
1
1
0
0
0
0
1

## Slide 16: Four Bit Synchronous Counter with Enable
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
T
>
Q
Q
Clock
Enable
Q0
Q1
Q2
Q3
Q0
Q1
Q1
Q0
Q2
1·x = x
0·x = 0

## Slide 17: Synchronous Four Bit Counter with D Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Next State Table
We will make a Karnaugh map to determine what connections need to be made between the outputs of the flip-flops and the inputs of the flip-flops
With D flip-flops, the value of the input of each stage should be the value of the Next state variable Yi

## Slide 18: Four Bit Counter Using D Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map for Y3
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
D3 = y1 y3 + y3 y0 + y3 y2 + y0 y1 y2 y3
D3 = y3  y0 y1 y2
y1 y3
y2 y3
y0 y3
See next slide
0
0
0
0
0
0
1
0
1
1
1
0
1
1
1
1

## Slide 19: Four Bit Counter Using D Flip-flops
D3 = y1 y3 + y3 y0 + y3 y2 + y0 y1 y2 y3
D3 = y3  y0 y1 y2
D3 = y3 (y0 + y1 + y2) + y0 y1 y2 y3
D3 = y3 (y0 y1 y2) + (y0 y1 y2 ) y3
factor
DeMorgan’s Theorem
XOR truth table

## Slide 20: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
D2 = y1 y2 + y0 y2 + y0 y1 y2
D2 = y2  y1 y0
Karnaugh Map for Y2
0
1
0
0
1
1
0
1
0
0
1
0
1
0
1
1
y1 y2
y0 y1 y2
y0 y2

## Slide 21: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
D1 = y1 y0 + y1 y0 = y1  y0
0
0
1
1
1
0
0
1
1
0
1
0
0
1
0
1

## Slide 22: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 1 0 1 0
1 0 1 0 | 1 0 1 1
1 0 1 1 | 1 1 0 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 1 1 1 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 0 0
Karnaugh Map
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
D0 = y0
1
1
0
1
0
0
0
1
1
1
0
0
1
0
0
1

## Slide 23: Four Bit Synchronous Counter
D0 = y0
D1 = y1  y0
D2 = y2  y1 y0
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q1
Q2
Q3
Q0
Q1
Q1
Q0
Q2
Q0
D3 = y3  y0 y1 y2
y0
y1
y2
y3

## Slide 24: Four Bit Synchronous Counter With Enable
D0 = y0E
D1 = y1  y0 E
D2 = y2  y1 y0 E
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q2
Q3
Q1
Q0
D3 = y3  y0 y1 y2 E
Enable
z
EQ0
EQ0Q1
EQ0Q1Q2
EQ0Q1Q2Q3
y0
y1
y2
y3

## Slide 25
D0 = y0
D’0 = y0  E
y 0 | E | y 0E
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
y0  0 = y0
y0  1 = y0
D’1 = y1  y0 E
D1 = y1  y0
D’2 = y2  y1 y0 E
D’3 = y3  y0 y1 y2 E
D2 = y2  y1 y0
D3 = y3  y0 y1 y2

## Slide 26: Four Bit Synchronous Counter With Enable
D0 = y0E
D1 = y1  y0 E
D2 = y2  y1 y0 E
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q2
Q3
Q1
Q0
D3 = y3  y0 y1 y2 E
Enable
z
EQ0
EQ0Q1
EQ0Q1Q2
EQ0Q1Q2Q3
y0
y1
y2
y3

## Slide 27
Add Parallel Load

## Slide 28: Four Bit Synchronous Counter With Enable
D0 = y0E
D1 = y1  y0 E
D2 = y2  y1 y0 E
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q2
Q3
Q1
Q0
D3 = y3  y0 y1 y2 E
Enable
z
EQ0
EQ0Q1
EQ0Q1Q2
EQ0Q1Q2Q3
y0
y1
y2
y3

## Slide 29: Four Bit Synchronous Counter With Enable and Parallel Load
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q2
Q3
Q1
Q0
Enable
z
EQ0
EQ0Q1
EQ0Q1Q2
EQ0Q1Q2Q3
0
1
0
1
0
1
0
1
Load
d0
d1
d2
d3
Parallel Inputs

## Slide 30: Four Bit Synchronous Counter With Enable and Parallel Load
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q2
Q3
Q1
Q0
Enable
z
EQ0
EQ0Q1
EQ0Q1Q2
EQ0Q1Q2Q3
0
1
0
1
0
1
0
1
Load
d0
d1
d2
d3
Parallel Inputs
Q0
Q1
Q2
Q3

## Slide 31: 74LS161 & 74LS163
From Texas Instruments Data Sheet
Power
Ripple Carry Out
Flip-flop Outputs
Setting this “low” clears the counter. With the 74LS161 this is asynchronous. With the 74LS163 this is synchronous.
Clock
Parallel Inputs
Setting this “low” causes the Parallel Input data to be loaded
Ground
Enable
Enable