## Slide 1: Other Counters
June 2025

## Slide 2: Decade Counter Using D Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 0 0 0 0
1 0 1 0 | d d d d
1 0 1 1 | d d d d
1 1 0 0 | d d d d
1 1 0 1 | d d d d
1 1 1 0 | d d d d
1 1 1 1 | d d d d
Karnaugh Map for Y3
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
y0 y1 y2
y0 y3
0
0
0
0
0
0
1
0
d
1
d
d
d
0
d
d
D3 = y0 y3 + y0 y1 y2

## Slide 3: Decade Counter Using D Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 0 0 0 0
1 0 1 0 | d d d d
1 0 1 1 | d d d d
1 1 0 0 | d d d d
1 1 0 1 | d d d d
1 1 1 0 | d d d d
1 1 1 1 | d d d d
Karnaugh Map for Y2
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
y0 y2
0
1
0
0
1
1
0
1
d
0
d
d
d
0
d
d
y0y1y2
y1 y2
D2 = y2  y1 y0
D2 = y1 y2 + y2 y0 + y2 y1 y0

## Slide 4: Decade Counter Using D Flip-flops
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 0 0 0 0
1 0 1 0 | d d d d
1 0 1 1 | d d d d
1 1 0 0 | d d d d
1 1 0 1 | d d d d
1 1 1 0 | d d d d
1 1 1 1 | d d d d
Karnaugh Map
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
D1 = y0 y1 y3 + y0 y1
0
0
1
1
1
0
0
1
d
0
d
d
d
0
d
d
y0y1
y0 y1 y3

## Slide 5: Four Bit Counter
Present state y3 y2y1 y0 | Next state
 | Y3 Y2Y1 Y0
0 0 0 0 | 0 0 0 1
0 0 0 1 | 0 0 1 0
0 0 1 0 | 0 0 1 1
0 0 1 1 | 0 1 0 0
0 1 0 0 | 0 1 0 1
0 1 0 1 | 0 1 1 0
0 1 1 0 | 0 1 1 1
0 1 1 1 | 1 0 0 0
1 0 0 0 | 1 0 0 1
1 0 0 1 | 0 0 0 0
1 0 1 0 | d d d d
1 0 1 1 | d d d d
1 1 0 0 | d d d d
1 1 0 1 | d d d d
1 1 1 0 | d d d d
1 1 1 1 | d d d d
Karnaugh Map
 | 0 0 | 0 1 | 11 | 1 0
0 0 |  |  |  | 
0 1 |  |  |  | 
11 |  |  |  | 
1 0 |  |  |  | 
y1 y0
y3y2
D0 = y0
1
1
0
1
0
0
0
1
d
1
d
d
d
0
d
d

## Slide 6: 0 – 15 Synchronous Counter
D0 = y0
D1 = y1  y0
D2 = y2  y1 y0
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
Q1
Q2
Q3
Q0
Q1
Q1
Q0
Q2
Q0
D3 = y3  y0 y1 y2
y0
y1
y2
y3
D0 = y0
D1 = y0 y1 y3 + y0 y1
D2 = y2  y1 y0
D3 = y0 y3 + y0 y1 y2
Changes for Decade Counter

## Slide 7: Synchronous Decade Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
D0 = y0
D1 = y0 y1 y3 + y0 y1
D3 = y0 y3 + y0 y1 y2
D2 = y2  y1 y0
y0 y1
y0 y1 y2
y0
y1
y2
y3

## Slide 8
Build a counter that counts in the sequence
1-4-6-5-3-7-2
0 0 1
1 0 0
1 1 0
1 0 1
0 1 1
1 1 1
0 1 0
A three-bit counter will work
and repeats.

## Slide 9: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 1 0 0
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 1 1 0
1 0 1 | 0 1 1
1 1 0 | 1 0 1
1 1 1 | 0 1 0
Karnaugh Map for Y2
 | 0 0 | 0 1 | 11 | 1 0
0 |  |  |  | 
1 |  |  |  | 
y1 y0
y2
y0 y2
d
1
1
0
0
1
0
1
y0 y2
D2 = y0y2 + y0 y2
D2 = y0  y2

## Slide 10: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 1 0 0
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 1 1 0
1 0 1 | 0 1 1
1 1 0 | 1 0 1
1 1 1 | 0 1 0
Karnaugh Map for Y1
 | 0 0 | 0 1 | 11 | 1 0
0 |  |  |  | 
1 |  |  |  | 
y1 y0
y2
d
1
0
0
1
1
1
0
y0 y1
y1 y2
D1 = y0 y1 + y1y2

## Slide 11: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 1 0 0
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 1 1 0
1 0 1 | 0 1 1
1 1 0 | 1 0 1
1 1 1 | 0 1 0
Karnaugh Map for Y0
 | 0 0 | 0 1 | 11 | 1 0
0 |  |  |  | 
1 |  |  |  | 
y1 y0
y2
d
0
0
1
1
1
0
1
y1 y2
y0 y1
y0 y1 y2
D0 = y0 y1y2 + y1y2 + y0 y1
D0 = y0 y1y2 + y1 (y2 + y0)
D0 = y1 y0y2 + y1 (y2 y0)
D0 = y1  y0y2

## Slide 12: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
D1 = y0 y1 + y1y2
D0 = y1  y0y2
D2 = y0  y2
y0
y1
y2
y0
y1
y2

## Slide 13
There are a couple of problems with this circuit
1-4-6-5-3-7-2
The circuit will count
There is no initialization
What happens if the circuit starts at 0-0-0 ?
but where does it start?

## Slide 14: What happens if the circuit starts at 0-0-0 ?
 | 0 0 | 0 1 | 11 | 1 0
0 | d | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
y1 y0
y2
Karnaugh Map for Y2
We counted this d as a zero

## Slide 15: What happens if the circuit starts at 0-0-0 ?
 | 0 0 | 0 1 | 11 | 1 0
0 | d | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
y1 y0
y2
Karnaugh Map for Y1
We counted this d as a zero

## Slide 16: What happens if the circuit starts at 0-0-0 ?
 | 0 0 | 0 1 | 11 | 1 0
0 | d | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
y1 y0
y2
Karnaugh Map for Y0
We counted this d as a zero

## Slide 17: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 1 0 0
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 1 1 0
1 0 1 | 0 1 1
1 1 0 | 1 0 1
1 1 1 | 0 1 0
We effectively had this next state as 0 0 0
If we start in the state 0 0 0, we get stuck there since that is also the next state.
We could put this next state as
0 0 1 and redo the Karnaugh table for Y0
Then if we started at 0 0 0, we would go next to 0 0 1
and not be stuck.

## Slide 18: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 1 0 0
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 1 1 0
1 0 1 | 0 1 1
1 1 0 | 1 0 1
1 1 1 | 0 1 0
Instead we will use a multiplexer to make a reset
Sending a reset signal will cause the value of 1 (0 0 1) to be loaded into the register

## Slide 19: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
D1 = y0 y1 + y1y2
D0 = y1  y0y2
D2 = y0  y2
y0
y1
y2
0
1
0
1
0
1
1
0
0
Reset/Run
y0
y1
y2

## Slide 22: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 1 0 0
0 1 0 | 0 0 1
0 1 1 | 1 1 1
1 0 0 | 1 1 0
1 0 1 | 0 1 1
1 1 0 | 1 0 1
1 1 1 | 0 1 0
We can add the ability to pause the counting or to count backwards
We can use a 4 to 1 multiplexer to add more functionality
Counting backwards will require a different next state table and Karnaugh maps

## Slide 23: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 0 1 0
0 1 0 | 1 1 1
0 1 1 | 1 0 1
1 0 0 | 0 0 1
1 0 1 | 1 1 0
1 1 0 | 1 0 0
1 1 1 | 0 1 1
Karnaugh Map for Y2
 | 0 0 | 0 1 | 11 | 1 0
0 |  |  |  | 
1 |  |  |  | 
y1 y0
y2
y1 y2
d
0
0
1
1
1
0
1
y0 y1
D2 = y1  y0 y2
y0 y1 y2
D2 = y0y2y1 + y0 y1 + y2 y1
D2 = y0y2y1 + (y0 + y2 ) y1
D2 = y0y2y1 + (y0 y2 ) y1

## Slide 24: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 0 1 0
0 1 0 | 1 1 1
0 1 1 | 1 0 1
1 0 0 | 0 0 1
1 0 1 | 1 1 0
1 1 0 | 1 0 0
1 1 1 | 0 1 1
Karnaugh Map for Y1
 | 0 0 | 0 1 | 11 | 1 0
0 |  |  |  | 
1 |  |  |  | 
y1 y0
y2
d
0
1
1
1
0
1
0
y0 y2
y0 y1
y0 y2
D1 = y0 y2 + y0y1 + y0y2
D1 = y0 Ꙩ y2 + y0y1

## Slide 25: Nonsequential Counter Using D Flip-flops
Present state y2y1 y0 | Next state
 | Y2Y1 Y0
0 0 0 | d d d
0 0 1 | 0 1 0
0 1 0 | 1 1 1
0 1 1 | 1 0 1
1 0 0 | 0 0 1
1 0 1 | 1 1 0
1 1 0 | 1 0 0
1 1 1 | 0 1 1
Karnaugh Map for Y0
 | 0 0 | 0 1 | 11 | 1 0
0 |  |  |  | 
1 |  |  |  | 
y1 y0
y2
d
1
0
1
0
1
1
0
y1 y2
y0 y1
D0 = y0 y1 + y1y2 + y0 y1
y0 y1
D0 = y0 Ꙩ y1 + y1y2

## Slide 26: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
D1 = y0 y1 + y1y2
D0 = y1  y0y2
D2 = y0  y2
y0
y1
y2
11
1
0
0
S1
y0
y1
y2
10
01
00
10
01
00
11
10
01
00
11
S0

## Slide 27: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
y0
y1
y2
11
1
0
0
S1
y0
y1
y2
10
01
00
10
01
00
11
10
01
00
11
S0
Code 0 0 -- Idle

## Slide 28: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
y0
y1
y2
11
1
0
0
S1
y0
y1
y2
10
01
10
01
00
11
10
01
00
11
S0
Code 0 1 – Count “Normal”
00
D1 = y0 y1 + y1y2
D0 = y1  y0y2
D2 = y0  y2

## Slide 29: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
y0
y1
y2
11
1
0
0
S1
y0
y1
y2
10
01
10
01
00
11
10
01
00
11
S0
Code 1 0 – Count “Backwards”
00
D0 = y0 Ꙩ y1 + y1y2
D1 = y0 Ꙩ y2 + y0y1
D2 = y1  y0 y2

## Slide 30: 1-4-6-5-3-7-2 Counter
D
>
Q
Q
D
>
Q
Q
D
>
Q
Q
Clock
y0
y1
y2
11
1
0
0
S1
y0
y1
y2
10
01
10
01
00
11
10
01
00
11
S0
Code 1 1 – Reset
00