## Slide 1: Analog Electronics Technology

## Slide 2: Analog Electronics Technology
Diodes
(Bipolar Junction Transistors)
Operational Amplifiers
BJTs
Op Amps

## Slide 3: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Standard diode application circuits
BJTs
Op Amps

## Slide 4: What You Should Learn Today
Diodes
Semiconductor basics
  Difference between insulators, conductors, and semiconductors
  What doping of semiconductors is
  Effect of doping on semiconductors
  Types of semiconductors (P and N)
  Relative amounts of conductors in P and N semiconductors

## Slide 5: Semiconductor Basics
Electrical Properties of Materials
Conductors
Insulators
Superconductors
Semiconductors
  Copper
  Aluminum
  Gold
  Rubber
  Plastic
  Ceramic

## Slide 6: A Quantum Mechanical Principle:
Electrons can only reside in specific energy states
Semiconductor Basics
Some energy levels have many possible states where electrons can reside
At other energy levels there are no states in which electrons can reside
Classical
Q.M.

## Slide 7
Places where electrons can be
Places where electrons can be
Available Energy States for Electrons as a Function of Energy
No electrons can be here
E

## Slide 8: More Quantum Mechanical Principles:
Unless excited, electrons reside in the lowest possible energy state
Only two electrons can reside in a given energy state
Semiconductor Basics
There are three possible outcomes

## Slide 9
Places where electrons can be
Places where electrons can be
Electrons partially fill the area
Outcome 1
No electrons can be here
E
Conductor

## Slide 10: Conductor
Applied Voltage Along Crystal
Places where electrons can be
No electrons can be here
Places where electrons can be
Electrons can easily move
E
It is like wanting to go somewhere and having plenty of room on the road

## Slide 11: Insulator
Places where electrons can be
No electrons can be here
Places where electrons can be
Electrons completely fill the area
E
Outcome 2

## Slide 12: Insulator
Applied Voltage Along Crystal
Electrons cannot move
Places where electrons can be
No electrons can be here
Places where electrons can be
Nothing can move if there is no place to move to
Traffic jam
E

## Slide 13: Semiconductor
Places where electrons can be
No electrons can be in the band gap
Places where electrons can be
Electrons completely fill the area
E
Because the band gap is so small, we can get electrons up to the higher level
Traffic jam here
We can show how to get here
Outcome 3

## Slide 14: Comparison of Electronic Structures
Conductor
Insulator
Semiconductor
E

## Slide 15: Semiconductor At Room Temperature
many closely spaced energy levels
band gap
Conduction Band
Valence Band
E
A few electrons have enough energy to get to the conduction band
The electrons leave behind holes which also allow current to flow

## Slide 16: 2-d Crystal Representation of Valence Band
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
electrons fill every available spot

## Slide 17: Crystal Representation with Electron Hole Pair
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
An electron gained enough energy to get to the conduction band
It left behind a hole in the valence band

## Slide 18: Crystal Representation with Electron Hole Pair
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Electrons in the conduction band can freely move around
Electrons near the hole can move into the hole

## Slide 19: Crystal Representation with Electron Hole Pair
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Electrons in the conduction band can fall into a hole and get trapped
New electron-hole pairs are always being created by thermal energy
Electron - hole cancellation
The equilibrium concentration of electrons in the conduction band is ni
ni is a function of temperature

## Slide 20: Doped Semiconductors
Impurities can be added to semiconductor crystals to change electrical characteristics.

## Slide 21: Crystal Representation of Doping
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
Si
Si
Si
Si
Si
Si
Atoms with extra electrons can replace Si atoms in the crystal
The extra electrons will easily get to the conduction band where they can move
This is called n-type doping
We call it n-type semiconductor because the extra electrons have negative charge
The atoms with extra electrons are called donor impurities

## Slide 22: Crystal Representation of Doping
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
Atoms with too few electrons can replace Si atoms in the crystal
This creates “holes” -- places where nearby electrons can move to
This is called p-type doping
We call it p-type semiconductor because the “holes” have positive charge

## Slide 23: Crystal Representation of Doping
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
Movement of holes

## Slide 24: Crystal Representation of Doping
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
Movement of holes

## Slide 25: Crystal Representation of Doping
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
We talk about “holes” moving – even though physically it is electrons that move
Movement of holes
The atoms with too few electrons are called acceptor impurities

## Slide 26: Typical Carrier Concentrations (Low Level Injection)
p type silicon
NA = 1015
n type silicon
ND = 1016
p = 1015 /cm3
ni = 1.02 x 1010 /cm3
n = 1.05 x 105 /cm3
n = 1016 /cm3
ni = 1.02 x 1010 /cm3
p = 1.05 x 104 /cm3
Hole concentrations
P type semiconductors have much higher hole concentrations
n type semiconductors have much higher electron concentrations
Electron
concentrations
n * p = ni 2
Notes: Doping between 1013 and 1021 /cm3

## Slide 27: Analog Electronics Technology
Semiconductor basics
  Difference between insulators, conductors, and semiconductors
  What doping of semiconductors is
  Effect of doping on semiconductors
  Types of semiconductors (P and N)
  Relative amounts of conductors in P and N semiconductors
What we discussed in this lecture