## Slide 1: Analog Electronics Technology
Diodes

## Slide 2: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits with known inputs
Solving diode circuits with unknown inputs
BJTs
Op Amps

## Slide 3: What you should learn today
Diode electrical characteristics
Diffusion Currents
Drift Currents

## Slide 4: Diffusion
Smoke from incense going throughout a room
When there is random motion, substances will naturally move from an area of high concentration to an area of lower concentration.
This process is called diffusion
Examples:
A drop of ink in a glass of water
The smell of perfume going throughout a room

## Slide 5: Typical Carrier Concentrations
p type silicon
NA = 1015
n type silicon
ND = 1016
p = 1015 /cm3
ni = 1.02 x 1010 /cm3
n = 1.05 x 105 /cm3
n = 1016 /cm3
ni = 1.02 x 1010 /cm3
p = 1.05 x 104 /cm3
Hole concentrations
P type semiconductors have much higher hole concentrations
n type semiconductors have much higher electron concentrations
Electron
concentrations

## Slide 6: Diodes
p type silicon
NA = 1015
n type silicon
ND = 1016
Eelectron
Making p-type semiconductor next to n-type semiconductor creates a p-n junction which is also called a diode

## Slide 7: Diffusion
In the p-n junction, the holes and the electrons have random motion because of thermal energy
The holes will diffuse from the high concentration (p-type semiconductor) towards the low concentration (n-type semiconductor).
The electrons will diffuse from the high concentration (n-type semiconductor) towards the low concentration (p-type semiconductor).

## Slide 8: Diodes
p type silicon
NA = 1015
n type silicon
ND = 1016
electron diffusion
Hole diffusion
current from electron diffusion
current from hole diffusion
Eelectron

## Slide 9: Electron – hole cancellation
Near the junction, electrons are diffusing into an area with many excess holes and holes are diffusing into an area with many excess electrons, resulting in much electron-hole cancellation.
Electrons in the conduction band can fall into the holes in the valence band, resulting in electron-hole cancellation.

## Slide 10: Crystal Representation of Doping
p-type
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
B
B
B
B
B
B
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
P
P
P
P
P
P
n-type

## Slide 11: Crystal Representation of Doping
p-type
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
B
B
B
B
B
B
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
P
P
P
P
P
P
n-type

## Slide 12: Space charge region
Near the junction, where electron-hole cancellation has occurred, very few free charge carriers remain.
  In the n region, positive ions will remain.
  In the p region, negative ions will remain.
The charged nuclei of the dopant atoms do remain, giving a region of electric field.
This is often called the “space charge region”

## Slide 13: Crystal Representation of Doping
p-type
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
B
B
B
B
B
B
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
P
P
P
P
P
P
n-type

## Slide 14: Space charge region for a step junction
p type silicon
n type silicon
charge
Distance from junction
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
Direction of electric field
hole drift
electron drift
current from hole drift
current from electron drift

## Slide 15: Drift Current
The space charge region generates an electric field.
The electric field causes charge carriers to drift.
Due to thermal energy, the charge carriers are in constant motion (Brownian motion)
Some charge carriers will naturally wander into the space charge region
The drift current opposes the diffusion current.
At equilibrium the drift current and the diffusion current are equal in magnitude and opposite in direction.

## Slide 16: Built-in voltage
Because of the space charge region, the diode has a built-in voltage
The built-in voltage depends upon the type of material (silicon, germanium, gallium arsenide), the temperature, and the doping levels in the p-type semiconductor and the n-type semiconductor
For a silicon at room temperature with normal doping levels, the built-in voltage is approximately 0.7 volts

## Slide 17: Diodes
p type silicon
NA = 1015
n type silicon
ND = 1016
Eelectron
Conduction band
Valence band

## Slide 18: Energy Band Diagram for PN Junction
Ev
Ec
Increasing energy of electron
Energy band for unbiased junction
-
p type silicon
n type silicon
Conduction band
Valence band

## Slide 19: Energy Band Diagram for PN Junction
Ev
Ec
Increasing energy of electron
Energy band for unbiased junction
p type silicon
n type silicon
Conduction band
Valence band

## Slide 20: Revisiting Diffusion Current
Ev
Ec
Increasing energy of electron
Energy band for unbiased junction
p type silicon
n type silicon
Conduction band
Valence band
Chart: Energy Distribution of Conductors
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 30 | 24.5619 | 20.1096 | 16.4643 | 13.4799 | 11.0364 | 9.0358 | 7.3979 | 6.0569 | 4.959 | 4.0601 | 3.3241 | 2.7215
EF

## Slide 21: Revisiting Diffusion Current
Ev
Ec
Increasing energy of electron
Energy band for unbiased junction
p type silicon
n type silicon
Conduction band
Valence band
Chart: Energy Distribution of Conductors
| 30 | 24.561922592339453 | 20.109601381069179 | 16.464349082820792 | 13.479868923516648 | 11.036383235143269 | 9.0358263573660604 | 7.3979089182481932 | 6.0568955398396618 | 4.9589666466475961 | 4.0600584970983808 | 3.324094750870016 | 2.7215385986823741
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12

## Slide 22: Energy Band Diagram for Forward Biased Diode
eVa
Ev
Ec
Increasing energy of electron
Energy band for unbiased junction
+
-
p type silicon
n type silicon
Polarity of applied voltage
drift current
diffusion current
Chart: Energy Distribution of Conductors
| 30 | 24.561922592339453 | 20.109601381069179 | 16.464349082820792 | 13.479868923516648 | 11.036383235143269 | 9.0358263573660604 | 7.3979089182481932 | 6.0568955398396618 | 4.9589666466475961 | 4.0600584970983808 | 3.324094750870016 | 2.7215385986823741
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12

## Slide 23: Energy Band Diagram for Reverse Biased Diode
eVa
Ev
Ec
Increasing energy of electron
Energy band for unbiased junction
p type silicon
n type silicon
+
-
Polarity of applied voltage
drift current
diffusion current
Chart: Energy Distribution of Conductors
| 30 | 24.561922592339453 | 20.109601381069179 | 16.464349082820792 | 13.479868923516648 | 11.036383235143269 | 9.0358263573660604 | 7.3979089182481932 | 6.0568955398396618 | 4.9589666466475961 | 4.0600584970983808 | 3.324094750870016 | 2.7215385986823741
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12

## Slide 24: Typical Carrier Concentrations
p type silicon
NA = 1015
n type silicon
ND = 1016
p = 1015 /cm3
ni = 1.02 x 1010 /cm3
n = 1.05 x 105 /cm3
n = 1016 /cm3
ni = 1.02 x 1010 /cm3
p = 1.05 x 104 /cm3

## Slide 25: Reverse Bias vs. Forward Bias
A reversed biased diode has very little current flow for moderate voltages.
A forward biased diode has very little resistance to current flow.
Minority carriers depleted by drift current
Diffusion current predominates because of reduced barrier height
Diffusion reduced because of increased barrier height

## Slide 26: What we studied today
Diode electrical characteristics
Diffusion Currents
Drift Currents