## Slide 1: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Standard diode application circuits
BJTs
Op Amps

## Slide 2: Diode Models & Different Methods of Solution
Use Shockley equation
Iterative solution
Graphical solution
Piecewise linear model
Semi-ideal model
Ideal model
Most accurate
Easiest
Semi-ideal model with resistance

## Slide 3
Solving Diode Circuits

## Slide 4: The schematic for a diode in a circuit
+
-
8 V
12 Ω
Diode symbol
“Arrow” points in forward direction (from p region to n region)

## Slide 5
Ideal Model

## Slide 6: Simple ideal model of diode
Perfect conductor when forward biased
Perfect insulator when reverse biased
This model can occasionally useful be for qualitative analysis of circuit.
I
V
Replace the forward biased diode with a wire
Remove the reverse biased diode from the circuit

## Slide 7: Using the simple ideal model of diode
From the circuit we can see that the diode is forward biased.
+
-
8 V
12 Ω
Replace the diode with a wire
Vdiode = 0 V
8 V = Iresistor * 12 Ω
Use KCL and KVL to solve the circuit
Idiode = Iresistor = 8 V / 12 Ω = 0.67A

## Slide 8: Using the simple ideal model of diode
From the circuit we can see that the diode is reverse biased.
+
-
8 V
12 Ω
Replace the diode with an open circuit (just remove the diode from the circuit)
Vdiode = 8 V
Idiode = Iresistor = 0 A

## Slide 9
Semi-Ideal Model

## Slide 10: Semi-ideal model of diode
Perfect conductor when forward biased beyond turn-on voltage
Perfect insulator when reverse biased
I
V
Vturnon (≈ 0.7 V for silicon or 0.3 V for germanium)
Replace the forward biased diode with a voltage source, Vturn-on
Remove the reverse biased diode from the circuit
Useful for semiquantitative analysis of circuit.

## Slide 11: Using the semi-ideal model of diode
From the circuit we can see that the diode is forward biased.
+
-
8 V
12 Ω
Replace the diode with a voltage source equivalent to the turn-on voltage
Vdiode = 0.7 V
Idiode = Iresistor = (8 V – 0.7 V) / 12 Ω
= 0.61A
+
-
0.7 V
Use KCL and KVL to solve the circuit
0 = 8 V – Iresistor ( 12 Ω) - (0.7 V)

## Slide 12
Semi-Ideal Model With Resistance

## Slide 13: Semi-ideal model of diode with resistance
Has output resistance when forward biased beyond certain voltage
Perfect insulator when reverse biased
Better model if parameters Von and ro are known
Often not a practical model.
I
V
Von
slope = 1/ro
Values of ro are usually between 2 Ω and 20 Ω

## Slide 14: Using the semi-ideal model of diode with resistance
From the circuit we can see that the diode is forward biased.
+
-
8 V
12 Ω
Replace the diode with a voltage source equivalent to the on voltage and a series resistor
Vdiode = Von + Idiode * ro
= 0.5 V + 3 Ω * 0.5 A
= 2.0 V
Idiode = Iresistor = (8 V – 0.5 V) / 15 Ω
= 0.5 A
+
-
0.5 V
3 Ω

## Slide 15
Graphical Analysis

## Slide 16: Graphical Analysis
Write equation from Kirchhoff's voltage law (KVL)
+
-
VA = 8 V
R1 = 12 Ω
ID
+
-
VD
VA – R1 ID – VD = 0
solve for the diode current, ID
ID = – VD /R1 + VA /R1
ID = – VD /12 + 2/3
Load line

## Slide 17: Graphical Analysis
Can be used with diode curve obtained from equation or from manufacturer.
ID = – VD /12 + 2/3
intercept = 2/3
slope = -1/12
Chart: Diode Current-Voltage Characteristics
| -4.9999999999998795E-2 | 1.2073675392798577E-15 | 5.000000000000121E-2 | 0.10000000000000121 | 0.15000000000000122 | 0.20000000000000123 | 0.25000000000000122 | 0.30000000000000121 | 0.3500000000000012 | 0.40000000000000119 | 0.45000000000000118 | 0.50000000000000122 | 0.55000000000000127 | 0.60000000000000131 | 0.65000000000000135 | 0.7000000000000014 | 0.75000000000000144 | 0.80000000000000149
 | -8.5519e-14 | 4.6629e-27 | 5.9058e-13 | 4.6691e-12 | 3.2834e-11 | 2.2734e-10 | 1.5706e-09 | 1.0847e-08 | 7.4906e-08 | 5.1729e-07 | 3.5723e-06 | 2.467e-05 | 0.00017036 | 0.0011765 | 0.0081248 | 0.056109 | 0.38748 | 2.6759
From graph estimate:
ID ≈ 0.60 A
VD ≈ 0.76 V
This plot came from Excel, using Io = 10-13 and T = 300 K
Load line
Plot load line

## Slide 18
Numerical Solutions
Automatic Calculator or Iterative

## Slide 19: Numerical Solution – Automatic Calculator Solution
Write equation from Kirchhoff's voltage law (KVL)
+
-
VA = 8 V
R1 = 12 Ω
ID
+
-
VD
VA – R1 ID – VD = 0
substituting values for our circuit gives
Replace the diode current, ID, with the expression from Shockley's equation
VA – R1 () – VD = 0
8 V – 12 Ω () – VD = 0
Some calculators will automatically solve this equation for VD, giving VD = 0.762 V
Once VD is found, use the Shockley equation to find ID
ID = = 0.603 A

## Slide 20: Numerical Solution – Iterative Calculator Solution
Write equation from Kirchhoff's voltage law (KVL)
VA = 8 V
+
-
R1 = 12 Ω
ID
+
-
VD
VA – R1 ID – VD = 0
Replace the diode current, ID, with the expression from Shockley's equation
VA – R1 () – VD = 0
Solve for the VD in the exponential

## Slide 21: Numerical Solution – Iterative Calculator Solution
VA – R1 () – VD = 0
Solve for the VD in the exponential
R1 () = VA – VD
= (VA – VD)/()
= (VA – VD)/() + 1
= ln[ (VA – VD)/() + 1 ]
= ln[ (VA – VD)/() + 1 ]

## Slide 22: Numerical Solution – Iterative Calculator Solution
= ln[ (VA – VD)/() + 1 ]
We now use this equation for iterative solution. Plug in our known values.
Guess a reasonable value for the diode voltage drop.
VD = 0.7 V is reasonable guess.
= ln[ ((8 V) – VD)/(10-13 A) + 1 ]
Plug the guess into the right side of the equation in order to calculate a new guess.
= ln[ ((8 V) – 0.7 V)/(10-13 A) + 1 ]
=
Plug this calculated value back into the right side of the equation in order to calculate a new guess.
Calculate a new value.

## Slide 23: Numerical Solution – Iterative Calculator Solution
= ln[ ((8 V) – VD)/(10-13 A) + 1 ]
= ln[ ((8 V) – 0.762407 V)/(10-13 A) + 1 ]
=
Plug this calculated value back into the right side of the equation in order to calculate a new guess.
= ln[ ((8 V) – 0.762185 V)/(10-13 A) + 1 ]
=
Since this is essentially the same as what we plugged in, it is the answer.
Value calculated last time

## Slide 24: Numerical Solution – Iterative Calculator Solution
=
Now use the Shockley equation to calculate the current.
=
=
= 0.603 A

## Slide 26: More complex circuits
If one diode is connected to a complex linear circuit, find the Thevenin equivalent of the linear circuit and then solve in a similar manner.

## Slide 27: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Find the Thevenin resistance and then use the superposition principle to find the Thevenin voltage equivalent of everything to the left of the diode.

## Slide 28: Example
Find the Thevenin Resistance
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Replace the current source with an open circuit.
Replace the voltage source with a wire (short circuit).

## Slide 29: Example
Find the Thevenin Resistance
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Find the equivalent resistance of the 12 Ω resistor in parallel with the 6 Ω resistor.
Req = (1/12 + 1/6)-1 = 4 Ω
4 Ω
Now the two 4 Ω resistors are in series. Adding them together gives
Rth = (4 Ω + 4 Ω) = 8 Ω

## Slide 30: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Now use the superposition principle to find the Thevenin voltage equivalent of everything to the left of the diode.

## Slide 31: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
First remove the current source to find the Thevenin voltage that results from the voltage source. The current source is replaced by an open circuit.

## Slide 32: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Since there is no current flowing through the 4 Ω resistor, there is no voltage drop across it. It can be replaced by a wire.

## Slide 33: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
The output voltage can now be calculated using the voltage divider rule:
Vout, voltage source = (3 V) (6 Ω)/(6 Ω + 12 Ω) = 1 V
Vout
-
+

## Slide 34: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Now find the Thevenin voltage attributable to the current source. To do this, short circuit the voltage source.

## Slide 35: Example
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Find the equivalent resistance of the 12 Ω resistor in parallel with the 6 Ω resistor.
Req = (1/12 + 1/6)-1 = 4 Ω
Now find the equivalent resistance of the two 4 Ω resistors in series.
Req,tot = (4 Ω + 4 Ω) = 8 Ω
Vout, current source = (0.25 A) (8 Ω) = 2 V
Vth = 1 V + 2 V = 3 V

## Slide 36: Example
+
-
3 V
8 Ω
Thevenin equivalent circuit.

## Slide 37: Example
+
-
Vth = 3 V
Rth = 8 Ω
Using Kirchhoff’s voltage law:
ID
ID =(Vth – Von)/Rth
Replace diode with voltage source
We will use the semi-ideal model
+
-
Von = 0.7 V
ID =(2.3 V)/8Ω = 0.29 A

## Slide 38: Example 2. Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω

## Slide 39: Example 2. Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
Find Thevenin Equivalent Resistance
ID
R = 4 Ω
Rth = (8 Ω) (4 Ω) / (8 Ω + 4 Ω) = 2.67 Ω
Vth = (3 V) (4 Ω) / (8 Ω + 4 Ω) = 1.0 V
Find Thevenin Equivalent Voltage

## Slide 40: Example 2. Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 1 V
Rth = 2.67 Ω
Use Semi-ideal Model
ID
ID = (1 V – 0.7 V) / (2.67 Ω) = 0.1124 A
Von = (0.7 V)
-
+
Replace diode with voltage source

## Slide 41: Example 2. Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
Using Kirchhoff’s current law:
ID
R = 4 Ω
I1
I2
= /(4 Ω) = 0.175 A
= 0.175 A + 0.1124 A = 0.287 A
+
-
Von = (0.7 V)
= +
Use Kirchhoff’s voltage law around loop on the right :

## Slide 42: Example 2. Alternate Solution. Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
ID
R = 4 Ω
I1
I2
= /(4 Ω) = 0.175 A
+
-
Von = (0.7 V)
Use Kirchhoff’s voltage law around loop on the right:
Use Kirchhoff’s voltage law around the outer loop:
= /(8 Ω) = 0.2875 A

## Slide 43: Example 2. Alternate Solution. Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
Using Kirchhoff’s current law:
ID
R = 4 Ω
I1
I2
+
-
Von = (0.7 V)
= +
= -
= 0.287 A -0.175 A
= 0.112 A

## Slide 44: Example 2. Solve Using Iteration Equations
+
-
Vth = 1 V
Rth = 2.67 Ω
Equivalent Circuit
ID
0 = Vth – Rth ID - VD
0 = Vth – Rth Io - VD
Rth Io = Vth - VD
= (Vth – VD)/ Rth Io
= (Vth – VD)/ Rth Io + 1
VD = VT ln[(Vth – VD)/ Rth Io + 1]

## Slide 45: Example 2. Solve Using Iteration Equations
Equation for iterating
VD = VT ln[(Vth – VD)/ Rth Io + 1]
= ln[ ((1 V) –VD)/(10-12 A) + 1 ]
= ln[ ((1 V) –0.7 V)/(10-12 A) + 1 ]
=
=
= = (10-12 A) *[ e(0.6621/0.0259) – 1 ] = 0.1265 A

## Slide 46: Example 2. Solve Using Iteration Equations
=
= = (10-12 A) *[ e(0.6621/0.0259) – 1 ] = 0.1265 A
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω
= /(4 Ω) = 0.1655 A
= 0.1655 A + 0.1265 A = 0.292 A

## Slide 47
We also did an iterative solution

## Slide 48: Comparison of results
 | Numerical Iteration | Semi-Ideal Model
Diode Voltage | 0.6621 V | 0.7 V (assumed)
Diode Current | 0.1265 A | 0.1124 A
Resistor Current | 0.292 A | 0.287 A

## Slide 49: Multiple diode circuits
4 V
R2 = 2 kΩ
0 V
+10 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Find the output voltage and the currents through each diode.
D1
D2
Find whether each diode is conducting (forward biased) or nonconducting (reverse biased).
A
The voltage at node A will be key in determining this.
First assume that diode D1 is reversed biased, and look at the remaining circuit with D1 removed.
We can easily see that diode D2 is forward biased under these conditions.
I = 9.3 V /8 kΩ = 1.1625 mA
VA = 1.1625 mA * 2 kΩ = 2.325 V
If D1 is reverse biased
+
-
Von = (0.7 V)

## Slide 50: Multiple diode circuits
4 V
R2 = 2 kΩ
0 V
+10 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Find the output voltage and the currents through each diode.
D1
D2
What happens if we connect diode D1 to the circuit?
A
If it were reverse biased, nothing would happen.
IR1 = 6 V /6 kΩ = 1.0 mA
VA = 2.325 V
It will be forward biased.
The current through R2 will rise.
The voltage at node A will rise.
The output voltage will rise.
Can the voltage at node A rise enough to reverse bias diode D2?
No!
VA = 3.3 V
VA = 4.0 V
IR2 = 3.3 V /2 kΩ = 1.625 mA
ID2 = IR1 = 1.0 mA
ID1 = IR2 - ID2 = 1. 625 mA - 1.0 mA
= 0. 625 mA

## Slide 51: Multiple diode circuits
2 V
R2 = 2 kΩ
0 V
+10 V
R1 = 6 kΩ
Vout
D1
D2
Find whether each diode is conducting (forward biased) or nonconducting (reverse biased).
A
We can easily see that diode D2 is forward biased under these conditions.
I = 9.3 V /8 kΩ = 1.1625 mA
VA = 1.1625 mA * 2 kΩ = 2.325 V
If D1 is reverse biased
+
-
Von = (0.7 V)

## Slide 52: Practice Problems
Use the semi-ideal model of the diode to solve the following problems

## Slide 53: Practice Problem: Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω

## Slide 54: Practice Problem: Find the current through the diode and the output voltage
Vout
5 V
ID
20 kΩ
20 kΩ
-5 V
Vout
5 V
ID
20 kΩ
-3 V

## Slide 55: Practice Problem: Find the current through the diode and the output voltage
Vout
2 V
ID
5 kΩ
20 kΩ
-8 V
Vout
5 V
ID
20 kΩ
-5 V

## Slide 56: Practice Problem: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω

## Slide 57: Practice Problem: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 16 Ω
R = 8 Ω
R = 2 Ω

## Slide 58: Diode Models & Different Methods of Solution
Use Shockley equation
Iterative solution
Graphical solution
Piecewise linear model
Semi-ideal model
Ideal model
Most accurate
Easiest
Semi-ideal model with resistance
What we talked about today