## Slide 1: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Standard diode application circuits
BJTs
Op Amps

## Slide 2: What we will do today
Use Thevenin equivalent circuits to solve more complicated diode circuits
We will mainly use the semi-ideal model of the diode to solve the circuit.
We will demonstrate that other models of the diode can be used to solve a problem once the Thevenin equivalent circuit has been found.
Solving diode circuits

## Slide 4: More complex circuits
If one diode is connected to a complex linear circuit, find the Thevenin equivalent of the linear circuit and then solve like before.

## Slide 5: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Find the Thevenin resistance and then use the superposition principle to find the Thevenin voltage equivalent of everything to the left of the diode.

## Slide 6: Example 1.
Find the Thevenin Resistance
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Replace the current source with an open circuit.
Replace the voltage source with a wire (short circuit).

## Slide 7: Example 1.
Find the Thevenin Resistance
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Find the equivalent resistance of the 12 Ω resistor in parallel with the 6 Ω resistor.
Req = (1/12 + 1/6)-1 = 4 Ω
4 Ω
Now the two 4 Ω resistors are in series. Adding them together gives
Rth = (4 Ω + 4 Ω) = 8 Ω

## Slide 8: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Now use the superposition principle to find the Thevenin voltage equivalent of everything to the left of the diode.

## Slide 9: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
First remove the current source to find the Thevenin voltage that results from the voltage source. The current source is replaced by an open circuit.

## Slide 10: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Since there is no current flowing through the 4 Ω resistor, there is no voltage drop across it. It can be replaced by a wire.

## Slide 11: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Vout, voltage source = (3 V) (6 Ω)/(6 Ω + 12 Ω) = 1 V
Vout
-
+
The output voltage can now be calculated using the voltage divider rule

## Slide 12: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Now find the Thevenin voltage attributable to the current source. To do this, short circuit the voltage source.

## Slide 13: Example 1.
+
-
3 V
0.25 A
12 Ω
6 Ω
4 Ω
Find the equivalent resistance of the 12 Ω resistor in parallel with the 6 Ω resistor.
Req = (1/12 + 1/6)-1 = 4 Ω
Now find the equivalent resistance of the two 4 Ω resistors in series.
Req,tot = (4 Ω + 4 Ω) = 8 Ω
Vout, current source = (0.25 A) (8 Ω) = 2 V
Vth = 1 V + 2 V = 3 V

## Slide 14: Example 1.
+
-
3 V
8 Ω
Thevenin equivalent circuit.

## Slide 15: Example 1.
+
-
Vth = 3 V
Rth = 8 Ω
Using Kirchhoff’s voltage law:
ID
Vth – ID Rth – Von = 0
Replace diode with voltage source
We will use the semi-ideal model
+
-
Von = 0.7 V
ID =(2.3 V)/8Ω = 0.29 A
ID =(Vth – Von)/Rth

## Slide 16: Example 2a. Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω

## Slide 17: Example 2a. Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
Find Thevenin Equivalent Resistance
ID
R = 4 Ω
Rth = (8 Ω) (4 Ω) / (8 Ω + 4 Ω) = 2.67 Ω
Vth = (3 V) (4 Ω) / (8 Ω + 4 Ω) = 1.0 V
Find Thevenin Equivalent Voltage

## Slide 18: Example 2a.
+
-
Vth = 1 V
Rth = 2.67 Ω
Use Semi-ideal Model
ID
ID = (1 V – 0.7 V) / (2.67 Ω)
Von = (0.7 V)
-
+
Replace diode with voltage source
Vth – ID Rth – Von = 0
ID = (Vth – Von)/Rth
ID = 0.1124 A
ID

## Slide 19: Example 2a. Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
Using Kirchhoff’s current law:
ID
R = 4 Ω
I1
I2
= /(4 Ω) = 0.175 A
= 0.175 A + 0.1124 A = 0.287 A
+
-
Von = (0.7 V)
= +
Use Kirchhoff’s voltage law around loop on the right :

## Slide 20: Example 2 b. Alternate Solution (without Thevenin equivalent). Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
ID
R = 4 Ω
I1
I2
Determine that it is forward biased
Remove from circuit
Use voltage divider rule
+
-
Von = (0.7 V)

## Slide 21: Example 2 b. Alternate Solution (without Thevenin equivalent). Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
ID
R = 4 Ω
I1
I2
= /(4 Ω) = 0.175 A
+
-
Von = (0.7 V)
Use Kirchhoff’s voltage law around loop on the right:
Use Kirchhoff’s voltage law around the outer loop:
= /(8 Ω) = 0.2875 A

## Slide 22: Example 2 b. Alternate Solution. Find the current through the diode and through the 8 Ohm resistor
+
-
Vth = 3 V
R = 8 Ω
Using Kirchhoff’s current law:
ID
R = 4 Ω
I1
I2
+
-
Von = (0.7 V)
= +
= -
= 0.287 A -0.175 A
= 0.112 A

## Slide 23: Example 2 c. Solve Using Shockley Equations
+
-
Vth = 1 V
Rth = 2.67 Ω
Thevenin Equivalent Circuit
ID
0 = Vth – Rth ID - VD
0 = Vth – Rth Io - VD
Rth Io = Vth - VD
Iteration
KVL
Substitute
Solve for VD
Io must be known

## Slide 24: Example 2 c. Solve Using Iteration Equations
Equation for iterating
=
Thevenin voltage
Thermal voltage
Substitute known values
Guess a value
Calculate a new value

## Slide 25: Example 2 c. Solve Using Iteration Equations
iterating
=
=
=
=

## Slide 26: Example 2 c. Solve Using Iteration Equations
= = (10-12 A) *[ e(0.6621/0.0259) – 1 ]
= 0.1265 A

## Slide 27: Example 2 c. Solve Using Iteration Equations
=
= 0.1265 A
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω
= /(4 Ω) = 0.1655 A
= 0.1655 A + 0.1265 A = 0.292 A
I1
I2

## Slide 28: Comparison of results
 | Numerical Iteration | Semi-Ideal Model
Diode Voltage | 0.6621 V | 0.7 V (assumed)
Diode Current | 0.1265 A | 0.1124 A
Resistor Current | 0.292 A | 0.287 A

## Slide 29: Example 3. Find the currents through the diode and through the 200 Ω resistor
Find the Thevenin equivalent resistance at the diode
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
ID
IS = 11.5 mA
R = 400 Ω
R = 1 kΩ

## Slide 30: Example 3.
Find the Thevenin equivalent resistance at the diode
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
IS = 11.5 mA
R = 400 Ω
R = 1 kΩ
Remove the current source
Short out the voltage source
The 1 kΩ resistor can be removed since only one of its terminals is connected to the circuit
The Thevenin equivalent resistance is 1 kΩ

## Slide 31: Example 3.
Use the superposition principle to find the Thevenin equivalent voltage.
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
IS = 11.5 mA
R = 400 Ω
R = 1 kΩ
Find the Thevenin equivalent voltage that is due to the voltage source
Remove the current source
No current flows through any resistor, so there are no voltage drops
Vth,V = 8 V
+
-
Vth

## Slide 32: Example 3. Find the currents through the diode and through the 200 Ω resistor
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
IS = 11.5 mA
R = 400 Ω
R = 1 kΩ
Find the Thevenin equivalent voltage that is due to the current source
Short out the voltage source
No current flows through the 400 Ω resistors, so there are no voltage drops across them.
They can be replaced with wires
Vth,I = ‒ 11.5 mA * 200 Ω
= ‒ 2.3 V
+
-
Vth

## Slide 33: Example 3.
Thevenin Equivalent Circuit
+
-
Vth = 5.7 V
Rth = 1 kΩ
I1
ID
The diode is forward biased.
Replace the diode with a voltage source
+
-
Von = 0.7 V
Apply KVL to the loop
5.7 V ‒ ID * ( 1 kΩ ) ‒ 0.7 V = 0
ID = 5.0 V / ( 1 kΩ )
= 5.0 mA

## Slide 34: Example 3. Find the currents through the diode and through the 200 Ω resistor
Use KCL to find the current through the 200 Ω resistor
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
ID
IS = 11.5 mA
R = 400 Ω
R = 1 kΩ
ID = 5.0 mA
I2 = ID + IS
I2 = 5.0 mA + 11.5 mA
I2 = 16.5 mA

## Slide 36: Example 3 b. Find the currents through the diode and through the 200 Ω resistor
Find the Thevenin equivalent resistance at the diode
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
ID
IS = 45 mA
R = 400 Ω
R = 1 kΩ

## Slide 37: Example 3 b. Find the currents through the diode and through the 200 Ω resistor
Find the Thevenin equivalent resistance at the diode
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
IS = 45 mA
R = 400 Ω
R = 1 kΩ
Remove the current source
Short out the voltage source
The 1 kΩ resistor can be removed since only one of its terminals is connected to the circuit
The Thevenin equivalent resistance is 1 kΩ

## Slide 38: Example 3 b. Find the currents through the diode and through the 200 Ω resistor
Use the superposition principle to find the Thevenin equivalent voltage.
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
IS = 45 mA
R = 400 Ω
R = 1 kΩ
Find the Thevenin equivalent voltage that is due to the voltage source
Remove the current source
No current flows through any resistor, so there are no voltage drops
Vth,V = 8 V
+
-
Vth

## Slide 39: Example 3 b. Find the currents through the diode and through the 200 Ω resistor
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
IS = 45 mA
R = 400 Ω
R = 1 kΩ
Find the Thevenin equivalent voltage that is due to the current source
Short out the voltage source
No current flows through the 400 Ω resistors, so there are no voltage drops across them.
They can be replaced with wires
Vth,I = ‒ 45 mA * 200 Ω
= ‒ 9.0 V
+
-
Vth
Vth,tot = Vth,v + Vth,I = ‒ 1.0 V Ω

## Slide 40: Example 3 b. Find the currents through the diode and through the 200 Ω resistor
Thevenin Equivalent Circuit
+
-
Vth = -1.0 V
Rth = 1 kΩ
I1
ID
The diode is reverse biased.
Replace the diode with an open circuit
ID = 0

## Slide 41: Example 3 b. Find the currents through the diode and through the 200 Ω resistor
Use KCL to find the current through the 200 Ω resistor
+
-
Vin = 8 V
R = 400 Ω
R = 200 Ω
I1
I2
ID
IS = 45 mA
R = 400 Ω
R = 1 kΩ
ID = 0 mA
I2 = ID + IS
I2 = 0 mA + 45 mA
I2 = 45 mA
= ID = 0 mA

## Slide 42: What have we learned today?
Thevenin equivalent circuits can help us solve more complicated diode circuits
Once we find the Thevenin equivalent circuit, we can use any of the methods that we learned last time to solve the circuit.
We will normally use the semi-ideal model of the diode to solve the circuit.
If it is obvious if the diode is forward biased or reverse biased, the appropriate model can be substituted (voltage source or open circuit) and normal methods used to solve the circuit without finding the Thevenin equivalent circuit.

## Slide 44: Practice Problems
Use the semi-ideal model of the diode to solve the following problems

## Slide 45: Practice Problem: Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω

## Slide 46: Practice Problem: Find the current through the diode and the output voltage
Vout
5 V
ID
20 kΩ
20 kΩ
-5 V
Vout
5 V
ID
20 kΩ
-3 V
+
-
+
-
5 V
5 V

## Slide 47: Practice Problem: Find the current through the diode and the output voltage
Vout
2 V
ID
5 kΩ
20 kΩ
-8 V
Vout
5 V
ID
20 kΩ
-5 V

## Slide 48: Practice Problem: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω

## Slide 49: Practice Problem: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 16 Ω
R = 8 Ω
R = 2 Ω