## Slide 1: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Standard diode application circuits
BJTs
Op Amps
Last lecture.

## Slide 2: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Solutions to practice problems
Standard diode application circuits
BJTs
Op Amps
Today

## Slide 3: Practice Problems
Use the semi-ideal model of the diode to solve the following problems

## Slide 4: Practice Problem 1: Find the current through the diode and through the 8 Ohm resistor
+
-
Vin = 3 V
R = 8 Ω
ID
R = 4 Ω
The diode is reverse biased.
-
+
ID = 0 A
IR8 = (3 V) / (8 Ω + 4 Ω )
= 0.25A

## Slide 6: Practice Problem 2: Find the current through the diode and the output voltage
Vout
5 V
ID
20 kΩ
20 kΩ
-5 V
The diode is forward biased.
+
-
+
-
5 V
5 V
+
-
Von = (0.7 V)
Replace the diode with a voltage source.
Use KVL around the loop
0 = (5 V) - ID (20 kΩ) - 0.7 V - ID (20 kΩ) + (5 V)
9.3 V = ID (40 kΩ)
ID = 9.3 V / (40 kΩ) = 0.23 mA
Vout = - 5 V + [9.3 V / (40 kΩ)] * (20 kΩ) = - 0.35 V

## Slide 8: Practice Problem 3: Find the current through the diode and the output voltage
The diode is forward biased.
+
-
+
-
5 V
3 V
Von = (0.7 V)
Replace the diode with a voltage source.
Use KVL around the loop
0 = (5 V) - ID (20 kΩ) - 0.7 V + (3 V)
7.3 V = ID (20 kΩ)
ID = 7.3 V / (20 kΩ) = 0.365 mA
Vout = - 3 V + 0.7 = -2.3 V
Vout
5 V
ID
20 kΩ
-3 V
+
-

## Slide 10: Practice Problem 4: Find the current through the diode and the output voltage
Vout
2 V
ID
5 kΩ
20 kΩ
-8 V
ID = 9.3 V / (25 kΩ) = 0.372 mA
Vout = 2 V - (5 kΩ) ID = 2 V - (5 kΩ) *9.3 V / (25 kΩ)
Vout = 0.14 V

## Slide 12: Practice Problem 5: Find the current through the diode and the output voltage
Vout
5 V
ID
20 kΩ
-5 V
The diode is reverse biased.
There is no current through the diode.
There is no voltage drop across the resistor.
Vout = 5 V

## Slide 14: Practice Problem 6: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω
V4Ω = (16 V)*(4Ω )/ (20 Ω ) = 3.2 V
+
-
The diode is forward biased.
Look at the circuit without the diode.
Use the voltage divider rule to find the voltage drop across the 4 ohm resistor.
Von = (0.7 V)

## Slide 15: Practice Problem 6: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω
+
-
The diode is forward biased.
Von = (0.7 V)
We have the equivalent circuit (according to the semi-ideal diode model)
We can use any method that we want to solve it
Mesh analysis
Superposition
Any combination of methods

## Slide 16: Practice Problem 6: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω
+
-
Von = (0.7 V)
Mesh analysis
We can write the mesh equations by inspection
Solve the set of mesh equations
I1
I2
IR8 = I1 =
ID = I2 =

## Slide 17: Practice Problem 6: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω
+
-
Von = (0.7 V)
Superposition
First look at the currents due to the 16 volt source
Calculate current through the resistors and diode
I1
Short out the 0.7 volt source
No current will flow through the 4 Ω resistor
I1 = 16 V / (16 Ω) = 1 A

## Slide 18: Practice Problem 6: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω
+
-
Von = (0.7 V)
Superposition cont.
Now look at the currents due to the 0.7 volt source
Calculate the current through the 4 ohm resistor
IR4
Short out the 16 volt source
IR4 = (0.7 V) / (4 Ω) = 0.175 A
Calculate the current through the outer loop
I3
I3 = (0.7 V) / (16 Ω) = 0.044 A
Note these loops are defined in a counterclockwise direction

## Slide 19: Practice Problem 6: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 4 Ω
R = 8 Ω
+
-
Von = (0.7 V)
Superposition cont.
Add the currents together
IR4
IR8 = I1 - I3 = 1 A - 0.044 A = 0.956 A
I3
ID = I1 - I3 - IR4 = 1 A - 0.044 A - 0.175 A
IR8
ID = 0.781 A
I1

## Slide 21: Practice Problem 7: Find the current through the diode and through the 8 Ohm resistors
+
-
Vin = 16 V
R = 8 Ω
ID
R = 16 Ω
R = 8 Ω
R = 2 Ω
+
-
Von = (0.7 V)
Mesh analysis
We can write the mesh equations by inspection
Solve the set of mesh equations
I1
I2
The diode is forward biased
IR8 = I1 =
ID = I2 =