## Slide 1: Analog Electronics Technology
Solving diode circuits with varying inputs

## Slide 2: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Circuits with varying inputs
Standard diode application circuits

## Slide 3: What we will do today
Small signal response of diodes
Large signal response of diodes
Transfer characteristics
Solving diode circuits with varying inputs

## Slide 4
Inputs to diode circuits often change
Small signal changes
Large signal changes
The input changes slightly around an average value that doesn’t change
Example:
=
The input changes by large amounts
Example:
=
Chart: Small Signal Changes
Chart: Large Signal Changes

## Slide 5
Small signal response of diode circuits

## Slide 6: Look at the current voltage curve
quiescent (DC) point
VD = 0.727 V
ID = 160 mA
We can approximate the curve with a tangent line
An increased voltage
Causes an increased current
slope of tangent line is =

## Slide 7: Shockley Ideal Diode Equation
+
-
VDC = 10 V
R1 = 80 Ω
VD
Vout
+
-
VAC
rd = VT/IQ

## Slide 8: To analyze a circuit with a DC component and a small AC component
+
-
VDC = 10 V
R1 = 80 Ω
VD
Vout
+
-
VAC

## Slide 9
quiescent point analysis (ignore VAC)
small signal analysis
VDC = 10 V
R1 = 80 Ω
VD
Vout = VQ
+
-
rd = VT/IQ
+
-
R1 = 80 kΩ
vout
+
-
VAC
First we find the quiescent point (DC conditions)
Then we find the small signal response
IQ

## Slide 10
quiescent point
VAC must be small

## Slide 11: Example 1: Find the ac voltage across the diode if the input voltage VAC is 500 mV sin(ω t)
+
-
VDC = 10 V
R1 = 80 Ω
VD
Vout = VQ + vac
-
VAC
ac component of output voltage
DC component of output voltage
+

## Slide 12: Example 1: Find the ac voltage output if the input voltage VAC is 500 mV sin(ω t)
+
-
VDC = 10 V
R1 = 80 Ω
ID
VD
VAC
First do the DC analysis with VAC = 0
The diode is forward biased, so VD ≈ 0.7 V
Use Kirchhoff’s voltage law and Ohm’s law to solve for the current
Von = (0.7 V)
-
+
Replace diode with voltage source
ID = (10.0 V - 0.7 V) / (80 Ω)
ID = 116 mA

## Slide 13: Example 1: Find the ac voltage output if the input voltage VAC is 500 mV sin(ω t)
Calculate the resistance rd
= 0.22 Ω
rd = VT/IQ
+
-
R1 = 80 Ω
VAC

## Slide 14: Example 1: Find the ac voltage output if the input voltage VAC is 500 mV sin(ω t)
Calculate the ac component of the current
sin(ω t)
We can use Ohm’s law to calculate the AC voltage across the diode
vdiode = sin(ω t) (0.22 Ω)
vdiode = 1.4 V sin(ω t)
rd = VT/IQ = 0.22 Ω
+
-
R1 = 80 Ω
VAC

## Slide 16: Example 2: Find the ac voltage across the diode if the input voltage VAC is 20 mV sin(ω t)
+
-
VDC = 5.9 V
R1 = 2 kΩ
VD
Vout = VQ + vac
-
VAC
ac component of output voltage
DC component of output voltage
+

## Slide 17: Example 2: Find the ac voltage across the diode if the input voltage VAC is 20 mV sin(ω t)
+
-
VDC = 5.9 V
R1 = 2 kΩ
VAC
IQ = 5.2 V /2 k Ω = 2.6 mA
rAC = VT / IQ = 0.026 v /2.6 mA = 10 Ω
Calculate dc current
Calculate ac diode resistance
Replace diode with voltage source
Von = (0.7 V)
-
+
Short out the AC source

## Slide 18: Example 2: Find the ac voltage across the diode if the input voltage VAC is 20 mV sin(ω t)
+
-
VDC = 5.9 V
R1 = 2 kΩ
Vout = VQ + vac
-
VAC
+
IQ = 5.2 V /2 k Ω = 2.6 mA
rAC = VT / IQ = 0.026 v /2.6 mA = 10 Ω
Calculate dc current
Calculate ac diode resistance
Calculate ac current
Iac = 20 mV sin(ω t) /2010 Ω ≈10 μA sin(ω t)
Calculate ac voltage
vac = 10 μA sin(ω t) * 10 Ω ≈100 μV sin(ω t)
Replace diode with resistor
rd = VT/IQ
= 10 Ω

## Slide 19
Large signal response of diode circuits

## Slide 20: Transfer Characteristics
+
-
Vin
R
-
+
Vout
Calculate the output voltage if the diode is forward biased
For what input voltages is the diode forward biased?
Calculate the output voltage if the diode is not forward biased
Vout
Vin
For what input voltages is the diode not forward biased?

## Slide 21: Transfer Characteristics
+
-
Vin
R
-
+
Vout
Calculate the output voltage if the diode is forward biased
Kirchhoff's Voltage Law
Vout
Vin
Von = (0.7 V)
Replace diode with voltage source
+
-
For what input voltages is the diode forward biased?
Vin - (0.7 V) - Vout = 0
Vout = Vin - (0.7 V)
Vin ≥ (0.7 V)
0.7 V

## Slide 22: Transfer Characteristics
+
-
Vin
R
-
+
Vout
Vout
Vin
0.7 V
Calculate the output voltage if the diode is not forward biased
Remove diode from circuit
No current flows through the resistor

## Slide 23: Find the Transfer Characteristics of the same Circuit but with the Diode Reversed
+
-
Vin
R
-
+
Vout

## Slide 24: Find the Transfer Characteristics of the same Circuit but with the Diode Reversed
+
-
Vin
R
-
+
Vout
Replace diode with voltage source
-
+
Calculate the output voltage if the diode is forward biased
Kirchhoff's Voltage Law
Vin + (0.7 V) - Vout = 0
Vout = Vin + (0.7 V)
For what input voltages is the diode forward biased?
Vin ≤ (-0.7 V)
Von = (0.7 V)

## Slide 25: Find the Transfer Characteristics of the same Circuit but with the Diode Reversed
+
-
Vin
R
-
+
Vout
Vout
Vin
-0.7 V
What will the output be if the diode is not forward biased?

## Slide 26: Find the Transfer Characteristics of this Circuit
+
-
Vin
R
-
+
Vout
-
+
Von = (0.7 V)
-
+
Von = (0.7 V)
For what input voltages is the diode forward biased?
Vin - (0.7 V) - Vout - (0.7 V) = 0
Vout = Vin - (1.4 V)
Vin ≥ (1.4 V)

## Slide 27: Find the Transfer Characteristics of this Circuit
+
-
Vin
R
-
+
Vout
Vout
Vin
1.4 V

## Slide 28: What we studied today
Small signal response of diodes
Large signal response of diodes
Transfer characteristics
Solving diode circuits with varying inputs

## Slide 30: Practice 1: Find the ac voltage across the diode if the input voltage VAC is 100 mV sin(ω t)
+
-
VDC = 6.7 V
R1 = 8 kΩ
VD
Vout = VQ + vac
-
VAC
ac component of output voltage
DC component of output voltage
+

## Slide 31: Practice Problem 2 a) Find the transfer characteristic of the following circuit
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Practice Problem 2 b) Find the current through the diode and the output voltage when the input is 6.3 volts
Practice Problem 2 c) Find the current through the diode and the output voltage when the input is -2.0 volts

## Slide 32: Practice Problem 3 a) Find the transfer characteristic of the following circuit
Practice Problem 3 b) Find the current through the diode and the output voltage when the input is 5.0 volts
Practice Problem 3 c) Find the current through the diode and the output voltage when the input is -2.0 volts
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ

## Slide 33: Practice Problem 4 a: Find the transfer characteristic of the following circuit
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
Practice Problem 4 b) Find the current through the diode and the output voltage when the input is 5.0 volts
Practice Problem 4 c) Find the current through the diode and the output voltage when the input is -4.5 volts