## Slide 1: Analog Electronics Technology
Practice Problems: Solving diode circuits with varying inputs

## Slide 3: Practice 1: Find the ac voltage across the diode if the input voltage VAC is 100 mV sin(ω t)
+
-
VDC = 6.7 V
R1 = 8 kΩ
VD
Vout = VQ + vac
-
VAC
ac component of output voltage
DC component of output voltage
+

## Slide 4: Practice 1: Find the ac voltage across the diode if the input voltage VAC is 100 mV sin(ω t)
First find the quiescent current
+
-
VDC = 6.7 V
R1 = 8 kΩ
VD
-
VAC
+
The diode is forward biased
Set VAC to 0
Use the semi-ideal model and replace the diode with a voltage source

## Slide 5: Practice 1: Find the ac voltage across the diode if the input voltage VAC is 100 mV sin(ω t)
Use KVL
VDC = 6.7 V
R1 = 8 kΩ
VD
-
+
6 V = I * 8 kΩ
+
-
0.7 V
I= 0.75 mA
Calculate the ac resistance of the diode
rAC = VT / IQ = 0.026 v /0.75 mA = 35 Ω

## Slide 6: Practice 1: Find the ac voltage across the diode if the input voltage VAC is 100 mV sin(ω t)
Now do the AC small signal analysis
+
-
R1 = 8 kΩ
VD
-
VAC
+
Use the voltage divider rule
Vout = 100 mV sin(ω t) * 35 Ω / 8035 Ω
RAC = 35 Ω
Vout = 0.44 mV sin(ω t)

## Slide 8: Practice Problem 2 a) Find the transfer characteristic of the following circuit
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Assume that the diode is forward biased
Use KVL
Vin – ID * 10 kΩ – 0.7 V – ID * 10 kΩ + 4.4 V = 0
Vin + 3.7 V – ID * 20 kΩ = 0
ID = (Vin + 3.7 V )/ 20 kΩ
ID = (Vin / 20 kΩ + 185 μA )

## Slide 9: Practice Problem 2 a) Find the transfer characteristic of the following circuit
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Find the output voltage
Vout = – 4.4 V + ID * 10 kΩ
Vout = – 4.4 V + Vin / 2 + 1.85 V
Vout = – 2.55 V + Vin / 2

## Slide 10: Practice Problem 2 a) Find the transfer characteristic of the following circuit
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Assume that the diode is just barely turned on
Idiode ≈ 0
The voltage drops across the resistors are negligible.
Vin = – 4.4 V + 0.7 V = -3.7 V
Find the range of input voltages for forward bias.
Forward bias for:
Vin ≥ -3.7 V

## Slide 11: Practice Problem 2 a) Find the transfer characteristic of the following circuit
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Now look at the output voltage when the diode is off.
Vout = – 4.4 V
No current flows, so there is no voltage drop across the resistor
Vout
Vin
-3.7 V
5.1 V
-4.4 V

## Slide 12
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Practice Problem 2 b) Find the current through the diode and the output voltage when the input is 6.3 volts
Vout = – 2.55 V + Vin / 2
This is in the range of inputs where the diode is conducting
Vout = – 2.55 V + 6.3 / 2
Vout = 0.6 V
ID = (0.6 V – (-4.4 V) ) / 10 kΩ
ID = 0.5 mA

## Slide 13
Vout
Vin
ID
10 kΩ
10 kΩ
-4.4 V
Practice Problem 2 c) Find the current through the diode and the output voltage when the input is -2.0 volts
Vout = – 2.55 V + Vin / 2
This is in the range of inputs where the diode is conducting
Vout = – 2.55 V + (-2.0 V) / 2
Vout = -3.55 V
ID = (-3.55 V – (-4.4 V) ) / 10 kΩ
ID = 0.085 mA

## Slide 15: Practice Problem 3 a) Find the transfer characteristic of the following circuit
Practice Problem 3 b) Find the current through the diode and the output voltage when the input is 5.0 volts
Practice Problem 3 c) Find the current through the diode and the output voltage when the input is -2.0 volts
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ

## Slide 16: Practice Problem 3 a) Find the transfer characteristic of the following circuit
Assume that the diode is forward biased
Use KVL
Vout = – 3 V + 0.7 V = – 2.3 V
ID = I1 – I2 = (Vin)/ 2 kΩ + 0.80 mA
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ
I1
I2
I1 = (Vin - Vout )/ 2 kΩ = (Vin )/ 2 kΩ + 1.15 mA
I2 = (Vout + 3 V )/ 2 kΩ = 0.35 mA
Find the input voltage at which the diode turns off

## Slide 17: Practice Problem 3 a) Find the transfer characteristic of the following circuit
In order for the diode to be on, the output must be – 2.3 V
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ
I1
I2
Then I2 = 0.35 mA
Therefore the voltage drop across the upper resistor must also equal one diode drop (0.7 V)
That current must also travel through I1
Vin = Vout + 0.7 V = – 1.6 V
Vin ≥ – 1.6 V when the diode is on

## Slide 18: Practice Problem 3 a) Find the transfer characteristic of the following circuit
If the diode is off, we can remove it from the circuit
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ
I1
I2
Then Vout = (Vin – 3 V)/2 = (Vin)/2 – 1.5 V
Vout
Vin
-1.6 V
-2.3 V

## Slide 19: Practice Problem 3 b) Find the current through the diode and the output voltage when the input is 5.0 volts
The diode is on; the output must be – 2.3 V
Then I2 = 0.35 mA
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ
I1
I2
ID = I1 – I2 = (Vin)/ 2 kΩ + 0.80 mA
ID = (5.0 V)/ 2 kΩ + 0.80 mA = 3.3 mA

## Slide 20: Practice Problem 3 c) Find the current through the diode and the output voltage when the input is -2.0 volts
Vout
Vin
ID
2 kΩ
-3 V
2 kΩ
I1
I2
The diode is off; the diode current equals zero
Vout = (Vin)/2 – 1.5 V = (–2 V)/2 – 1.5 V
Vout = – 2.5 V

## Slide 22: Practice Problem 4 a: Find the transfer characteristic of the following circuit
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
Practice Problem 4 b) Find the current through the diode and the output voltage when the input is 5.0 volts
Practice Problem 4 c) Find the current through the diode and the output voltage when the input is -4.5 volts

## Slide 23: Practice Problem 4 a: Find the transfer characteristic of the following circuit
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
For input voltages near zero, the diode will be reverse biased.
For the diode to be on, the input voltage will definitely need to be less than -5.7 volts (the output voltage will be -5.7 volts)
Initially we will assume that the diode is off

## Slide 24: Practice Problem 4 a: Find the transfer characteristic of the following circuit
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
Remove the diode from the circuit.
Since the diode is off, I1 = I2
I1 = (Vin - (-5V) )/22 kΩ
I1
I2
I1 = (Vin )/22 kΩ + 227 μA
Vout = -5 V + I2 * 2 kΩ
= -5 V + (Vin )/11 + 454 mV
= -4.546 V + (Vin )/11

## Slide 25: Practice Problem 4 a: Find the transfer characteristic of the following circuit
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
The diode turns off when the output voltage is -5.7 V
I1
I2
Vout = -5.7 V = -4.546 V + (Vin )/11
Vin = (-5.7 V + 4.546 V ) * 11
Vin = -12.7 V
The diode is off for Vin ≥ -12.7 V

## Slide 26: Practice Problem 4 a: Find the transfer characteristic of the following circuit
When the diode is on, the output voltage is -5.7 V
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
I1
I2
Vout
Vin
-12.7 V
-5.7 V
-4.546 V

## Slide 28: Practice Problem 4 b) Find the current through the diode and the output voltage when the input is 5.0 volts
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
I1
I2
The diode is off, ID = 0
Vout = -4.546 V + (Vin )/11
Vout = -4.09 V

## Slide 29: Practice Problem 4 c) Find the current through the diode and the output voltage when the input is -4.5 volts
Vout
Vin
ID
20 kΩ
-5 V
2 kΩ
I1
I2
The diode is off, ID = 0
Vout = -4.546 V + (Vin )/11
Vout = -4.955 V