## Slide 1: Analog Electronics Technology
Solving diode circuits with varying inputs

## Slide 2: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Circuits with varying inputs
Transfer characteristics of circuits with multiple diodes
Standard diode application circuits

## Slide 3: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Find transfer characteristics
D1
D2

## Slide 4: Circuits with multiple diodes and an unknown input
The circuit needs to be solved for each possible combination of diode states
For two diodes:
Diode 1 State | Diode 2 State | Input Conditions | Output
off | off |  | 
off | on |  | 
on | off |  | 
on | on |  | 
+
-
Vin
R
-
+
Vout
In general, for N diodes, there are 2N possible combinations of diodes being on or off together

## Slide 5: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Find transfer characteristics
D1
D2

## Slide 6: Circuits with multiple diodes and an unknown input
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
D1
D2
+
-
Vin
+
-
5 V
+
-
5 V

## Slide 7: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Assume D1 is cut off (reverse biased)
D1
D2
A
We can remove it
Can D2 also be cut off?
No!

## Slide 8: Circuits with multiple diodes and an unknown input
The circuit needs to be solved for each possible combination of diode states
For two diodes:
Diode 1 State | Diode 2 State | Input Conditions | Output
off | off |  | 
off | on |  | 
on | off |  | 
on | on |  | 

## Slide 9: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Assume D1 is cut off (not conducting)
D1
D2
A
I = 9.3 V / 8 kΩ = 1.16 mA
Vout = 5 V – (6 kΩ) ( 1.16 mA) = - 1.975 V
Calculate current
Calculate output voltage
We can remove it
Can D2 also be cut off?
No!
Replace D2 with voltage source
-
+
Von = (0.7 V)
5 V - 6 kΩ * I – 0.7 V - 2 kΩ * I + 5 V = 0
9.3 V - 8 kΩ * I = 0
Now we need to calculate the input range that causes D1 to be cut off (not conducting)

## Slide 10: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Assume D1 is cut off (not conducting)
D1
D2
A
I = 9.3 V / 8 kΩ = 1.16 mA
Vout = - 1.975 V
VA = Vout – 0.7 V = - 2.675 V
Vin < - 1.975 V
Calculate current
Calculate output voltage
Calculate voltage at node A
Calculate voltage range for input voltage
We can remove it
Can D2 also be cut off?
No!
Replace D2 with voltage source
-
+
Von = (0.7 V)

## Slide 11: Circuits with multiple diodes and an unknown input
The circuit needs to be solved for each possible combination of diode states
For two diodes:
Diode 1 State | Diode 2 State | Input Conditions | Output
off | off |  | 
off | on | Vin < - 1.975 V | Vout = - 1.975 V
on | off |  | 
on | on |  | 

## Slide 12: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Assume D2 is cut off
D1
D2
A
Vout = 5 V
Vin >= 5 V
Calculate output voltage
Calculate voltage range for input voltage
Calculate voltage range for node A
VA >= 4.3 V
Remove it from the circuit
No current through R1
There is a voltage drop across R2
D1 must be forward biased
-
+
Von = (0.7 V)

## Slide 13: Circuits with multiple diodes and an unknown input
The circuit needs to be solved for each possible combination of diode states
For two diodes:
Diode 1 State | Diode 2 State | Input Conditions | Output
off | off |  | 
off | on | Vin < - 1.975 V | Vout = - 1.975 V
on | off | Vin >= 5 V | Vout = 5 V
on | on |  | 

## Slide 14: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
Assume both diodes are conducting
D1
D2
A
VA = Vin – 0.7 V
Calculate output voltage
Calculate voltage range for input voltage
Calculate voltage for node A
Vout = Vin
- 1.975 V <= Vin <= 5 V
-
+
Von = (0.7 V)
-
+
Von = (0.7 V)

## Slide 15: Circuits with multiple diodes and an unknown input
The circuit needs to be solved for each possible combination of diode states
For two diodes:
Diode 1 State | Diode 2 State | Input Conditions | Output
off | off |  | 
off | on | Vin < - 1.975 V | Vout = - 1.975 V
on | off | Vin >= 5 V | Vout = 5 V
on | on | - 1.975 V <= Vin <= 5 V | Vout = Vin

## Slide 16: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
With the transfer characteristics we can easily solve for different inputs
D1
D2
A
What are the currents through the diodes when Vin = 1 V?
Vin
5 V
Vout
5 V
-1.975 V
-1.975 V
Vout = 1 V
ID2 = IR1 = ( 5 V - 1 V)/ 6 kΩ = 0.67 mA
VA = 0.3 V
IR2 = ( 0.3 V – (-5 V) )/ 2 kΩ = 2.65 mA
ID1 = IR2 - ID2 = 2.65 mA - 0.67 mA = 1.98 mA

## Slide 17: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
D1
D2
A
What are the currents through the diodes when Vin = - 1 V?
Vin
5 V
Vout
5 V
-1.975 V
-1.975 V
Vout = -1 V
ID2 = IR1 = ( 5 V – (- 1 V))/ 6 kΩ = 1 mA
VA = -1.7 V
IR2 = ( -1.7 V – (-5 V) )/ 2 kΩ = 1.65 mA
ID1 = IR2 - ID2 = 1.65 mA - 1 mA = 0.65 mA

## Slide 18: Circuits with multiple diodes and an unknown input
Vin
R2 = 2 kΩ
-5 V
+5 V
R1 = 6 kΩ
Vout
All voltages relative to ground
D1
D2
A
What are the currents through the diodes when Vin = - 3 V?
Vin
5 V
Vout
5 V
-1.975 V
-1.975 V
Vout = -1.975 V
ID2 = IR1 = ( 5 V – (- 1.975 V))/ 6 kΩ = 1.1625 mA
VA = -2.675 V
IR2 = ( - 2.675 V – (-5 V) )/ 2 kΩ = 1.1625 mA
ID1 = IR2 - ID2 = 1.1625 mA - 1.1625 mA = 0 mA
Reverse biased

## Slide 19
Practice Problems

## Slide 20: Practice Problem 1: Find the value of the unknown resistor that makes the current through that resistor ½ of the current through the 8 Ohm resistor.
+
-
Vin = 18.1 V
R = 8 Ω
ID
R = ??

## Slide 21: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
Practice Problem 2 b) Find the current through the diodes and the output voltage when the input is 5.0 volts
Practice Problem 2 c) Find the current through the diode and the output voltage when the input is 1.0 volts
-
+
Vout