## Slide 1: Analog Electronics Technology
Circuits with Multiple Diodes
Solutions to Practice Problems

## Slide 2: Practice Problem 1: Find the value of the unknown resistor that makes the current through that resistor ½ of the current through the 8 Ohm resistor.
+
-
Vin = 18.1 V
R = 8 Ω
ID
R = ??
All diodes will be on
I1
I2
I3
How do we know that??
Assume all diodes are off
No currents flow
No voltage drops
A
B
C
D
VBC = 18.1 V
The two diodes between B and C must be on

## Slide 3: Practice Problem 1: Find the value of the unknown resistor that makes the current through that resistor ½ of the current through the 8 Ohm resistor.
+
-
Vin = 18.1 V
R = 8 Ω
ID
R = ??
All diodes will be on
I1
I2
I3
Currents do flow
KCL at node C
A
B
C
D
I1 = I2 + I3
The two diodes between B and C must be on
I1 = I1/2 + I3
I3 = I1/2
Since current flows through the diode, it is on

## Slide 4: Practice Problem 1: Find the value of the unknown resistor that makes the current through that resistor ½ of the current through the 8 Ohm resistor.
+
-
Vin = 18.1 V
R = 8 Ω
ID
R = ??
All diodes will be on
I1
I2
I3
A
B
C
D
Replace the diodes with voltage sources
+
-
0.7 V
+
-
0.7 V
+
-
0.7 V
Apply KVL around the outer loop
18.1 V – I1 * 8 Ω – 0.7 V – 0.7 V – 0.7 V =0
I1 = 16 V / 8 Ω = 2 A

## Slide 5: Practice Problem 1: Find the value of the unknown resistor that makes the current through that resistor ½ of the current through the 8 Ohm resistor.
+
-
Vin = 18.1 V
R = 8 Ω
ID
R = ??
I1
I2
I3
A
B
C
D
+
-
0.7 V
+
-
0.7 V
+
-
0.7 V
I2 = I1 / 2 = 1 A
Ohm’s Law
0.7 V = 1 A * R
R = 0.7 Ω

## Slide 7: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
Practice Problem 2 b) Find the current through the diodes and the output voltage when the input is 5.0 volts
Practice Problem 2 c) Find the current through the diode and the output voltage when the input is 1.0 volts
-
+
Vout

## Slide 8: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Diode 1 State | Diode 2 State | Diode 3 State | Input Conditions | Output
off | off | off |  | 
on | off | off |  | 
off | on | off |  | 
on | on | off |  | 
off | off | on |  | 
on | off | on |  | 
off | on | on |  | 
on | on | on |  | 
0 V
Vin < 0.7 V

## Slide 9: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Diode 1 State | Diode 2 State | Diode 3 State | Input Conditions | Output
off | off | off |  | 
on | off | off |  | 
off | on | off |  | 
on | on | off |  | 
off | off | on |  | 
on | off | on |  | 
off | on | on |  | 
on | on | on |  | 
0 V
Vin < 0.7 V

## Slide 10: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Replace diode 3 with a voltage source
+
-
0.7 V
Apply KVL around the loop
Vin – I * 1 kΩ – 0.7 V – I * 4 kΩ = 0
Vin – 0.7 V = I * ( 1 kΩ + 4 kΩ)
I = (Vin – 0.7 V) / ( 5 kΩ)
Vout = I * ( 4 kΩ) = (Vin – 0.7 V) *4 / 5

## Slide 11: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
+
-
0.7 V
Vout = (Vin – 0.7 V) *4 / 5
For what values of Vin will D1 and D2 be off while D3 is on?
If D1 and D2 are off there is no current flow through the 2 kΩ resistor and no voltage drop across it.
A
B
VAB = Vout + 0.7 V
1.4 V = Vout + 0.7 V
Vout = 0.7 V
When D1 and D2 turn on:

## Slide 12: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
+
-
0.7 V
0.7 V = (Vin – 0.7 V) *4 / 5
A
B
1.575 V > Vin ≥ 0.7 V
0.7 V = Vin *4 / 5 – 0.7 V *4 / 5
0.7 V *9 / 5 = Vin *4 / 5
Vin = 0.7 V *9 / 4 = 1.575 V
when D1 and D2 turn on
It also should be now evident that diodes 1 and 2 will never be on unless diode 3 is already on.

## Slide 13: Practice Problem 2: Find the transfer characteristics for the following circuit.
Diode 1 State | Diode 2 State | Diode 3 State | Input Conditions | Output
off | off | off |  | 
on | off | off |  | 
off | on | off |  | 
on | on | off |  | 
off | off | on |  | 
on | off | on |  | 
off | on | on |  | 
on | on | on |  | 
0 V
Vin < 0.7 V
1.575 V > Vin ≥ 0.7 V
(Vin – 0.7 V) *4 / 5
Vin ≥ 1.575 V

## Slide 14: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Replace all diodes with voltage sources
+
-
0.7 V
Use mesh currents to write equations
+
-
0.7 V
+
-
0.7 V
I1
I2
Vin – I1 * 1 kΩ – 0.7 V – 0.7 V – (I1 – I2 )* 2 kΩ = 0
I1 * 3 kΩ – I2 * 2 kΩ = Vin – 1.4 V
– (I2 – I1 )* 2 kΩ + 0.7 V + 0.7 V – 0.7 V – I2 * 4 kΩ = 0
-I1 * 2 kΩ + I2 * 6 kΩ = 0.7 V
Loop 1:
Loop 2:

## Slide 15: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
+
-
0.7 V
+
-
0.7 V
+
-
0.7 V
I1
I2
I1 * 3 kΩ – I2 * 2 kΩ = Vin – 1.4 V
-I1 * 2 kΩ + I2 * 6 kΩ = 0.7 V
We want to eliminate I1 and get I2 in terms of Vin
I1 * 2 kΩ = I2 * 6 kΩ – 0.7 V
I1 = I2 * 3 – 0.7 V / 2 kΩ
I1 = I2 * 3 – 0.35 mA
Loop 1:
Loop 2:
rearrange
Solve for I1

## Slide 16: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
+
-
0.7 V
+
-
0.7 V
+
-
0.7 V
I1
I2
( I2 * 3 – 0.35 mA)* 3 kΩ – I2 * 2 kΩ = Vin – 1.4 V
Solve for I2 in terms of Vin
I2 * 9 kΩ – I2 * 2 kΩ = Vin – 1.4 V + 0.35 mA * 3 kΩ
I2 * 7 kΩ = Vin – 1.4 V + 1.05 V
I2 * 7 kΩ = Vin – 0.35 V
I2 = (Vin – 0.35 V )/ 7 kΩ
Vout = I2 * 4 kΩ
Vout = (Vin – 0.35 V ) * 4 kΩ / 7 kΩ
Vout = Vin * 4 / 7 – 0.20 V
I1

## Slide 17: Practice Problem 2: Find the transfer characteristics for the following circuit.
Diode 1 State | Diode 2 State | Diode 3 State | Input Conditions | Output
off | off | off |  | 
on | off | off |  | 
off | on | off |  | 
on | on | off |  | 
off | off | on |  | 
on | off | on |  | 
off | on | on |  | 
on | on | on |  | 
0 V
Vin < 0.7 V
1.575 V > Vin ≥ 0.7 V
(Vin – 0.7 V) *4 / 5
Vin ≥ 1.575 V
Vin * 4 / 7 – 0.20 V

## Slide 18: Practice Problem 2: Find the transfer characteristics for the following circuit.
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Chart: Transfer Characteristics
| -1 | -0.9 | -0.8 | -0.70000000000000007 | -0.60000000000000009 | -0.50000000000000011 | -0.40000000000000013 | -0.30000000000000016 | -0.20000000000000015 | -0.10000000000000014 | -1.3877787807814457E-16 | 9.9999999999999867E-2 | 0.19999999999999987 | 0.29999999999999988 | 0.39999999999999991 | 0.49999999999999989 | 0.59999999999999987 | 0.69999999999999984 | 0.79999999999999982 | 0.8999999999999998 | 0.99999999999999978 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -8.8818e-17 | 0.08 | 0.16 | 0.24 | 0.32 | 0.4 | 0.48 | 0.56 | 0.64 | 0.71429 | 0.77143 | 0.82857 | 0.88571 | 0.94286 | 1 | 1.0571 | 1.1143 | 1.1714 | 1.2286 | 1.2857 | 1.3429 | 1.4 | 1.4571 | 1.5143 | 1.5714 | 1.6286 | 1.6857 | 1.7429 | 1.8 | 1.8571 | 1.9143 | 1.9714 | 2.0286 | 2.0857

## Slide 19: Practice Problem 2 b) Find the current through the diodes and the output voltage when the input is 5.0 volts
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Vout = Vin * 4 / 7 – 0.20 V
Vout = 2.66 V
All diodes are on
ID3 = 2.66 V / 4 kΩ = 665 μ A
ID1 = ID2 = (2.66 V -0.7 V)/ 2 kΩ = 980 μ A
Diode 1 | Diode 2 | Diode 3 | Input Conditions | Output
off | off | off | Vin < 0.7 V | 0 V
off | off | on | 1.575 V > Vin ≥ 0.7 V | (Vin – 0.7 V) *4 / 5
on | on | on | Vin ≥ 1.575 V | Vin * 4 / 7 – 0.20 V

## Slide 20: Practice Problem 2 c) Find the current through the diode and the output voltage when the input is 1.0 volts
+
-
Vin
R = 1 kΩ
D1
R = 2 kΩ
R = 4 kΩ
D2
D3
-
+
Vout
Diodes D1 and D2 are off
Diode D3 is on
Vout = (Vin – 0.7 V) *4 / 5
Vout = 0.24 V
ID3 = 0.24 V / 4 kΩ
ID3 = 60 μ A
ID1 = ID2 = 0
Diode 1 | Diode 2 | Diode 3 | Input Conditions | Output
off | off | off | Vin < 0.7 V | 0 V
off | off | on | 1.575 V > Vin ≥ 0.7 V | (Vin – 0.7 V) *4 / 5
on | on | on | Vin ≥ 1.575 V | Vin * 4 / 7 – 0.20 V