## Slide 1: Analog Electronics Technology
Transfer Characteristics of Circuits with Multiple Diodes

## Slide 2: Analog Electronics Technology
Diodes
Semiconductor basics
Diode electrical characteristics
Solving diode circuits
Diode Models
Solving simple circuits using diode models
Solving more complex circuits
Circuits with varying inputs
Transfer characteristics of circuits with multiple diodes
Standard diode application circuits

## Slide 3: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
Vin

## Slide 4: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I3
Vin

## Slide 5: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
Assume no output current
Applying Kirchhoff’s Current Law:
I2 flows through D2
Current through R3 equals I1 + I2

## Slide 6: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
Assume diode 1 is off
Can diode 2 also be off at the same time?
Calculate I2
I2 = 9.3 V / 8 kΩ = 1.16 mA
Calculate Vout
Vout = 10 V - 1.16 mA * 6 kΩ = 3.025 V
Calculate VC
VC = 2.325 V
C
Calculate range for Vin
Vin <= 3.025 V
No
-
+
Von = (0.7 V)

## Slide 7: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
Assume diode 2 is off
Calculate Vout
Vout = 10 V
Calculate range for VC
VC >= 9.3 V
C
Calculate range for I3 (current through R3)
I3 >= 9.3 V / 2 k Ω = 4.65 mA
Calculate minimum voltage drop across 4 k Ω resistor
V4 >= 4.65 mA * 4 k Ω = 18.6 V
Calculate range for Vin
Vin >= 9.3 V + 18.6 V + 0.7V
Vin >= 28.6 V
Vin >= VC + V4 + VON
Diode 1 is on

## Slide 8: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
Assume both diodes are on
KVL around loop
Vin – 0.7 V – 4 kΩ * I1 – 2 kΩ (I1 + I2) = 0
C
Vin – 0.7 V – 6 kΩ * I1 – 2 kΩ * I2 = 0

## Slide 9: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
Assume both diodes are on
KVL around this loop
10 V – 0.7 V – 6 kΩ * I2 – 2 kΩ (I1 + I2) = 0
C
9.3V – 2 kΩ * I1 – 8 kΩ * I2 = 0
Multiply by 3
27.9V – 6 kΩ * I1 – 24 kΩ * I2 = 0

## Slide 10: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
Assume both diodes are on
C
From before
Subtract second equation from the first
28.6 V –Vin – 22 kΩ * I2 = 0
28.6 V –Vin = 22 kΩ * I2
I2 = 1.3 mA –Vin / 22 kΩ
Calculate Vout
Vout = 10 V – 6 kΩ * I2 = 10 V – 7.8 V + 3/11 Vin
Vout = 2.2 V + 3/11 Vin
27.9V – 6 kΩ * I1 – 24 kΩ * I2 = 0
Vin – 0.7 V – 6 kΩ * I1 – 2 kΩ * I2 = 0

## Slide 11: Multiple diode circuits with unknown input
R3 = 2 kΩ
0 V
+10 V
R2 = 6 kΩ
Vout
All voltages relative to ground
Find the transfer characteristics
D1
D2
R1 = 4 kΩ
I1
I2
I1 + I2
Vin
C
Chart: Transfer Characteristics

## Slide 12: Multiple diode circuits with unknown input
The circuit needs to be solved for each possible combination of diode states
For two diodes:
Diode 1 State | Diode 2 State | Input Conditions | Output
off | off |  | 
off | on |  | 
on | off |  | 
on | on |  | 
2.2 V + 3/11 Vin
Vin >= 28.6 V
10 V
3.025 V
Vin <= 3.025 V
3.025 V <= Vin <= 28.6 V