## Slide 1: Analog Electronics Technology
Lab 2
Clipper and Clamper Circuits

## Slide 2: Clipper Circuits Theory
+
-
Vin
R
Vout
-
+
Vb
Find the transfer characteristics of this circuit
If the diode is reverse biased, what is the output?
What input voltages cause the diode to be off?
Vout = Vin
Vin < Vb + 0.7 V
If the diode is forward biased, what is the output?
Vout = Vb + 0.7 V
What input voltages cause the diode to be forward biased?
Vin ≥ Vb + 0.7 V
There is no current through the resistor
Von
Remove from circuit

## Slide 3: Clipper Circuits
+
-
Vin
R
Vout
-
+
Vb
Find the transfer characteristics of this circuit
Vout
Vin
Vout = Vin
Vout = Vb + 0.7 V
Vb + 0.7 V

## Slide 4: Clipper Circuits
+
-
Vin
R
Vout
-
+
Vb = 3.3 V
Vout
Vin
Vout = Vin
Vout = Vb + 0.7 V
Vb + 0.7 V
Chart: Input voltage
Chart: Output Voltage
Vb + Von

## Slide 5: Clipper Circuits
+
-
Vin
R
Vout
-
+
Vb = 2.6 V
With battery polarity reversed, clipping occurs at –Vb + 0.7
Vout
Vin
Chart: Output Voltage
Chart: Input voltage

## Slide 6: Clipper Circuits
+
-
Vin
R
Vout
-
+
Vb
What happens if we reverse the direction of the diode?
Vout
Vin
If the diode is reverse biased, what is the output?
What input voltages cause the diode to be reverse biased?
Vout = Vin
Vin > Vb - 0.7 V
If the diode is forward biased, what is the output?
Vout = Vb - 0.7 V
What input voltages cause the diode to be forward biased?
Vin ≤ Vb - 0.7 V

## Slide 7: Clipper Circuits
+
-
Vin
R
Vout
-
+
Vb=1.9 V
What happens if we reverse the direction of the diode?
Vout
Vin
Chart: Input voltage
Chart: Output Voltage
Vb - Von

## Slide 8: Clipper Circuits
+
-
Vin
R
Vout
-
+
Vb
Find the transfer characteristics of this circuit
Vout
Vin
With battery polarity reversed, clipping occurs at –Vb - 0.7
Chart: Output Voltage
Chart: Input voltage

## Slide 9: Clipper Circuit
+
-
Vin
R = 1 kΩ
Vout
-
+
Vb
Figure 1. Clipper Circuit
Function Generator
DC Adjustable Voltage Power Supply
Chart: Output Voltage
Chart: Output Voltage
DC Voltages
5 V
4 V
2 V
0 V
-1 V
-2 V
-4 V
-5 V
Sine wave 6V mag
Vout
Vin
Vout = Vin
Vout = Vb + 0.7 V
Vb + 0.7 V

## Slide 10: Clipper Circuit
Vout
-
+
+
-
Vin
R = 1 kΩ
Vb
Figure 1. Clipper Circuit
Function Generator
DC Adjustable Voltage Power Supply
DC Voltages
5 V
4 V
2 V
0 V
-1 V
-2 V
-4 V
-5 V
Sine wave 6V mag
Chart: Output Voltage
Chart: Output Voltage
Reverse Diode
Vout
Vin

## Slide 11: Lab 2 Part 2
Clamper Circuits

## Slide 12: Clamper Circuits
Clamper circuits shift the DC value of a waveform.
Chart: time
+
-
Vin
C
Vout
-
+
Vb
VC
+
-
Vin - VC - Vout = 0
Vout = Vin - VC
Vout = Von + Vb
If the diode is conducting
Assume that Vb is positive, and the capacitor is initially discharged
The diode will be initially reverse biased
Vout = Vin
The voltage across the diode is Vin – Vb
Vin = Von + Vb
The diode will start conducting when

## Slide 13: Clamper Circuits
Clamper circuits shift the DC value of a waveform.
Chart: time
+
-
Vin
C
Vout
-
+
Vb
VC
+
-
Vin - VC - Vout = 0
Vout = Vin - VC
Vout = Von + Vb
If the diode is conducting
When the diode conducts the capacitor will start charging
Calculate the voltage on the capacitor when the input is at the maximum value
When the input voltage starts decreasing, the diode stops conducting and the charge is trapped on the capacitor
The diode never again conducts
Vin - VC = Von + Vb
VC = Vin - Von - Vb
VC,max = Vin,max - Von - Vb
VC = VC,max
Vout = Vin – VC,max
Vout = Vin – Vin,max + Von + Vb
Input reaches maximum

## Slide 14: Clamper Circuits
Clamper circuits shift the DC value of a waveform.
+
-
Vin
C
Vout
-
+
Vb
VC
+
-
Vout = Vin – Vin,max + Von + Vb
Chart: Time
Chart: Time
Vb + Von

## Slide 15: Clamper Circuits
+
-
Vin
C = 1 μF
Vout
-
+
Vb
VC
+
-
Record the steady state input and output waveforms for at least two positive values and two negative values of Vb
Function Generator
DC Adjustable Voltage Power Supply
Set to sine wave 6V magnitude 1 Hz
Reverse the diode and repeat the measurements
R= 1 kΩ
Set Vb to 2 V
Turn off signal generator
Use resistor to discharge capacitor
Manually trigger the oscilloscope to capture the input and immediately turn on the signal generator
Hopefully, the captured waveform will show the startup voltage and the changeover to steady state