## Slide 1: Analog Electronics Technology
BJT operation

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
BJT basics
Common Emitter Amplifier Circuits
Voltage Divider Biasing
Degenerate Resistor
Rules of Thumb
Other Biasing Methods
Common Base & Common Collector Amplifier Circuits
Op Amps

## Slide 3: What we will talk about today
Parts of a BJT
Base, Emitter, Collector
Electrical symbols for BJTs
Regions of operation
BJT configurations
Common emitter, common base, common collector
Characteristic curves for common emitter configuration
Underlying physics
Equations for BJTs
Model for the BJT

## Slide 4: PNP Bipolar Junction Transistor (BJT)
p+-type
n-type
It looks like two back to back diodes.
space charge region
space charge region
p-type
Emitter
Collector
Base
A BJT has three terminals (metal contacts)
p
p
n
n
This is a pnp bipolar junction transistor. There is also an npn bipolar junction transistor.
The small base width causes it to behave much differently.

## Slide 5: Bipolar Junction Transistor (BJT) types
This is a pnp bipolar junction transistor.
p+-type
n-type
space charge region
space charge region
p-type
Emitter
Collector
Base
n+-type
p-type
space charge region
space charge region
n-type
Emitter
Collector
Base
This is an npn bipolar junction transistor.
electrical symbol
base
emitter
collector
electrical symbol
base
emitter
collector
There is always an arrow between the emitter and the base
The arrow points in the direction of current flow

## Slide 6: What types of transistors are these? Identify the terminals.
A pnp bipolar junction transistor.
An npn bipolar junction transistor.
base
emitter
collector
base
emitter
collector
base
emitter
collector
An npn bipolar junction transistor.

## Slide 7: pnp BJT regions of operation
This is a pnp bipolar junction transistor.
p+-type
n-type
space charge region
space charge region
p-type
Emitter
Collector
Base
electrical symbol
base
emitter
collector
VEB
VCB
Active
Saturation
Cutoff
Inverted
Emitter-base junction forward biased
Emitter-base junction reverse biased
Collector-base junction reverse biased
Collector-base junction forward biased
A BJT has four regions of operation, corresponding to the four combinations of forward or reverse biasing for the p-n junctions
The normal region of operation is the active region

## Slide 8: npn BJT regions of operation
n+-type
p-type
space charge region
space charge region
n-type
Emitter
Collector
Base
This is an npn bipolar junction transistor.
electrical symbol
base
emitter
collector
VEB
VCB
Active
Saturation
Cutoff
Inverted
Emitter-base junction forward biased
Emitter-base junction reverse biased
Collector-base junction reverse biased
Collector-base junction forward biased
Here are the four regions of operation for an npn BJT
It is important to identify which type of transistor you are designing for

## Slide 9: Configurations of BJTs in circuits
common emitter
VEB
+
-
VEC
+
-
input
output
common base
input
VEB
+
-
VBC
+
-
output
common collector
VBC
+
-
VEC
+
-
input
output
They are named for the terminal that is shared by the input and the output

## Slide 10: Output characteristics of a pnp BJT in common emitter configuration
p+-type
n-type
space charge region
space charge region
p-type
Emitter
Collector
Base
base
emitter
collector
IB= 0
Inverted
IC
VEC
Increasing base current
Active
Cutoff
VCB= 0
Saturated
We choose an operating point in the active region.
A small change in base current causes a large change in collector current
Notice that in the inverted region the transistor is less responsive
This is because of different doping levels and physical geometry.
p+
p+
p+
n
n
n
n-
E
B
C
p-

## Slide 11: Note: base expanded in drawing only for ease of showing currents
The main current comes from holes injected into the forward biased diode.
Most of the holes injected from the emitter into the base diffuse across the base before they can recombine. These holes become the major part of the collector current.
Some of the holes injected from the emitter into the base recombine in the base and become a part of the base current (IB2).
p+-type
n-type
space charge region
space charge region
p-type
Emitter
Collector
Base
IE
IEp
IEn
IB1
IB2
IB
ICn
ICp
IC
What happens on a small scale (for pnp BJT)

## Slide 12: Figures of Merit of Bipolar Junction Transistors
The common base current gain (α ) is the ratio of the collector current to the emitter current.
p+-type
n-type
space charge region
space charge region
p-type
Emitter
Collector
Base
IE
IEp
IEn
IB1
IB2
IB
ICn
ICp
IC

## Slide 13: Figures of Merit of Bipolar Junction Transistors
The current gain, βdc, is the ratio of the collector current to the base current.
Values of βdc usually range between 50 and 300, but can have values outside of this range for special devices
We usually assume that βdc is constant over the entire active range, but that is not necessarily true.
p+-type
n-type
space charge region
space charge region
p-type
Emitter
Collector
Base
IE
IEp
IEn
IB1
IB2
IB
ICn
ICp
IC

## Slide 14: Equations for real pnp BJT
(We will use approximations)
IB= 0
Inverted
IC
VEC
Increasing base current
Active
Cutoff
VCB= 0
Saturated

## Slide 15: Approximations valid for forward active region only
for pnp BJTs
for npn BJTs
IB= 0
Inverted
IC
VEC
Increasing base current
Active
Cutoff
VCB= 0
Saturated

## Slide 16: More relationships valid for both pnp and npn BJTs
for active region
Our most important equations

## Slide 17: One model of BJT in forward active region – diode and dependent current source
ID
β ID
base
emitter
collector
pnp BJT
ID
β ID
base
emitter
collector
npn BJT

## Slide 18: What we talked about today
Parts of a BJT
Base, Emitter, Collector
Electrical symbols for BJTs
Regions of operation
BJT configurations
Common emitter, common base, common collector
Characteristic curves for common emitter configuration
Underlying physics
Equations for BJTs
Model for the BJT

## Slide 19
Practice Problems

## Slide 20: What types of transistors are these? Identify the terminals.

## Slide 21: What types of transistors are these? Identify the terminals.