## Slide 1: Analog Electronics Technology
BJT operation

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
BJT basics
Common Emitter Amplifier Circuits
Voltage Divider Biasing
Degenerate Resistor
Rules of Thumb
Other Biasing Methods
Common Base & Common Collector Amplifier Circuits
Op Amps

## Slide 3: What we will talk about today
Common Emitter Amplifier Circuits
DC biasing
Finding voltages and currents for common emitter amplifiers
Graphical solutions

## Slide 4
Solutions to practice problems from last time

## Slide 5: What types of transistors are these? Identify the terminals.
p
p
n
base
emitter
collector
pnp
p
n
n
base
emitter
collector
npn
p
n
n
base
emitter
collector
npn

## Slide 6: What types of transistors are these? Identify the terminals.
p
n
n
base
emitter
collector
npn
p
n
p
base
emitter
collector
pnp
n
p
p
base
emitter
collector
pnp

## Slide 7: Configurations of BJTs in circuits
common emitter
VEB
+
-
VEC
+
-
input
output
common base
input
VEB
+
-
VBC
+
-
common collector
VBC
+
-
VEC
+
-
input
output
output

## Slide 8: Common Emitter Amplifier Circuit
We can substitute the model of the BJT into the circuit.
DC bias
AC signal

## Slide 9: Common Emitter Amplifier Circuit
The average value of Vin = 0. We can remove it for DC analysis
ID
β ID
Replace the diode with a voltage source

## Slide 10: Common Emitter Amplifier Circuit
Apply Kirchhoff’s voltage law around the inner loop.
0 = - 0.7 V - ID R1 + Vbb
ID = ( Vbb - 0.7 V) / R1
β ID
Since we know that the current around the outer loop is β ID, do KVL around the outer loop
Vout - RC β ID + Vcc = 0
Vout = - Vcc + RC β ID
Vout = - Vcc + RC β ( Vbb - 0.7 V) / R1
ID

## Slide 12: Common Emitter Amplifier Circuit Example 1 DC Analysis
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and choose Rc so that Vout = 4.0 V.
= 8V
Substitute model and find IB
What type of transistor is it?

## Slide 13: Common Emitter Amplifier Circuit Example 1
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and choose Rc so that Vout = 4.0 V.
Substitute model and find IB
= 2 V
ID
β ID
We will use our semi-ideal model of the diode

## Slide 14: Common Emitter Amplifier Circuit Example 1
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and choose Rc so that Vout = 4.0 V.
= 2 V
0.7V
β ID
Calculate the base current (KVL)
IB = 1.3 V / = 13 μA
Calculate the collector current
IC = β IB = 100 * 13 μA = 1.3 mA
Find RC
8 V – 1.3 mA * RC = 4.0 V
RC = 4 V / 1.3 mA = 3.1
2.0 V - IB * – 0.7 V = 0

## Slide 15
Next is a related problem.

## Slide 16: Common Emitter Amplifier Circuit Example 2
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 8V

## Slide 17: Common Emitter Amplifier Circuit Example 2
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
Calculate the base current (KVL)
IB = 1.3 V / = 13 μA
Calculate the collector current
IC = β IB = 100 * 13 μA = 1.3 mA
2.0 V - IB * – 0.7 V = 0
= 2 V
0.7V
β ID
Same as last problem
Find the voltage drop across the collector resistor
Vdrop = IC RC = (1.3 mA) * (6.2 k ) = 8.06 V
Vout = 8 V - Vdrop = -0.06 V
The transistor is in saturation.
These equations are only good for the forward active mode.

## Slide 18: Common Emitter Amplifier Circuit Example 2
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and Vout.
= 8V
First calculate the base current
IB = 13 μA
IC = Vdrop / RC = (8 V – 0.2 V) / = 1.26 mA
Now, from the voltage drop across the collector resistor we can calculate the current.
Vout = VCE,sat = 0.2 V (since it is in saturation)

## Slide 19: Common Emitter Amplifier Circuit Design – graphical solution
Use semi-ideal diode model with load line
Chart: Diode Current-Voltage Characteristics
| -4.9999999999998795E-2 | 1.2073675392798577E-15 | 5.000000000000121E-2 | 0.10000000000000121 | 0.15000000000000122 | 0.20000000000000123 | 0.25000000000000122 | 0.30000000000000121 | 0.3500000000000012 | 0.40000000000000119 | 0.45000000000000118 | 0.50000000000000122 | 0.55000000000000127 | 0.60000000000000131 | 0.65000000000000135 | 0.7000000000000014 | 0.7010000000000014 | 0.75100000000000144
 | -8.5519e-14 | 4.6629e-27 | 5.9058e-13 | 4.6691e-12 | 3.2834e-11 | 2.2734e-10 | 1.5706e-09 | 1.0847e-08 | 7.4906e-08 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 100 | 1000

## Slide 20: Common Emitter Amplifier Circuit Example 2b
Find the load line for the base “diode”
= 8V
KVL around inner loop
Vbb - IB * R1 – Vbe = 0
Intercept
IB = Vbb / R1 - Vbe / R1
Slope = -1/R1

## Slide 21: Common Emitter Amplifier Circuit Design – graphical solution
find base (diode) current
Use semi-ideal diode model with load line
Chart: Diode Current-Voltage Characteristics
| -4.9999999999998795E-2 | 1.2073675392798577E-15 | 5.000000000000121E-2 | 0.10000000000000121 | 0.15000000000000122 | 0.20000000000000123 | 0.25000000000000122 | 0.30000000000000121 | 0.3500000000000012 | 0.40000000000000119 | 0.45000000000000118 | 0.50000000000000122 | 0.55000000000000127 | 0.60000000000000131 | 0.65000000000000135 | 0.7000000000000014 | 0.7010000000000014 | 0.75100000000000144
 | -8.5519e-14 | 4.6629e-27 | 5.9058e-13 | 4.6691e-12 | 3.2834e-11 | 2.2734e-10 | 1.5706e-09 | 1.0847e-08 | 7.4906e-08 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 100 | 1000
Vbb /R1
Vbb

## Slide 22: Common Emitter Amplifier Circuit Design – graphical solution
find base (diode) current
On transistor characteristics drawing, find curve corresponding to base current
Use semi-ideal diode model with load line
Vbb /R1
Chart: Diode Current-Voltage Characteristics
| -4.9999999999998795E-2 | 1.2073675392798577E-15 | 5.000000000000121E-2 | 0.10000000000000121 | 0.15000000000000122 | 0.20000000000000123 | 0.25000000000000122 | 0.30000000000000121 | 0.3500000000000012 | 0.40000000000000119 | 0.45000000000000118 | 0.50000000000000122 | 0.55000000000000127 | 0.60000000000000131 | 0.65000000000000135 | 0.7000000000000014 | 0.7010000000000014 | 0.75100000000000144
 | -8.5519e-14 | 4.6629e-27 | 5.9058e-13 | 4.6691e-12 | 3.2834e-11 | 2.2734e-10 | 1.5706e-09 | 1.0847e-08 | 7.4906e-08 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 100 | 1000
Vbb
IC
VCE
Find the load line from the circuit

## Slide 23: Common Emitter Amplifier Circuit Example 2b
Find the load line for the transistor
= 8V
KVL around outer loop
Vcc – IC * RC – VCE = 0
Intercept
IC = VCC / RC – VCE / RC
Slope = -1/RC
Realize that Vout is the same as VCE

## Slide 24: Common Emitter Amplifier Circuit Design – graphical solution
find base (diode) current
Use semi-ideal diode model with load line
Vbb /R1
Chart: Diode Current-Voltage Characteristics
| -4.9999999999998795E-2 | 1.2073675392798577E-15 | 5.000000000000121E-2 | 0.10000000000000121 | 0.15000000000000122 | 0.20000000000000123 | 0.25000000000000122 | 0.30000000000000121 | 0.3500000000000012 | 0.40000000000000119 | 0.45000000000000118 | 0.50000000000000122 | 0.55000000000000127 | 0.60000000000000131 | 0.65000000000000135 | 0.7000000000000014 | 0.7010000000000014 | 0.75100000000000144
 | -8.5519e-14 | 4.6629e-27 | 5.9058e-13 | 4.6691e-12 | 3.2834e-11 | 2.2734e-10 | 1.5706e-09 | 1.0847e-08 | 7.4906e-08 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 100 | 1000
Vbb
IC
VCE
Transistor is in saturation
IC = Vcc / RC - VCE / RC
Vcc /RC
slope = -1 /RC
slope = -1 /RC
intercept
Use the given value for Rc to plot the load line
Adjust Rc until the intersection of the load line and the base current curve is centered
Vcc

## Slide 25: What we talked about today
Common Emitter Amplifier Circuits
DC biasing
Finding voltages and currents for common emitter amplifiers
Graphical solutions