## Slide 1: Analog Electronics Technology
BJT operation

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
BJT basics
Common Emitter Amplifier Circuits
Voltage Divider Biasing
Degenerate Resistor
Rules of Thumb
Other Biasing Methods
Common Base & Common Collector Amplifier Circuits
Op Amps

## Slide 3: What we will talk about today
Common Emitter Amplifier Circuits
DC biasing
Finding voltages and currents for common emitter amplifiers

## Slide 4: Common Emitter Amplifier Circuit Example 3
A transistor with β = 120, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents. Choose Rc so that the output voltage is 5 V
10 V
Insert the model for the transistor

## Slide 5: Common Emitter Amplifier Circuit Example 3
A transistor with β = 120, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents. Choose Rc so that the output voltage is 5 V
10 V
ID
β ID
Insert the model for the forward biased diode
0.7 V
Apply KVL around the base loop
10.0 V – IB * 100 kΩ – 0.7 V = 0
IB = ( 10.0 V – 0.7 V) / 100 kΩ = 93 μA
= ID
IC = β ID = 120 * 93 μA
Look at collector current
IC = β ID = 11.2 mA

## Slide 6: Common Emitter Amplifier Circuit Example 3
A transistor with β = 120, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents. Choose Rc so that the output voltage is 5 V
10 V
ID
β ID
0.7 V
Apply KVL around the loop with the collector resistor
10.0 V – IC * RC – Vout = 0
Solve for the collector resistance
Vout = 10.0 V – 11.2 mA * RC
= 5 V
RC * 11.2 mA = 10 V – 5 V
RC = 5 V / 11.2 mA = 450 Ω

## Slide 8: Common Emitter Amplifier Circuit Example 4
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the resistor values so that base current is 31 μA and the output voltage is 5 V.
10 V
10.0 V – IB * RB – Von = 0
10.0 V – 31 μA * RB – 0.7 V = 0
Apply KVL around the base-emitter loop
Solve for the base resistance

## Slide 9: Common Emitter Amplifier Circuit Example 4
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the resistor values so that base current is 31 μA and the output voltage is 5 V.
10 V
IC = β IB
Vout = 10.0 V – 2.48 mA * RC
Find the collector current
Find for the collector resistance
= 80 * 31 μA
IC = 2.48 mA
= 5 V
RC = 5 V / 2.48 mA

## Slide 11: Common Emitter Amplifier Circuit Example 5
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
10 V
10 V – IB * – 0.7 V = 0
Apply KVL through the base
Solve for the base current
IB = (10 V – 0.7 V) / = 46.5 μA
Solve for the collector current
IC = β IB = 80 * 46.5 μA = 3.72 mA
Solve for the output voltage
Vout = 10 V – 3.72 mA * = 6.28 V

## Slide 12: Common Emitter Amplifier Circuit Example 5
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
10 V
Does this make sense??
= 6.28 V
It puts the transistor in the forward active region
The equations and models that we used should apply
Yes

## Slide 14: Common Emitter Amplifier Circuit Example 6
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Design the circuit so that the base current is 75 μA and the output voltage is 5 V
12.7 V
12.7 V – 75 μA * – 0.7 V = 0
Apply KVL through the base
Solve for the base resistance
RB = (12.7 V – 0.7 V) / 75 μA = 160
Solve for the collector current
IC = β IB = 100 * 75 μA = 7.5 mA
Solve for the collector resistance
5 V = 12.7 V – 7.5 mA *
= (12.7 V – 5 V) / 7.5 mA =7.7 V / 7.5 mA = 1.03

## Slide 16
Practice Problems

## Slide 17: Common Emitter Amplifier Circuit Practice Problem 1
5.7 V
10 V
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage

## Slide 18: Common Emitter Amplifier Circuit Practice Problem 2
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
10 V

## Slide 19: Common Emitter Amplifier Circuit Practice Problem 3
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
4.7 V
8V

## Slide 20: Common Emitter Amplifier Circuit Practice Problem 4
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Design the circuit so that the output voltage is 5 V and the collector current is 2 mA
10 V

## Slide 21: Common Emitter Amplifier Circuit Practice Problem 5
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
4.7 V
15V

## Slide 22: Common Emitter Amplifier Circuit Practice Problem 6
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Design the circuit so that the base current is 75 μA and the output voltage is 5 V
12.7 V

## Slide 23: Common Emitter Amplifier Circuit Practice Problem 6
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
5.7 V
10V

## Slide 24: Common Emitter Amplifier Circuit Practice Problem 7
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
8 V