## Slide 1: Analog Electronics Technology
BJT operation

## Slide 2
Practice Problems

## Slide 3: Common Emitter Amplifier Circuit Practice Problem 1
5.7 V
10 V
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
Insert the model for the BJT

## Slide 4: Common Emitter Amplifier Circuit Practice Problem 1
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
5.7 V – IB * – 0.7 V = 0
5.7 V
10 V
ID
β ID
Apply KVL through the base
Solve for the base current
IB = (5.7 V – 0.7 V) / = 25 μA
Solve for the collector current
IC = β IB = 80 * 25 μA = 2 mA
Solve for the output voltage
Vout = 10 V – 2 mA * = 6 V

## Slide 5: Common Emitter Amplifier Circuit Practice Problem 1
5.7 V
10 V
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
Does this make sense??
= 6 V
It puts the transistor in the forward active region
The equations and models that we used should apply
Yes

## Slide 7: Common Emitter Amplifier Circuit Practice Problem 2
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
10 V
Insert the model for the BJT

## Slide 8: Common Emitter Amplifier Circuit Practice Problem 2
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
10 V
ID
β ID
10 V – IB * – 0.7 V = 0
Apply KVL through the base
Solve for the base current
IB = (10 V – 0.7 V) / = 46.5 μA
Solve for the collector current
IC = β IB = 100 * 46.5 μA = 4.65 mA
Solve for the output voltage
Vout = 10 V – 4.65 mA * = 5.35 V
IC

## Slide 9: Common Emitter Amplifier Circuit Practice Problem 2
A transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
10 V
Does this make sense??
= 5.35 V
It puts the transistor in the forward active region
The equations and models that we used should apply
Yes

## Slide 11: Common Emitter Amplifier Circuit Practice Problem 3
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
4.7 V
8V
4.7 V – IB * – 0.7 V = 0
Apply KVL through the base
Solve for the base current
IB = (4.7 V – 0.7 V) / = 40 μA
Solve for the collector current
IC = β IB = 100 * 40 μA = 4 mA
Solve for the output voltage
Vout = 8 V – 4 mA * = 0 V

## Slide 12: Common Emitter Amplifier Circuit Practice Problem 3
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
4.7 V
8V
Does this make sense??
= 0 V
It puts the transistor in saturation
The equations and models that we used do not apply
No!
Vout = VCE,sat = 0.2 V
IC = (8 V - 0.2 V) /

## Slide 14: Common Emitter Amplifier Circuit Practice Problem 4
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Design the circuit so that the output voltage is 5 V and the collector current is 2 mA
10 V
10 V –2 mA* RC = 5 V
Apply KVL through the collector
Solve for the collector resistance
RC = (10 V – 5 V) / = 2.5
Solve for the base current
IC = β IB
Solve for the base resistance
RB = (10 V – 0.7 V) / 25 μA =
= 80 IB
= 25 μA

## Slide 16: Common Emitter Amplifier Circuit Practice Problem 5
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
4.7 V
15V
4.7 V – IB * – 0.7 V = 0
Apply KVL through the base
Solve for the base current
IB = (4.7 V – 0.7 V) / = 40 μA
Solve for the collector current
IC = β IB = 80 * 40 μA = 3.2 mA
Solve for the output voltage
Vout = 15 V – 3.2 mA * = 2.2 V

## Slide 17: Common Emitter Amplifier Circuit Practice Problem 5
An npn transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
4.7 V
15V
Does this make sense??
= 2.2 V
It puts the transistor in the forward active region
The equations and models that we used should apply
Yes
It would be better to design the circuit so that it was farther from saturation

## Slide 19: Common Emitter Amplifier Circuit Practice Problem 6
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
5.7 V
10V
5.7 V – IB * – 0.7 V = 0
Apply KVL through the base
Solve for the base current
IB = (5.7 V – 0.7 V) / = 50 μA
Solve for the collector current
IC = β IB = 100 * 50 μA = 5 mA
Solve for the output voltage
Vout = 10 V – 5 mA * = -10 V
The transistor is in saturation!

## Slide 20: Common Emitter Amplifier Circuit Practice Problem 6
An npn transistor with β = 100, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
5.7 V
10V
Solve for the collector current
IC = (10 V – 0.2 V ) / = 2.45 mA
The output voltage is 0.2 V
If we wanted the transistor to be in the active region and the output to be near mid-range, we could change the collector resistor to 1 k
Vout = 10 V – 5 mA * = 5 V

## Slide 22: Common Emitter Amplifier Circuit Practice Problem 7
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
8 V
8 V – IB * – 0.7 V = 0
Apply KVL through the base
Solve for the base current
IB = (8 V – 0.7 V) / = 36.5 μA
Solve for the collector current
IC = β IB = 80 * 36.5 μA = 2.92 mA
Solve for the output voltage
Vout = 8 V – 2.92 mA * = 2.16 V

## Slide 23: Common Emitter Amplifier Circuit Practice Problem 7
A transistor with β = 80, VBE,on = 0.7 V, VCE,sat = 0.2 V is biased as shown. Find the DC currents and the output voltage
8 V
Does this make sense??
= 2.16 V
It puts the transistor in the forward active region
The equations and models that we used should apply
Yes
It perhaps could be designed so that it was a bit farther from saturation