## Slide 1: Analog Electronics Technology
BJT operation

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
BJT basics
Common Emitter Amplifier Circuits
Voltage Divider Biasing
Degenerate Emitter Resistor
Rules of Thumb
Other Biasing Methods
Common Base & Common Collector Amplifier Circuits
Op Amps

## Slide 3: What we will talk about today
Voltage divider biasing of Common Emitter Amplifier Circuits with degenerate emitter
Guidelines for emitter voltage
Guidelines for resistive ladder currents
Guidelines for collector voltage (output voltage)

## Slide 4: Common Emitter Amplifier Circuit – Biasing with Voltage Divider and Emitter Resistor
If β RE is too much greater than RTH the range of operation is reduced – it takes less to drive the transistor to saturation or cutoff
There are trade-offs involved
Some “rules of thumb” have been developed to help give good results without too much difficulty
Degenerate emitter

## Slide 6: Common Emitter Amplifier Circuit – Biasing with Voltage Divider and Emitter Resistor
Rule of thumb:
Make voltage VE between 10% and 33% of VCC
Rule of thumb:
Make VCE half of
(VCC - VE)
Rule of thumb:
Make current through R1 at least ten times the base current
I1 > 10 IB

## Slide 7: Common Emitter Amplifier Circuit – Biasing with Voltage Divider and Emitter Resistor
Voltages for minimum RE
Voltages for maximum RE
Leeway from cutoff
Leeway from Saturation
Leeway from cutoff
Leeway from Saturation
Less β dependence

## Slide 9: Common Emitter Amplifier Circuit – Example 4
Find values for the resistors to bias the circuit so that IC = 10 mA. The transistor has β = 200.
= 10 V
10 V
1. Choose VE
2. Calculate RE from VE and IE
IE = IC + IB
IC = β IB
IB = IC /β
IE = IC + IC /β = IC (1+ 1/β)
IE = IC (1+ β)/β
-2.0 V (Using rule of thumb)

## Slide 10: Common Emitter Amplifier Circuit – Example 4
Find values for the resistors to bias the circuit so that IC = 10 mA. The transistor has β = 200.
= 10 V
10 V
3. Use rule of thumb to set Vout
= -6.0 V

## Slide 11: Common Emitter Amplifier Circuit – Example 4
Find values for the resistors to bias the circuit so that IC = 10 mA. The transistor has β = 200.
= 10 V
10 V
4. Calculate RC from VC and IC
5. Calculate base voltage by subtracting one diode drop from VE
VB = -2.0 V - 0.7 V = -2.7 V
6. Calculate base current from collector current
IB = IC /β = 50 μA

## Slide 12: Common Emitter Amplifier Circuit – Example 4
Find values for the resistors to bias the circuit so that IC = 10 mA. The transistor has β = 200.
= 10 V
10 V
7. Use the rule of thumb, to set the current through R1
10. Calculate R2 from voltage and current
I1 = 10 IB = 500 μA
8. Calculate the value of R1 from voltage and current
9. Use KCL to calculate the current through R2

## Slide 14: Common Emitter Amplifier Circuit – Example 5
Find values for the resistors to bias the circuit so that IB = 0.1 mA.
The transistor has β = 100.
What type of transistor is it?
pnp or npn?
= 10 V
10 V
2. Using the rule of thumb,
choose a voltage for VE
3. What is the approximate current through RE ?
4. Calculate the value for RE.
Rule of thumb:
Make voltage VE between 10% and 33% of VCC
2.0 V
0.1 mA * 101 = 10.1 mA
≈10 mA
2.0 V / 10 mA = 200

## Slide 15: Common Emitter Amplifier Circuit – Example 5
Find values for the resistors to bias the circuit so that IB = 0.1 mA. The transistor has β = 100.
= 10 V
10 V
What type of transistor is it?
pnp or npn?
2. Using the rule of thumb,
choose a voltage for VE
3. What is the approximate current through RE ?
4. Calculate the value for RE.
Rule of thumb:
Make voltage VE between 10% and 33% of VCC

## Slide 16: Common Emitter Amplifier Circuit – Example 5
Find values for the resistors to bias the circuit so that IB = 0.1 mA. The transistor has β = 100.
= 10 V
10 V
5. Using the rule of thumb, what is the output voltage, Vout
7. Calculate the value for RC.
6. What is the collector current?
Rule of thumb:
Make VCE half of (VCC - VE)
6.0 V
= 100 * 0.1 mA = 10 mA
4.0 V / 10 mA = 400
IC = β IB
6.0 V

## Slide 17: Common Emitter Amplifier Circuit – Example 5
Find values for the resistors to bias the circuit so that IB = 0.1 mA. The transistor has β = 100.
= 10 V
10 V
8. What is the base voltage, VB ?
9. Using the rule of thumb, what is the current through R1?
10. What is the current through R2?
Rule of thumb:
Make current through R1 at least ten times the base current
I1 ≥ 10 IB
VB = 2.0 V + 0.7 V = 2.7 V
0.1 mA * 10 = 1. mA
=
1. mA 0.1 mA = 0.9 mA

## Slide 18: Common Emitter Amplifier Circuit – Example 5
Find values for the resistors to bias the circuit so that IB = 0.1 mA. The transistor has β = 100.
= 10 V
10 V
11. Calculate the value for R1.
12. Calculate the value for R2.
1. mA
0.9 mA
VB = 2.7 V

## Slide 20: Common Emitter Amplifier Circuit – Example 6
Find the values of the DC currents and voltages of the circuit. The transistor has β = 96.
= 10 V
10 V
Find the Thevenin equivalent resistance looking to the left from the base of the transistor
What is the Thevenin voltage?

## Slide 21: Common Emitter Amplifier Circuit – Example 6
Find the values of the DC currents and voltages of the circuit. The transistor has β = 96.
Write the KVL equation for the base-emitter loop
What is the relationship between the base current and the emitter current?
= 10 V
10 V
Substitute

## Slide 22: Common Emitter Amplifier Circuit – Example 6
Find the values of the DC currents and voltages of the circuit. The transistor has β = 96.
Calculate IE
What is the emitter voltage?
= 10 V
10 V
What is the collector current?

## Slide 23: Common Emitter Amplifier Circuit – Example 6
Find the values of the DC currents and voltages of the circuit. The transistor has β = 96.
= 10 V
10 V
What is the output voltage?
What is the base voltage?

## Slide 24: What we talked about today
Voltage divider biasing of Common Emitter Amplifier Circuits with degenerate emitter
Guidelines for emitter voltage
Guidelines for resistive ladder currents
Guidelines for collector voltage (output voltage)

## Slide 25
Practice Problems

## Slide 26: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V

## Slide 27: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V

## Slide 28: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V