## Slide 1: Analog Electronics Technology
BJT operation
Voltage Divider Bias Practice Problems

## Slide 2: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V

## Slide 3: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V
1. Calculate IE
IE = IB (β +1)
2. Choose VE
IE = 20 μA (101)
IE = 2.02 mA
VE = 4.00 V
10% = 1.50 V
33% = 5.00 V

## Slide 4: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V
3. Calculate RE
4. (2. revisited) Recalculate VE
RE = 4.00 V / 2.02 mA
Standard 5% value
RE = 1.98 kΩ
RE ≈ 2 kΩ
VE = 2 kΩ * 2.02 mA
VE = 4.04 V
= 4.04 V

## Slide 5: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V
5. Calculate VB
6. Calculate I1
VB = VE + 0.7 V
I1 = 10 * IB
VB = 4.74 V
I1 = 200 μA
= 4.04 V
4.74 V
200 μA

## Slide 6: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V
7. Calculate I2
8. Calculate R1
R1 = (VCC - VB )/ I1
I2 = I1 - IB
I2 = 180 μA
= 4.04 V
4.74 V
200 μA
180 μA
R1 = (10.26 V)/ 200 μA
R1 = 51.3 kΩ
R1 = 51 kΩ
Standard 5% value

## Slide 7: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V
9. Calculate R2
10. Calculate Vout
R2 = (VB )/ I2
Vout = (VCC + VE )/2
= 4.04 V
4.74 V
200 μA
180 μA
R2 = (4.74 V)/ 180 μA
R2 = 26.3 kΩ
Standard 2% value
R2 = 26.1 kΩ
Vout = (15 V + 4.04 V )/2
Vout = 9.52 V

## Slide 8: Common Emitter Amplifier Circuit – Practice Problem 1
Find values for the resistors to bias the circuit so that IB = 20 μA. The transistor has β = 100.
= 15 V
15 V
11. Calculate IC
12. Calculate RC
IC = β IB
RC = (VCC - Vout )/ IC
= 4.04 V
4.74 V
200 μA
180 μA
IC = 2 mA
RC = (15 V - 9.52 V )/ 2 mA
RC = (5.48 V )/ 2 mA
RC = 2.74 kΩ
Standard 2% value

## Slide 10: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V
3.0 mA.

## Slide 11: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V
1. Calculate IB
IB = IC / β
IB = 30 μA / 150
IB = 0.2 μA
2. Calculate IE
IE = IB (β +1)
IE = 0.2 μA + 30 μA
IE = IB + IC
IE = 30.2 μA

## Slide 12: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V
3. Choose VE
VE = 2.3 V
4. Calculate RE
RE = VE / IE
10% = 1.0 V
33% = 3.33 V
RE = 2.3 V / 30.2 μA
RE = 76.2 kΩ
RE = 75 kΩ
Standard 2% value
VE = 2.27 V

## Slide 13: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V
5. Calculate VB
VB = VE + VON
6. Calculate I1
I1 = 10 IB
VB = 3.0 V
I1 = 2 μA
7. Calculate R1
R1 = 7.0 V/ 2 μA
R1 = 3.5 MΩ
R1 = 3.5 MΩ
Standard 2% value

## Slide 14: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V
8. Calculate I2
I2 = 9 IB
I1 = 1.8 μA
9. Calculate R2
R2 = 3.0 V/ 1.80 A
R2 = 1.67 MΩ
R2 = 1.69 MΩ
Standard 2% value

## Slide 15: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 30 μA. The transistor has β = 150.
= 10 V
10 V
10. Calculate Vout
11. Calculate RC
RC = 3.85 V/ 30 μ A
RC = 128 kΩ
RC = 127 kΩ
Standard 2% value
Vout = (VCC + VE )/2
Vout = (10 V + 2.3 V )/2
Vout = 6.15 V

## Slide 17: Common Emitter Amplifier Circuit – Practice Problem 2 b
Find values for the resistors to bias the circuit so that IC = 3 mA. The transistor has β = 150.
= 10 V
10 V
1. Calculate IB
IB = IC / β
IB = 3 mA / 150
IB = 20 μA
2. Calculate IE
IE = IB (β +1)
IE = 3 mA + 0.02 mA
IE = IB + IC
IE = 3.02 mA

## Slide 18: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 3 mA. The transistor has β = 150.
= 10 V
10 V
3. Choose VE
VE = 2.3 V
4. Calculate RE
RE = VE / IE
10% = 1.0 V
33% = 3.33 V
RE = 2.3 V / 3.02 mA
RE = 762 Ω
RE = 750 Ω
Standard 2% value
VE = 2.27 V

## Slide 19: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 3 mA. The transistor has β = 150.
= 10 V
10 V
5. Calculate VB
VB = VE + VON
6. Calculate I1
I1 = 10 IB
VB = 3.0 V
I1 = 200 μA
7. Calculate R1
R1 = 7.0 V/ 200 μA
R1 = 35 kΩ
R1 = 34.8 kΩ
Standard 2% value

## Slide 20: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 3 mA. The transistor has β = 150.
= 10 V
10 V
8. Calculate I2
I2 = 9 IB
I1 = 180 μA
9. Calculate R2
R2 = 3.0 V/ 180 μA
R2 = 16.7 kΩ
R2 = 16.9 kΩ
Standard 2% value

## Slide 21: Common Emitter Amplifier Circuit – Practice Problem 2
Find values for the resistors to bias the circuit so that IC = 3 mA. The transistor has β = 150.
= 10 V
10 V
10. Calculate Vout
11. Calculate RC
RC = 3.85 V/ 3 mA
RC = 1.28 kΩ
RC = 1.27 kΩ
Standard 2% value
Vout = (VCC + VE )/2
Vout = (10 V + 2.3 V )/2
Vout = 6.15 V

## Slide 23: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V

## Slide 24: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V
Find the Thevenin equivalent resistance looking to the left from the base of the transistor
What is the Thevenin voltage?

## Slide 25: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V
Find the Thevenin equivalent resistance looking to the left from the base of the transistor
What is the Thevenin voltage?

## Slide 26: Common Emitter Amplifier Circuit – Practice Problem 3
Write the KVL equation for the base-emitter loop
What is the relationship between the base current and the emitter current?
Substitute
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V

## Slide 27: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V
Calculate IE
What is the emitter voltage?
What is the collector current?

## Slide 28: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V
What is the output voltage?
What is the base voltage?

## Slide 29: Common Emitter Amplifier Circuit – Practice Problem 3
Find the values of the DC currents and voltages of the circuit. The transistor has β = 127.
= 10 V
10 V
Calculate I1
– 5 = 396
Calculate I2