## Slide 1: Analog Electronics Technology
Current Sources, Active Loads

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
BJT basics
Common Emitter Amplifier Circuits
Voltage Divider Biasing
Degenerate Emitter Resistor
Rules of Thumb
Other Biasing Methods
Common Base & Common Collector Amplifier Circuits
Op Amps

## Slide 3: What we will talk about today
Current mirrors
Active Loads

## Slide 4: Current Mirrors
Q2
IC2
IB2
VDD=-5 V
Q1
Iref
IC1
IB1
Q3
IC3
IB3
VCC= 5 V
What makes the collector currents different?
A difference in the transistors
Only used in integrated circuits
With integrated circuits we can control IS so that the transistors match
With integrated circuits we can adjust different parameters so that one transistor has a different current

## Slide 5: Current Mirrors
Q2
IC2
IB2
VDD=-5 V
Q1
Iref
IC1
IB1
Q3
IC3
IB3
VCC= 5 V
What makes the collector currents different?
A difference in the transistors
Only used in integrated circuits
The base currents being supplied by Iref
Iref = IC1 + IB1 + IB2
+ IB3 + IB4 + IB5 + …
(makes collector currents different from Iref )

## Slide 6: Current Mirrors
Q2
IC2
IB2
VDD=-5 V
Q1
Iref
IC1
IB1
Q3
IC3
IB3
VCC= 5 V
What makes the collector currents different?
A difference in the transistors
Only used in integrated circuits
The base currents being supplied by Iref
Circuit changes can compensate
Q4
IC4
IB4

## Slide 7: Current Mirrors
Q2
IC2
IB2
VDD=-5 V
Q1
Iref
IC1
IB1
Q3
IC3
IB3
VCC= 5 V
What makes the collector currents different?
A difference in the transistors
Only used in integrated circuits
The base currents being supplied by Iref
The Early Effect
IC2 is not totally independent of VCE
Circuit changes can compensate
Circuit changes can compensate

## Slide 9: Active Loads
One of out “rules of thumb” was to make the output voltage halfway between VCC and VE
We will make the output voltage half of VCC
If we make VCC = 2 V, then Vout = 1 V and RC = (1 V)/2 mA = 0.5 k

## Slide 10: Active Loads
We will make the output voltage half of VCC
If we make VCC = 2 V, then Vout = 1 V and RC = 1 V/2 mA = 0.5 k
We previously found the gain of this circuit.
Gain ≈ - RC / RE
Gain ≈ - 0.23

## Slide 11: Active Loads
If we make VCC = 10 V,
Gain ≈ - 1.16
then Vout = 5 V
RC = 5 V/2 mA = 2.5 k
If we make VCC = 20 V,
Gain ≈ - 2.3
then Vout = 10 V
RC = 10 V/2 mA = 5 k
If we make VCC = 100 V,
Gain ≈ - 23
then Vout = 50 V
RC = 50 V/2 mA = 25 k

## Slide 12: Active Loads
The larger that we make RC, the larger the gain
This comes with the expense of requiring higher voltages in order to keep the output midway between the supply voltage and saturation.

## Slide 13: Common Emitter Amplifier Circuit Design – graphical solution
IC
VCE
Transistor is in saturation
IC = Vcc / RC - VCE / RC
Vcc /RC
slope = -1 /RC
slope = -1 /RC
intercept
Use the given value for Rc to plot the load line
Adjust Rc until the intersection of the load line and the base current curve is centered
Vcc
= 8V
= 2V

## Slide 14: Common Emitter Amplifier Circuit Design – graphical solution
IC
VCE
IC = Vcc / RC - VCE / RC
Vcc /RC
slope = -1 /RC
intercept
Use the given value for Rc to plot the load line
Keep Rc the same and adjust VCC until the intersection of the load line and the base current curve is centered
Vcc
= 8V
= 2V
slope = -1 /RC
By increasing Rc , we need to adjust VCC to prevent saturation
Vcc

## Slide 15: Common Emitter Amplifier Circuit Design – graphical solution
IC
VCE
The higher the collector resistance, the lower the slope and the higher the gain.
We need a non-linear “load line” so that we can have a low slope on our “load line”, but it won’t require a high voltage
What type of device has an almost zero slope on an I-V graph?
A zero slope on an I-V graph means that it maintains the same current regardless of the voltage across it.
A current source
An ideal current source → zero slope
A real current source → near zero slope

## Slide 16: Active Loads
How do we replace the collector resistor with a current source?
We do something similar to how we replaced the emitter resistor with a current source, but we use pnp transistors

## Slide 17: Active Loads
5 V

## Slide 18
Q2
IC2
IB2
VDD=-5 V
Q1
Iref
IC1
IB1
Q3
IC3
IB3
5 V

## Slide 19: What we talked about today
Current mirrors
Active Loads