## Slide 1: Analog Electronics Technology
BJT small signal response

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
BJT basics
DC Biasing
Common Emitter Amplifier Circuits
Common Base Amplifier Circuits
Common Collector Amplifier Circuits
Small Signal Analysis
Op Amps

## Slide 3: What we will talk about today
Small signal analysis using DC results
Small signal models of BJT
Modification for Early Effect

## Slide 4: Common Emitter Amplifier Circuit – graphical solution
find base (diode) current
On transistor characteristics drawing, find curve corresponding to base current
Use semi-ideal diode model with load line
Vbb /R1
Chart: Diode Current-Voltage Characteristics
| -4.9999999999998795E-2 | 1.2073675392798577E-15 | 5.000000000000121E-2 | 0.10000000000000121 | 0.15000000000000122 | 0.20000000000000123 | 0.25000000000000122 | 0.30000000000000121 | 0.3500000000000012 | 0.40000000000000119 | 0.45000000000000118 | 0.50000000000000122 | 0.55000000000000127 | 0.60000000000000131 | 0.65000000000000135 | 0.7000000000000014 | 0.7010000000000014 | 0.75100000000000144
 | -8.5519e-14 | 4.6629e-27 | 5.9058e-13 | 4.6691e-12 | 3.2834e-11 | 2.2734e-10 | 1.5706e-09 | 1.0847e-08 | 7.4906e-08 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 5.1729e-07 | 100 | 1000
Vbb
IC
VEC
load line
Vcc /RC
slope = -1 /RC
Choose a value for Rc
Vcc
Curves of constant base current
Find quiescent (DC) operating point
Transistor curves

## Slide 5: Small signal response of Common Emitter Amplifier
10 V
So far we have ignored the effects of this part of the circuit
The capacitor blocked DC signals
The small signal response looks at how these signals are amplified

## Slide 6
Easiest but not as Accurate Method:
Modify results from DC analysis

## Slide 7: From Prior Lecture: Common Emitter Amplifier Circuit
DC bias
AC signal
Vout = - Vcc + RC β ( Vbb - 0.7 V) / R1
Include vin with Vbb
Vout = - Vcc + RC β ( [ Vbb + vin ] - 0.7 V) / R1
Vout = - Vcc + RC β ( Vbb - 0.7 V) / R1 + RC β vin / R1
Separate out the term with vin
DC part
Small signal part

## Slide 8: From Prior Lecture: Common Emitter Amplifier Circuit
DC bias
AC signal
Vout = - Vcc + RC β ( Vbb - 0.7 V) / R1 + RC β vin / R1
DC part
Small signal part
Small signal gain is the small signal output divided by the small signal input
AV = RC β / R1
Usually the small signal polarity is shown opposite of what we did
Which results in a negative sign here
‒

## Slide 9
Common Emitter
with
Emitter Resistor and Voltage Divider

## Slide 10: From Prior Lecture: Common Emitter Amplifier Circuit – Biasing with Voltage Divider and Emitter Resistor
If Zs >> R1, R2
If Zs << R1, R2

## Slide 11: From Prior Lecture: Common Emitter Amplifier Circuit – Biasing with Voltage Divider and Emitter Resistor
‒
‒
For large β

## Slide 13
Small signal model of BJT

## Slide 14: Large signal model of BJT in forward active region – diode and dependent current source
ID
β ID
base
emitter
collector
pnp BJT
ID
β ID
base
emitter
collector
npn BJT
Do you remember the small signal model of the diode?

## Slide 15: Small signal model of BJT in forward active region – resistor and dependent current source
rπ
rπ
rπ= VT / IBQ
IB
β IB
base
emitter
collector
pnp BJT
IB
β IB
base
emitter
collector
npn BJT
This is the same resistance as the small signal resistance of the diode

## Slide 16: Small Signal BJT Analysis
Use the large signal model of the transistor to determine biasing (quiescent point)
Use the small signal model of the transistor to determine response to small inputs
rπ= VT / IBQ

## Slide 17
For the common emitter BJT, we need to modify the model to improve accuracy.
This model works well for the common base biased transistor.

## Slide 18: Common Emitter Amplifier Operating Curves
IC
VEC
Curves of constant base current
Slope of line = 1/(output resistance)
IB1
IB2
IB3
IB4
IB5
IB6
IB7
IB8

## Slide 19: Common Emitter Amplifier – Early Effect
For a common emitter BJT operating in the forward active region, the linear portion of the curve has a non-zero slope (exaggerated here for clarity).
The extrapolated lines all converge at a common point on the negative voltage axis as shown.
IC
VEC
- VA
IB1
IB2
IB3
IB4
IB5
IB6
IB7

## Slide 20: Common Emitter Amplifier – Early Effect
This phenomenon is called the Early effect, named after the person who first analyzed it.
VA is called the Early voltage
IC
VEC
- VA

## Slide 21: Bipolar Junction Transistor (BJT)
p+-type
n-type
As VCE grows and the base collector junction gets more reverse biased, the space charge region grows making the base shrink.
space charge region
space charge region
p-type
Emitter
Collector
Base
A smaller base gives less opportunity for recombination in the base, so the efficiency of the transistor is increased.

## Slide 22: Common Emitter Amplifier – Early Effect
The Early effect can be included in the transistor equations by adding a factor to the equation for the collector current.
For a pnp transistor, the equation becomes:
For an npn transistor, the equation becomes:
Added factor for the Early effect.
The slope of the line is the reciprocal of the output impedance of the common emitter amplifier.
ro = VA / IC0
Early voltages are typically between 50 V and 100 V.

## Slide 23: Adjusted small signal model of common emitter BJT in forward active region
rπ= VT / IBQ
IB
β IB
base
emitter
collector
pnp BJT
rπ
ro
IB
β IB
base
emitter
collector
npn BJT
rπ
ro
ro= VA / ICQ

## Slide 24: Equivalent model of common emitter BJT in forward active region
rπ= VT / IBQ
IB
gm Vπ
base
emitter
collector
pnp BJT
rπ
ro
IB
gm Vπ
base
emitter
collector
npn BJT
rπ
ro
ro= VA / ICQ
Vπ
+
-
Vπ
+
-
gm rπ = β
transconductance
Intrinsic capacitance can be added for high frequency analysis

## Slide 26: From Before: Common Emitter Amplifier Circuit
DC bias
AC signal
AV = RC β / R1
‒
More accurate results using small signal model
AV = ‒ (RC || ro ) β / (R1 + rπ )
If rπ << R1 and RC << ro then this is equivalent to the former result

## Slide 27: From Prior Lecture: Common Emitter Amplifier Circuit – Biasing with Voltage Divider and Emitter Resistor
Next time we will use the small signal model of the transistor to analyze the common emitter amplifier with voltage divider biasing and with an emitter resistor.