## Slide 1: Analog Electronics Technology
Op Amps

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
Op Amps

## Slide 3: What we will talk about today
Ideal Op Amps
Non-inverting Op Amp circuits
Inverting Op Amp circuits ??

## Slide 4
An op amp is a differential amplifier.
The output of the amplifier equals the internal forward gain of the amplifier, a, times the difference of the inputs.
—
+
V-
V+
Vout
Vout = a (V+ - V-)
Negative input
Positive input
Internal forward gain

## Slide 5: Ideal Op Amp
The internal forward gain is infinite
The input current is zero for both terminals
The output resistance is zero
—
+
Vn
Vp
Vout
rd
ro
aVo
(The input resistance is infinite)

## Slide 6: Noninverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
The input voltage, Vin, is applied to the positive input of the amplifier
The resistors R1 and R2 form a voltage divider so that a portion of the output is applied to the negative terminal.
V- = Vout R1 / (R1 + R2)

## Slide 7: Noninverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
Define feedback factor, b: b = R1 / (R1 + R2)
Then: V- = b * Vout
The op amp output equals the internal gain times the input difference
Vout = a (V+ - V-) = a ( Vin - b * Vout )

## Slide 8: Noninverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
Vout = a ( Vin - b * Vout )
Vout ( 1 + a*b) = a ( Vin)
Vout + a * b * Vout = a ( Vin)
Vout = a Vin - a b * Vout
Distribute the a
Rearrange to get terms with Vout together
Factor out Vout
Vout = ( Vin) a/ ( 1 + a*b)
Solve for Vout
feedback factor
b = R1 / (R1 + R2)

## Slide 9: Noninverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
Vout = ( Vin) a/ ( 1 + a*b)
Find the closed loop voltage gain, A
feedback factor
b = R1 / (R1 + R2)

## Slide 10: Noninverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
If a*b >> 1
feedback factor
b = R1 / (R1 + R2)

## Slide 11: Noninverting Amplifier Example 1
—
+
Vin
Vout
+
—
R2 = 2 kΩ
R1= 1 kΩ
Find the output of the following circuit.
(1+ R2 / R1 )
= 3

## Slide 12: Noninverting Amplifier Example 1
—
+
Vin
Vout
+
—
R2 = 2 kΩ
R1= 1 kΩ
A word of caution:
= 1
= 3
= 2
= 6
= 10
= 30
Power supply for Op Amp
Often ±15 V
Could be ±18 V or ±12 V
The output is limited by the power supply voltage

## Slide 13: Noninverting Amplifier Example 2
—
+
Vin
Vout
+
—
R2
R1
(1+ R2 / R1 ) = 5
Design a circuit whose output voltage will be 5 times the input voltage.
(1+ R2 / R1 ) = 5
R2 / R1 = 4
Choose R2 = 4 k Ω R1 = 1 k Ω

## Slide 14: Noninverting Amplifier Example 3
—
+
Vin
Vout
+
—
R2 = 2 kΩ
R1= 10 kΩ
(1+ R2 / R1 )
What is the gain (Vout / Vin) of the following circuit.
= (1+ 2 kΩ / 10 kΩ )
= 1.2

## Slide 15: Noninverting Amplifier Example 4
—
+
Vin
Vout
+
—
R2 = 100 Ω
R1= 100 kΩ
(1+ R2 / R1 )
What is the gain (Vout / Vin) of the following circuit.
= (1+ 0.1 kΩ / 100 kΩ )
= 1.001

## Slide 16: Noninverting Amplifier Example 5
—
+
Vin
Vout
+
—
R2 = 100 Ω
R1= 10 MΩ
(1+ R2 / R1 ) = (1+ 0.1 kΩ / 10000 kΩ ) = 1.00001
What is the gain (Vout / Vin) of the following circuit.

## Slide 17: Noninverting Amplifier Example 6
—
+
Vin
Vout
+
—
R2 = 100 Ω
(1+ R2 / R1 )
What is the gain (Vout / Vin) of the following circuit.
= (1+ 0.1 kΩ /
∞ kΩ )
= 1

## Slide 18: Voltage Follower
—
+
Vin
Vout
+
—
for the special case of R2 / R1 0