## Slide 1: Analog Electronics Technology
Op Amps

## Slide 2: Analog Electronics Technology
Diodes
BJT’s
Op Amps
Ideal Op Amps
Non-inverting Op Amps
Inverting Op Amps

## Slide 3: What we will talk about today
Inverting Op Amp circuits

## Slide 4: Inverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
The positive input of the amplifier equals zero.
Use the superposition principle to find what V- is.

## Slide 5: Inverting Amplifier
What is the voltage at V- from Vout ?
—
+
Vin
Vout
+
—
R2
R1
Short circuit Vin
R1 and R2 form a voltage divider so that a portion of the output is applied to the negative terminal.
V- = Vout R1 / (R1 + R2)

## Slide 6: Inverting Amplifier
R1 and R2 form a voltage divider so that a portion of the output is applied to the negative terminal.
—
+
Vin
Vout
+
—
R2
R1
What is the voltage at V- from Vin ?
Short circuit Vout
V- = Vin R2 / (R1 + R2)

## Slide 7: Inverting Amplifier
V- = Vout R1 / (R1 + R2) + Vin R2 / (R1 + R2)
Add together the two contributions:
Vout = a (V+ - V- )
Vout = -a [Vout R1 / (R1 + R2) + Vin R2 / (R1 + R2)]
Internal gain of the amplifier:
Substitute:
—
+
Vin
Vout
+
—
R2
R1
Contribution from output
Contribution from input
V+ = 0

## Slide 8: Inverting Amplifier
Vout = -a [Vout R1 / (R1 + R2) + Vin R2 / (R1 + R2)]
Vout + a Vout R1 / (R1 + R2) = - a Vin R2 / (R1 + R2)
Vout (R1 + R2) + a Vout R1 = - a Vin R2
Multiply by (R1 + R2) :
—
+
Vin
Vout
+
—
R2
R1
Vout [(R1 + R2) + a R1 ] = - a Vin R2

## Slide 9: Inverting Amplifier
Vout [(R1 + R2) + a R1] = - a Vin R2
Since a is extremely large:
Solve for gain:
—
+
Vin
Vout
+
—
R2
R1

## Slide 10: Inverting Amplifier
Alternate method based upon ideal op amp properties
—
+
Vin
Vout
+
—
R2
R1
Virtual Ground
The op amp will force its input terminals to be at the same voltage
Since the V+ terminal is grounded, the V- terminal will also be at zero volts
The V- terminal will not actually be grounded. No current will flow from the terminal to ground, but the terminal will be at zero volts

## Slide 11: Inverting Amplifier
Since the V- terminal is at virtual ground, we can determine the current through R1
I1 = Vin / R1
No current flows into the terminals of an ideal op amp
Apply KCL to the V- node
—
+
Vin
Vout
+
—
R2
R1
I1
I2
I1 = I2

## Slide 12: Inverting Amplifier
—
+
Vin
Vout
+
—
R2
R1
Calculate the voltage drop across I2
V2 = I2 R2
I1
I2
V2
+
-
Vout = -V2
= -I2 R2
= -I1 R2
= -(Vin / R1 ) R2
Vout /Vin = -(R2/ R1 )

## Slide 13: Inverting Amplifier Example 1
—
+
Vin
Vout
+
—
10 kΩ
1 kΩ
Calculate the gain of the above circuit
Vout /Vin = -(R2/ R1 )
= -(10 kΩ/ 1 kΩ)
= - 10

## Slide 14: Inverting Amplifier Example 2
—
+
Vin
Vout
+
—
1 kΩ
10 kΩ
Calculate the gain of the above circuit
Vout /Vin = -(R2/ R1 )
= -(1 kΩ/ 10 kΩ)
= - 0.1

## Slide 15: Inverting Amplifier Example 3
—
+
Vin
Vout
+
—
R2
R1
Design a circuit that has a gain of -20
Vout /Vin = -(R2/ R1 ) = -20
Choose R2 = 20 kΩ
R1 = 1 kΩ

## Slide 16: Circuit Designs of Various Gains

## Slide 17: Example 4
Design a circuit that has a gain of 3
The gain is positive, so we need a non-inverting op amp.
—
+
Vin
Vout
+
—
R2
R1

## Slide 18: Example 5
Design a circuit that has a gain of -12
The gain is negative, so we need an inverting op amp.
—
+
Vin
Vout
+
—
R2
R1

## Slide 19: Example 6
Design a circuit that has a gain of -0.5
The gain is negative, so we need an inverting op amp.
—
+
Vin
Vout
+
—
R2
R1

## Slide 20: Example 6
Design a circuit that has a gain of 0.25
The gain is positive, so we need a non-inverting op amp.
—
+
Vin
Vout
+
—
R2
R1
We don’t know how to do that.

## Slide 21
-∞
∞
0
1
-1
Inverting amplifier
R2 < R1
R2 > R1
Noninverting amplifier
Gain
—
+
Vin
Vout
+
—
R2
R1
—
+
Vin
Vout
+
—
R2
R1

## Slide 22: Method 1 – Two inverting op amps
—
+
Vin
+
—
R2
R1
—
+
Vout
R4
R3
Vout

## Slide 23
There is another way that will not require two op amps

## Slide 24: Method 2
+
—
Vin
A voltage divider will reduce the voltage
Vm
R3 = 3 kΩ and R4 = 1 kΩ will reduce the output by 3 fourths
3 kΩ
R3
R4
1 kΩ
The problem with this is that a load will further reduce the voltage
RL =1 kΩ
A voltage follower can solve this problem

## Slide 25: Method 2 – Voltage Divider Followed by Voltage Follower
—
+
Vout
+
—
Vin
R3
R4
A voltage follower will provide a low resistance output so that a load will not cause voltage droop
Vm

## Slide 26
-∞
∞
0
1
-1
Inverting amplifier
R2 < R1
R2 > R1
Noninverting amplifier
Voltage divider with voltage follower

## Slide 28: Practice Problems – Circuit Designs of various gains

## Slide 29: Practice Problem 1
Design a circuit that has a gain of 6

## Slide 30: Practice Problem 2
Design a circuit that has a gain of -12

## Slide 31: Practice Problem 3
Design a circuit that has a gain of 0.4

## Slide 32: Practice Problem 4
Design a circuit that has a gain of ‒ 0.6

## Slide 33: Practice Problem 5
Design a circuit that has a gain of 15