## Slide 1: Analog Electronics Technology
Op Amps

## Slide 2: What we will talk about today
Input impedance of op amp amplifiers
Problems caused
Solutions
More op amp circuits
Adding voltages
(V1 + V2)
Weighted addition
(3V1 + 5V2)

## Slide 3: Look at the input impedance of both amplifier types
Noninverting
—
+
Vin
Vout
+
—
R2
R1
—
+
Vin
Vout
+
—
R2
R1
Input resistance of the amplifier is approximately equal to the input resistance of the op amp
Input resistance of the amplifier is approximately equal to R1
Inverting
Ideal op amp
infinite
Real op amp
very high

## Slide 4: Why is input impedance important?
Inverting Amplifier
—
+
Vout
R2
R1
The combination of the source resistance, RS, and the input resistance of the amplifier, R1, forms a voltage divider which attenuates the input voltage.
Vin
+
—
Source with internal resistance
RS

## Slide 5: Why is input impedance important?
Inverting Amplifier
—
+
Vout
R2 = 50 kΩ
R1= 10 kΩ
—
+
Vout
R2 = 500 Ω
R1= 100 Ω
Vin
+
—
Source
RS
Vin
+
—
Source
RS

## Slide 6: A two-stage amplifier can solve the problem.
Inverting Amplifier
—
+
Vout
R2
R1
The low output resistance of the voltage follower makes the inverting amplifier see the full voltage from the source.
Source with internal resistance
+
RS
Vin
—
—
+
Vout
Voltage Follower
The high input resistance of the voltage follower keeps the source from being loaded down.

## Slide 7: A “T” arrangement can also help
—
+
Vin
Vout
+
—
R2
R1
Source with internal resistance
RS
R3
R4
The gain can be increased without using a very large feedback resistor or too small of an input resistor

## Slide 8: A “T” arrangement Example
—
+
Vin
Vout
+
—
R2
R1
Source with internal resistance
RS
R3
R4
RS = 10 kΩ
We want a gain of -100
We want R1 = 100 kΩ to prevent too much loading
We want all resistors <= 500 kΩ
Choose R2 = 500 kΩ

## Slide 9: A “T” arrangement Example
—
+
Vin
Vout
+
—
R2
R1
Source with internal resistance
RS
R3
R4
RS = 10 kΩ
We want a gain of -100
We want R1 = 100 kΩ to prevent too much loading
We want all resistors <= 500 kΩ
Choose R3 = 500 kΩ

## Slide 10: A “T” arrangement Example
—
+
Vin
Vout
+
—
R2
R1
Source with internal resistance
RS
R3
R4
RS = 10 kΩ
We want a gain of -100
We want R1 = 100 kΩ to prevent too much loading
We want all resistors <= 500 kΩ
Choose R3 = 500 kΩ
Choose R4 = 25 kΩ
We were able to get a gain of -100 without loading down the source and without using large resistors

## Slide 12: A Summing Amplifier Circuit
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
Inputs to be added
Resistors provide weighting factors
For simple addition, make all resistors identical
For example:
3 V1 + 2 V2 + V3
Negative

## Slide 13: A Summing Amplifier Circuit
The negative input of the op amp is at virtual ground.
I3 = V3 / R3
I2 = V2 / R2
I1 = V1 / R1
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
Since no current flows into the op amp inputs,
If = I1 + I2 + I3
The voltage drop across the feed back resistor is:
Vf = If Rf = (I1 + I2 + I3)Rf

## Slide 14: A Summing Amplifier Circuit
The output of the op amp is Vout = - Vf
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
Notice that it is always the negative of the sum
The ratios of the resistors provide weighting factors.

## Slide 15: A Summing Amplifier Circuit Example 1
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
1 kΩ
1 kΩ
1 kΩ
1 kΩ

## Slide 16: A Summing Amplifier Circuit Example 2
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
2 kΩ
1 kΩ
3 kΩ
6 kΩ

## Slide 17: A Summing Amplifier Circuit -- Example 3
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
Example: Design a circuit that computes
C
Choose a value for Rf, and then calculate the others
Choose Rf = 10 kΩ
then R1 = 5 kΩ
R2 = 30 kΩ
R3 = 40 kΩ

## Slide 18: A Summing Amplifier Circuit -- Example 4
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
Example: Design a circuit that computes
C
Choose Rf = 10 kΩ
then R1 = 2 kΩ
R2 = 20 kΩ
R3 = 5 kΩ

## Slide 19: A Summing Amplifier Circuit -- Example 5
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
Example: Design a circuit that computes
C
Choose Rf = 12 kΩ
then R1 = 2 kΩ
R2 = 24 kΩ
R3 = 3 kΩ