## Slide 1: Analog Electronics Technology
Op Amps

## Slide 2: What we will talk about today
Subtracting voltages
(V1 ‒ V2)
Multiplying the difference between voltages
6 (V1 ‒ V2)

## Slide 3: A Difference Circuit
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4

## Slide 4: A Difference Circuit – Method 1 (Superposition Principle)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
Short circuit V2, and find the output that is due to V1.
With V2 short circuited, the positive terminal is grounded.
The amplifier then acts like a normal inverting amplifier with respect to V1
the output is:
Vo,1 = - V1 (R2 / R1)
the output due to source 1

## Slide 5: A Difference Circuit – Method 1 (Superposition Principle)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
Now short circuit V1, and find the output that is due to V2.
Let’s compare the circuit to a non-inverting amplifier

## Slide 6: A Difference Circuit – Method 1 (Superposition Principle)
—
+
Vout
R2
R1
+
V1
—
This is a non-inverting amplifier
With V1 short circuited, our circuit acts like a non-inverting amplifier
The input to the non-inverting amplifier is reduced by the voltage divider formed by R3 and R4.
+
Vin
—
R3
R4
+
V2
—

## Slide 7: A Difference Circuit – Method 1 (Superposition Principle)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
The effective voltage supplied to the non-inverting amplifier is thus:
Vin,eff = V2 R4 / ( R3+ R4)
The output is:
Vo,2 = V2 R4 / ( R3+ R4) * (1 + R1 /R2)
gain

## Slide 8: A Difference Circuit – Method 1 (Superposition Principle)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
By the superposition principle, Vout is the sum of those two components:
Vout = Vo,1 + Vo,2
Vout = V2 R4 / ( R3+ R4) * (1 + R1 /R2) - V1 (R2 / R1)

## Slide 9: A Difference Circuit
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
I1
If we choose resistors so that then

## Slide 10: A Difference Circuit
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
I1
If we choose resistors so that then
For simple subtraction, choose
R1 = R2 and
R3 = R4
choose a different ratio to multiply the difference
= M

## Slide 11: A Difference Circuit – Example 1
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
I1
Design a circuit that has a voltage output Vout = 6 (V2 – V1)
Choose resistors
R2 = 6 kΩ
R1 = 1 kΩ
R4 = 6 kΩ
R3 = 1 kΩ
Would resistors
R2 = 6 kΩ
R1 = 1 kΩ
R4 = 60 kΩ
R3 = 10 kΩ
work?
Yes!
6 kΩ / 1 kΩ =6
60 kΩ / 10 kΩ =6

## Slide 12: A Difference Circuit – Example 2
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
I1
Design a circuit that has a voltage output Vout = 20 (V2 – V1)
Choose resistors
R2 = 20 kΩ
R1 = 1 kΩ
R4 = 20 kΩ
R3 = 1 kΩ

## Slide 13
Practice Problems
Adding and Subtracting

## Slide 14
Design circuits to do the following calculations:
1. Design a circuit that has a voltage output Vout = 3 (V2 – V1)
2. Design a circuit that has a voltage output Vout = ‒ (3 V1 + 6 V2 + 4 V3 )
3. Design a circuit that has a voltage output Vout = ‒ (⅓ V1 + 2 V2 + 5 V3 )

## Slide 15
Design circuits to do the following calculations:
4. Design a circuit that has an output voltage Vout = 12 (V1 – V2)
5. Design a circuit that has a voltage output Vout = ‒ (3 V1 + ⅝ V2 + ⅓ V3 )
6. Design a circuit that has a voltage output Vout = ‒ (8 V1 + 6 V2 + 4 V3 )

## Slide 16: Challenge Problem!
Design a circuit that computes
This will require more than one op amp.

## Slide 18: A Difference Circuit – Method 2 (Using the properties of an ideal op amp)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
Neither V1 nor Vout have any effect on the voltage at the positive input. It is totally determined by the input V2.
R3 and R4 form a voltage divider for the input V2.
The voltage at the positive terminal is given by
V+ = V2 R4 / (R3 + R4)

## Slide 19: A Difference Circuit – Method 2 (Using the properties of an ideal op amp)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
One property of an ideal op amp is that the voltage at the negative terminal is force to be the same as that of the positive terminal.
Therefore
V- = V+ = V2 R4 / (R3 + R4)

## Slide 20: A Difference Circuit – Method 2 (Using the properties of an ideal op amp)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
The current through the resistor R1 can now be found.
I1 = [V1 - V2 R4 / (R3 + R4) ]/ R1
Since no current flows into the inputs of an ideal op amp, this same current must flow through R2. So the voltage drop across R2 is
Vdrop = R2[V1 - V2 R4 / (R3 + R4) ]/ R1
I1

## Slide 21: A Difference Circuit – Method 2 (Using the properties of an ideal op amp)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
The output voltage can now be found.
Vout = V- - Vdrop
I1
Vout = V2 R4 / (R3 + R4) - R2[V1 - V2 R4 / (R3 + R4) ]/ R1
= V2 R4 / (R3 + R4) + V2 R2 R4 / R1(R3 + R4) - R2[V1]/ R1
= V2 R4 / (R3 + R4)[ 1 + R2 / R1] - R2V1/ R1

## Slide 22
The rest is a direct repeat of slides 9 and 10

## Slide 23: A Difference Circuit
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
I1
If we choose resistors so that then

## Slide 24: A Difference Circuit
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
I1
If we choose resistors so that then
For simple subtraction, choose
R1 = R2 and
R3 = R4
choose a different ratio to multiply the difference
= M