## Slide 1: Analog Electronics Technology
Op Amps

## Slide 2
Practice Problems
Adding and Subtracting

## Slide 3
1. Design a circuit that has a voltage output Vout = 3 (V2 – V1)
—
+
Vout
R2
R1
+
V1
—
R3
+
V2
—
R4
Choose resistors
R2 = 6 kΩ
R1 = 2 kΩ
R4 = 6 kΩ
R3 = 2 kΩ
W
= 3
Difference circuit
6 kΩ
2 kΩ
6 kΩ
2 kΩ

## Slide 4
2. Design a circuit that has a voltage output Vout = ‒ (3 V1 + 6 V2 + 4 V3 )
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
C
Choose a value for Rf, and then calculate the others
Choose Rf = 12 kΩ
then R1 = 4 kΩ
R2 = 2 kΩ
R3 = 3 kΩ
Summing circuit
12 kΩ
4 kΩ
2 kΩ
3 kΩ

## Slide 5
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
C
Choose a value for Rf, and then calculate the others
Choose Rf = 10 kΩ
then R1 = 30 kΩ
R2 = 5 kΩ
R3 = 2 kΩ
Summing circuit
3. Design a circuit that has a voltage output Vout = ‒ (⅓ V1 + 2 V2 + 5 V3 )
10 kΩ
30 kΩ
5 kΩ
2 kΩ

## Slide 6
—
+
Vout
R2
R1
+
—
R3
+
—
R4
Choose resistors
R2 = 12 kΩ
R1 = 1 kΩ
R4 = 12 kΩ
R3 = 1 kΩ
W
= 12
Difference circuit
4. Design a circuit that has an output voltage Vout = 12 (V1 – V2)
V1
V2
12 kΩ
1 kΩ
12 kΩ
1 kΩ

## Slide 7
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
C
Choose a value for Rf, and then calculate the others
Choose Rf = 15 kΩ
then R1 = 5 kΩ
R2 = 24 kΩ
R3 = 45 kΩ
Summing circuit
5. Design a circuit that has a voltage output Vout = ‒ (3 V1 + ⅝ V2 + ⅓ V3 )
15 kΩ
5 kΩ
24 kΩ
45 kΩ

## Slide 8
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
C
Choose a value for Rf, and then calculate the others
Choose Rf = 24 kΩ
then R1 = 3 kΩ
R2 = 4 kΩ
R3 = 6 kΩ
Summing circuit
6. Design a circuit that has a voltage output Vout = ‒ (8 V1 + 6 V2 + 4 V3 )
24 kΩ
3 kΩ
4 kΩ
6 kΩ

## Slide 9: Challenge Problem!
Design a circuit that computes
This will require more than one op amp.
Summing Amplifier
Unity gain inverter
Summing Amplifier
DifferenceAmplifier

## Slide 10: Challenge Problem Solution 1
—
+
Vout
Rf
R1
+
V1
—
+
V2
—
+
V3
—
R2
R3
I2
I1
I3
If
Design a circuit that computes
C
Choose Rf = 8 kΩ then R1 = 2 kΩ
R2 = 4 kΩ
R3 = 1 kΩ
Summing Amplifier
Unity gain inverter
8 kΩ
2 kΩ
4 kΩ
1 kΩ
—
+
Vout
1 kΩ
1 kΩ

## Slide 11: Challenge Problem Solution 2
—
+
Vout
Rf
+
V2
—
+
V3
—
R2
R3
Design a circuit that computes
C
Choose Rf = 2 kΩ then R2 = 4 kΩ
R3 = 1 kΩ
Summing Amplifier
DifferenceAmplifier
2 kΩ
4 kΩ
1 kΩ
1 kΩ
4 kΩ
1 kΩ
—
+
Vout
+
V1
—
4 kΩ
R2d
R1d
R3d
R4d