## Slide 1: Analog Electronics Technology
Op Amps

## Slide 2: What we will talk about today
More op amp circuits
Integrators
Miller Integrators
Voltage Sources
Current to Voltage Conversion

## Slide 3: An Integrator
—
+
Vout
C
R1
+
V1
—
I1
Since the positive input is grounded, the negative input is a virtual ground.
Calculate the current through R1.
I1 = V1 / R1
No current flows into the input terminals of an op amp. What is the capacitor current?
IC = I1 = V1 / R1
IC

## Slide 4: An Integrator
—
+
Vout
C
R1
+
V1
—
I1
Therefore
IC
-
For a capacitor: Q = C V
IC = V1 / R1

## Slide 5: An Integrator
—
+
Vout
C
R1
+
V1
—
I1
IC

## Slide 6: An Integrator
—
+
Vout
C
R1
+
V1
—
I1
IC
Input
Output
V1
Vout
time
time

## Slide 7: An Integrator
—
+
Vout
C
R1
+
V1
—
I1
IC
Output
A problem with an integrator
Input
Small DC offset
Causes the output to eventually saturate

## Slide 8: A Miller Integrator
—
+
Vout
C
R1
+
V1
—
I1
IC
R2
A very large resistance
At DC and extremely low frequencies it acts like an inverting op amp
At normal frequencies it acts like an integrator

## Slide 10: A Voltage Source
VCC = 15 V
R1 = 10 kΩ
R2 = 20 kΩ
RL = 5 kΩ
A load resistance can affect the voltage of a voltage divider
Vout = 2.1 V
This is sometimes called voltage droop.

## Slide 11: A Voltage Source
We can solve this problem by using an op amp as a buffer
VCC = 15 V
R1 = 10 kΩ
R2 = 20 kΩ
RL = 5 kΩ
Now the op amp can drive the load, eliminating voltage droop.
—
+
Vout
A voltage follower
A voltage divider

## Slide 12: A Voltage Source
VCC = 15 V
R1 = 100 kΩ
R2 = 200 kΩ
RL = 5 kΩ
—
+
Vout
What happens if there are fluctuations in the supply voltage?
Vout = (1/3) VCC
If VCC drifts, so does Vout
If VCC = 15.09 V, Vout = 5.03 V

## Slide 13: A Voltage Source with Zener Diode
VCC = 15 V
R2 = 200 kΩ
RL = 5 kΩ
—
+
Vout
R3
R4
A Zener diode provides a more stable reference
Example:
VZ = 2.50 V
Example:
1 kΩ
Example:
3 kΩ
Example:
Vout = 10.0 V

## Slide 14: A Voltage Source with Zener Diode
VCC = 15 V
R2 = 200 kΩ
RL = 5 kΩ
—
+
Vout
R3
R4
A variable resistor makes the power supply adjustable

## Slide 15: A Voltage Source with Zener Diode
Even better methods exist involving a Zener diode reference and extra circuitry to provide stabilization
VCC = 15 V
R2 = 200 kΩ
RL = 5 kΩ
—
+
Vout
R3
R4
A variable resistor makes the power supply adjustable
The Zener voltage does vary very slightly with current.

## Slide 16: A Voltage Source with Zener Diode
RL = 5 kΩ
—
+
Vout
R1
R2
RF
Better voltage regulation, but there is a problem
The diode is biased by the output of the op amp
VZ = 2.50 V
1 kΩ
3 kΩ
Vout = 10.0 V
Stable output
Stable current
Stable Zener voltage

## Slide 17: A Voltage Source with Zener Diode
RL = 5 kΩ
—
+
Vout
R1
R2
RF
The problem
This is also a stable state!
VZ = 2.50 V
1 kΩ
3 kΩ
Vout = 0.0 V
V+ = 0.0 V
We need start-up circuitry

## Slide 18: A Voltage Source
VCC = 15 V
RL = 5 kΩ
—
+
Vout
R1
R2
100 kΩ
RF
A better voltage regulator
10 kΩ
VZ = 2.50 V
1 kΩ
3 kΩ
1.36 V
0.66 V
2.5 V
Zener turned on
Diode reverse biased
2.64 V
10.0 V
Stable output
Stable current
Stable Zener
voltage

## Slide 20: A Current to Voltage Converter
For our normal inverting op amp, the current flowing from the voltage source equals the voltage divided by the resistance Rin
Rin
RF
—
+
Vout
+
V1
—
This can be converted to a current-to-voltage converter by removing Rin and connecting a current source directly to the negative input of the op amp.

## Slide 21: A Current to Voltage Converter
Since the input resistance of the op amp is extremely large, the current I1 all flows through the feedback resistor RF.
RF
—
+
Vout
I1
Since the negative input of the op amp is at virtual ground, the output of the op amp is given by:
Vout = -I1 RF

## Slide 22: A Current to Voltage Converter
A high sensitivity requires a large feedback resistor, RF.
RF
—
+
Vout
I1
Vout = -I1 RF
1 V/μA requires Rf = 1 MΩ
1 V/nA requires Rf = 1 GΩ

## Slide 23: A High Sensitivity Current to Voltage Converter
Do a current balance on node A
RF
—
+
Vout
Iin
R1
R2
A
Vf
Iin

## Slide 24: A High Sensitivity Current to Voltage Converter
RF
—
+
Vout
Iin
R1
R2
A
Vf
Iin
Since no current flows into the input of an op amp, Iin flows through the feedback resistor, Rf

## Slide 25: A High Sensitivity Current to Voltage Converter
RF
—
+
Vout
Iin
R1
R2
A
Vf
Iin
If R1 is small compared to Rf and R2, this term can be much larger than both of them.

## Slide 26: Example:
RF
—
+
Vout
Iin
R1
R2
A
Vf
Iin
Design a current to voltage converter that has a sensitivity of 1 V per nanoamp. Do not use any resisters over 1 mΩ. Use standard 1% tolerance resistors.

## Slide 27: Example:
RF
—
+
Vout
Iin
R1
R2
A
Vf
Iin
Design a current to voltage converter that has a sensitivity of 1 V per nanoamp. Do not use any resisters over 1 MΩ. Use standard 1% tolerance resistors.
If we choose Rf = 1 MΩ, then R2/R1 = 1000
Choose R2 = 1 MΩ and R1 = 1 kΩ

## Slide 28: Example:
RF
—
+
Vout
Iin
R1
R2
A
Vf
Iin
Design a current to voltage converter that has a sensitivity of 1 V per nanoamp. Do not use any resisters over 1 MΩ. Use standard 1% tolerance resistors.
Rf = 1 MΩ
R2 = 1 MΩ
R1 = 1 kΩ