## Slide 1: Analog Electronics Technology
Lab 4
Op Amp Integrators

## Slide 2: Op Amp Integrator Circuit
V+ (15 V) and V- (-15 V) from DC Power Supply
Function Generator
—
+
Vout
C = 1 μF
R1= 10 kΩ
+
Vin
—
Figure 1. An Integrator Circuit
V+
V-
I1
IC

## Slide 3: Op Amp Integrator Theory
Virtual ground
Inputs forced to the same voltage
I1 = Vin/ R1
—
+
Vout
C = 1 μF
R1= 10 kΩ
+
Vin
—
Figure 1. An Integrator Circuit
V+
V-
I1
IC
For an ideal op amp the input current is zero
IC = I1 = Vin/ R1

## Slide 4: Integrator Theory
—
+
Vout
C
R1
+
Vin
—
I1
Therefore
IC
─
For a capacitor: Q = C V
IC = Vin / R1
VC
+
—

## Slide 5: An Integrator
—
+
Vout
C
R1
+
Vin
—
I1
IC

## Slide 6: Op Amp Integrator – Alternate Calculation
Switch to Frequency Domain
Vout = -R2/ R1 * Vin
Inverting Op Amp
—
+
Vout
R1
+
Vin
—
V+
V-
I1
R2
Vout = -Z2/ Z1 * Vin
—
+
Vout
C
R1
+
Vin
—
I1
Z1
Z2
Switch results back to time domain
1/(jω) in frequency domain pairs with integration in the time domain

## Slide 7: Op Amp Integrator Procedure
Set function generator to zero output
Theoretical Output
Real Output
—
+
Vout
C = 1 μF
R1= 10 kΩ
+
Vin
—
Figure 1. An Integrator Circuit
V+
V-
I1
IC
R= 1 kΩ
The problem: small DC offsets get integrated
Probably the small DC offsets are internal to the op amp
One solution: use the “Offset Null” pins of the op amp
Instead, we will use the DC offset of the function generator
Adjust the DC offset to minimize drift
Offset Null

## Slide 8: Op Amp Integrator Procedure
6V amplitude sine wave at f=100 Hz
—
+
Vout
C = 1 μF
R1= 10 kΩ
+
Vin
—
Figure 1. An Integrator Circuit
V+
V-
I1
IC
R= 1 kΩ
DC offset to minimize drift
Output should lead the input by 90°
Look at AC amplitudes
Look at phases
Output should peak when the input crosses zero

## Slide 10: Miller Integrator Theory
Work in Frequency Domain
Vout = -Zf/ Z1 * Vin
—
+
Vout
C
R1
+
Vin
—
I1
Rm
At very low frequencies
Inverting op amp
At high frequencies
Integrator
Active Low Pass Filter

## Slide 11: Miller Integrator Procedure
—
+
Vout
C = 1 μF
R1 = 10 kΩ
+
Vin
—
I1
Rm = 1 MΩ
Set function generator to zero output
R= 1 kΩ
Make sure that the output does not saturate
Make sure that any DC offset is not integrated

## Slide 12: Miller Integrator Procedure (cont.)
—
+
Vout
C
R1
+
Vin
—
I1
Rm
Compare magnitudes of input and output waves
Set function generator to give 6V amplitude sine wave
at f=1 kHz
Use the DC offset of the function generator to minimize DC component of output
Compare phases of input and output waves
Is the gain what you would expect?
Is the phase difference what you would expect?
Capture the input & output
Chart: Time
Ch. A
Ch. B

## Slide 13: Miller Integrator Procedure (cont.)
—
+
Vout
C
R1
+
Vin
—
I1
Rm
Compare magnitudes of input and output waves
The amplitude of the sine wave will need to be adjusted
Adjust DC offset to minimize DC component of output
Compare phases of input and output waves
Change the frequency to a lower frequency
Keep changing to lower frequencies until you see a noticeable change.
The change of phase will probably be more noticeable than the change in the gain
The change will probably not be noticeable until the frequency is less than 1 Hz
Capture the traces that show it acting like an integrator and traces showing it acting less like an integrator.