## Slide 1: Analog Electronics Technology
Lab 5
Active Filters

## Slide 2: Active Low-Pass Filter Circuit
The circuit is the same as the Miller integrator, but with different component values
—
+
Vout
C
R1
+
Vin
—
I1
Rf
At very low frequencies
Inverting op amp
At high frequencies
Integrator
I renamed the resistor Rf (f for feedback) instead of Rm (m for Miller)
Output can have more energy than the input
Miller 10 kΩ
LP 10 kΩ
Miller 1 MΩ
LP 100 kΩ
Miller 1 μF
LP 10 nF
, 1 nF
, 100 pF

## Slide 3: Comparing Integrator and Miller Integrator
Make a log-log plot of the transfer function, Vout/Vin
Chart: Miller Integrator Transfer Function
Inverting op amp
Integrator
Chart: phase
Chart: Integrator Transfer Function
Chart: phase
Corner Frequency

## Slide 4: Comparing Miller Integrator and Active Low-Pass Filter
Chart: Miller Integrator Transfer Function
Inverting op amp
Integrator
Chart: phase
Chart: Lowpass Filter 1 Transfer Function
Chart: phase
Rf/R1

## Slide 5: Comparing Active Low-Pass Filters
Chart: Lowpass Filter 2 Transfer Function
Chart: phase
Chart: phase
Chart: Lopwpass Filter 3 Transfer Function
Calculate Corner Frequency

## Slide 6: Active Low-Pass Filter Procedure
Calculate the corner (knee) frequency
—
+
Vout
C = 10 nF
R1 =100kΩ
+
Vin
—
I1
Rf =100kΩ
Set the function generator to produce a sine wave of 1.3 Volts at a frequency below the corner frequency
Function Generator
Adjust the DC level of the function generator if necessary.
Measure the input and output magnitude and phase.
Chart: Time
Repeat the measurements at two additional frequencies below the corner frequency, two or three frequencies near the corner frequency, and three frequencies above the corner frequency.
Adjust the magnitude and offset of the sine wave as warranted.
Ch. A
Ch. B

## Slide 7: Active Low-Pass Filter Procedure (cont.)
Calculate the corner (knee) frequency
—
+
Vout
C = 1 nF
R1 =100kΩ
+
Vin
—
I1
Rf =100kΩ
Set the function generator to produce a sine wave of 1.3 Volts at a frequency below the corner frequency
Change the capacitor to a 1 nF capacitor
Adjust the DC level of the function generator if necessary.
Measure the input and output magnitude and phase.
Chart: Time
Repeat the measurements at two additional frequencies below the corner frequency, two or three frequencies near the corner frequency, and three frequencies above the corner frequency.
Adjust the magnitude and offset of the sine wave as warranted.
Repeat the procedure from the previous slide

## Slide 8: Active Low-Pass Filter Procedure (cont.)
Calculate the corner (knee) frequency
—
+
Vout
C = 100 pF
R1 =100kΩ
+
Vin
—
I1
Rf =100kΩ
Set the function generator to produce a sine wave of 1.3 Volts at a frequency below the corner frequency
Change the capacitor to a 100 pF capacitor
Adjust the DC level of the function generator if necessary.
Measure the input and output magnitude and phase.
Chart: Time
Repeat the measurements at two additional frequencies below the corner frequency, two or three frequencies near the corner frequency, and at least two frequencies above the corner frequency.
Adjust the magnitude and offset of the sine wave as warranted.
Repeat the procedure from the previous slide

## Slide 9: Active Low-Pass Filter
Chart: Lowpass Filter 2 Transfer Function
Chart: phase
For each filter make a log-magnitude vs. log-frequency plot and make a phase vs. log-frequency plot.
Compare the plots with the expected results.