## Slide 1: Digital Signal Processing
Fall 2025

## Slide 2: Who am I?
Kendall Stephenson
Given name
Family name
Name:
Formal Greetings:
“Hello Professor Stephenson”
“Hello Mr. Stephenson”
Informal Greetings:
“Hi Kendall”
Instructor at Cornell College
Mount Vernon, Iowa

## Slide 3: What are Digital Signals?
Also called discrete signals
They can only have specific values
The opposite of analog (continuous) signals

## Slide 4: Example of an Analog (Continuous)Signal
Chart: Circuit Voltage
Chart: Circuit Voltage
| 4.0000000000000022E-2 | 4.2000000000000023E-2 | 4.4000000000000025E-2 | 4.6000000000000027E-2 | 4.8000000000000029E-2 | 5.0000000000000031E-2 | 5.2000000000000032E-2 | 5.4000000000000034E-2 | 5.6000000000000036E-2 | 5.8000000000000038E-2 | 6.0000000000000039E-2 | 6.2000000000000041E-2 | 6.4000000000000043E-2 | 6.6000000000000045E-2 | 6.8000000000000047E-2 | 7.0000000000000048E-2 | 7.200000000000005E-2 | 7.4000000000000052E-2 | 7.6000000000000054E-2 | 7.8000000000000055E-2 | 8.0000000000000057E-2 | 8.2000000000000059E-2 | 8.4000000000000061E-2 | 8.6000000000000063E-2 | 8.8000000000000064E-2 | 9.0000000000000066E-2 | 9.2000000000000068E-2 | 9.400000000000007E-2 | 9.6000000000000071E-2 | 9.8000000000000073E-2 | 0.10000000000000007 | 0.10200000000000008 | 0.10400000000000008 | 0.10600000000000008 | 0.10800000000000008 | 0.11000000000000008
 | 1.989 | 2.0289 | 2.0679 | 2.1061 | 2.1436 | 2.1804 | 2.2164 | 2.2518 | 2.2864 | 2.3203 | 2.3536 | 2.3862 | 2.4181 | 2.4494 | 2.4801 | 2.5102 | 2.5397 | 2.5687 | 2.597 | 2.6248 | 2.652 | 2.6787 | 2.7049 | 2.7305 | 2.7557 | 2.7803 | 2.8044 | 2.8281 | 2.8513 | 2.8741 | 2.8964 | 2.9182 | 2.9396 | 2.9606 | 2.9812 | 3.0014
Chart: Circuit Voltage
| 5.2000000000000032E-2 | 5.4000000000000034E-2 | 5.6000000000000036E-2 | 5.8000000000000038E-2 | 6.0000000000000039E-2 | 6.2000000000000041E-2 | 6.4000000000000043E-2
 | 2.2164 | 2.2518 | 2.2864 | 2.3203 | 2.3536 | 2.3862 | 2.4181

## Slide 5: Example of Function with Discrete Values for Vertical Axis
Chart: Students in Classroom

## Slide 6: Example of Function with Discrete Values for Both Axes
Chart: Peaches Produced in a Growing Season
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0 | 0 | 0 | 7 | 15 | 24 | 32 | 37 | 40 | 35 | 44 | 48 | 41 | 48 | 49 | 52 | 33 | 46 | 48 | 51 | 55
Kilograms of Peaches
Continuous

## Slide 7: Analog Signals are often Sampled to Make Digital Signals
Chart: 
Chart: Circuit Voltage

## Slide 8: Input & Output of a Discrete System
We will define the inputs of a discrete system as x[ n ]
We will define the output of a discrete system as y[n]
n is the index number
n is an integer
it tells us the position in the list
The inputs might be samples from a continuous variable
Example:
x[ ] = { 1, 7, 4, 2, 5 }
we usually start with zero
x[ 0 ]
x[ 1 ]
x[ 2 ]
x[ 3 ]
x[ 4 ]
We often call n the sample number even if it is not a sample of a continuous variable
Our goal or objective usually is to find a relationship between the outputs, y[n], and the inputs (and the other outputs)

## Slide 9: Multiplying a Sequence by a Constant
y[ n ] = 3 x[ n ]
When we multiply (or divide) a sequence by a constant, each term is individually multiplied by that constant
For inputs:
x[ ] = { 1, 7, 4, 2, 5 }
y[ ] = { 3, 21, 12, 6, 15 }
Example:

## Slide 10: Delays (Shifts)
y[ n ] = x[ n - 2 ]
A delay (or shift) in a sequence is indicated by subtracting an integer from the argument n
For inputs:
x[ ] = { 1, 7, 4, 2, 5 }
y[ ] = { 0, 0, 1, 7, 4}
Example:
Assume x[ n ] = 0 for all n < 0
y[ n ] = x[ n + 2 ]
An expression such as
indicates that the system is noncausal
This is not possible for a time-based systems operating in real time
The current output depends upon a “future” input
advancement instead of delay
Noncausal systems can be used for recorded signals and for systems that are not time based
filtering vocal recordings
image processing

## Slide 11: Basic Signals
The analysis of discrete signals uses basic signals that are similar to those used in systems with continuous signals
Unit Impulse
Unit Step
Chart: Unit Impulse
| -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Unit Step
| -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 12: Basic Signals
Real Exponential
Chart: Real Exponential
| -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 0 | 0 | 0 | 0 | 4 | 2.8 | 1.96 | 1.372 | 0.9604 | 0.67228 | 0.4706 | 0.32942 | 0.23059 | 0.16141 | 0.11299 | 0.079093 | 0.055365
Chart: Real Exponential
| -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 0 | 0 | 0 | 0 | 3 | 3.6 | 4.32 | 5.184 | 6.2208 | 7.465 | 8.958 | 10.7495 | 12.8995 | 15.4793 | 18.5752 | 22.2903 | 26.7483
Decaying Exponential
Increasing Exponential

## Slide 13: Basic Signals
sinusoidal
Chart: 4 sin( 0.1 π n)
compare to analog signals

## Slide 14: Basic Signals
Compare analog and digital sinusoidal signals
The functions are periodic (values repeat)
Relationships between periods and frequencies are not as simple for digital signals
T =
The function may repeat in a period, N
for every t
Period, T, is time in which the function repeats
This is true if
for every n
m is an integer

## Slide 15: Basic Signals
sinusoidal
Chart: 4 sin( 0.1 π n)

## Slide 16: Basic Signals
sinusoidal
Chart: 4 sin( 0.75 𝜋 n)
Let m = 3
Chart: 
300 Hz Signal
Sampled every 1.25 mS
3 Cycles
6 π radians

## Slide 17: Basic Signals
sinusoidal
Chart: sin( 0.5625 π n)
Let m = 9
900 Hz Signal
Chart: 
Sampled every 312.5 μS
9 Cycles
18 π radians

## Slide 18: Basic Signals
sinusoidal
No integer value of m will make N an integer
The function is not periodic
Chart: sin( 0.5 n)

## Slide 19: Basic Signals
Compare analog and digital sinusoidal signals
The functions are periodic
T =
The function may be periodic
The period is inversely proportional to the frequency
Frequency
If you double the frequency, you halve the period
Period, N
0.1
20
0.5625
32
0.75
8
0.5
nonperiodic

## Slide 20: Basic Signals
Oscillations of digital sinusoidal signals do not increase uniformly

## Slide 21: Basic Signals
Oscillations of digital sinusoidal signals do not increase uniformly

## Slide 22: Memoryless Systems
y[ n ] = 3 x[ n ]
A system is said to be memoryless if the output only depends upon the current input
Examples:
The output of systems with memory depends upon past inputs or past outputs.
y[ n ] = ( x[ n ] )2
They can also depend upon the current input.
y[ n ] = ( x[ n ] + x[ n-1 ] )/2
Example:

## Slide 23: Linear Systems
A system is linear if the principle of superposition applies
where a and b are constants
If the response of the system to the input x1[n] is y1[n]
and the response of the system to the input x2[n] is y2[n]
Then the system is linear if the response of the system to the input (a * x1[n] + b * x2[n]) is y[n] = a * y1[n] + b * y2[n]

## Slide 24: Time Invariant Systems
A system is time invariant (shift invariant) if a shift in time (index) of the input signal only changes the output by the same shift experienced by the input
The system is time invariant if
y1[ n ] = f( x1 [ n ] )
y2[ n ] = f( x1 [ n - k ] )
input shifted by k
y2[ n ] = y1[ n - k ] )

## Slide 25
Practice Problems

## Slide 26
Each of the equations below represents a system. For each system state whether the system is
causal and memoryless
causal with memory
noncausal

## Slide 27
Each of the following, state if the system is periodic
If the system is periodic, give the period, N