## Slide 1: Digital Signal Processing
Fall 2025

## Slide 2
Practice Problems

## Slide 3
Problem 1: A signal has a range from 0 Volts to +5 Volts and contains noise that has a root-mean-squared (rms) value of 2 mV. The signal is to be digitized by an A/D converter. The maximum permissible noise (after conversion) is 2.2 mV rms. What is the minimum number of bits for the A/D converter? What will be the noise level in the output of the A/D converter if this number of bits are used?
Find quantization noise (rms)
Find step size
Find number of bits

## Slide 4
Problem 1: A signal has a range from 0 Volts to +5 Volts and contains noise that has a root-mean-squared (rms) value of 2 mV. The signal is to be digitized by an A/D converter. The maximum permissible noise (after conversion) is 2.2 mV rms. What is the minimum number of bits for the A/D converter? What will be the noise level in the output of the A/D converter if this number of bits are used?
Find quantization error
Find total noise
Find step size
11 bit
12 bit
(rms)
(rms)

## Slide 5
Each of the signals below is to be sampled at the indicated frequency or period.
Indicate if aliasing will occur
If aliasing will occur, indicate the frequency at which the aliased signal will appear
If aliasing will occur, state the minimum sampling frequency (or maximum sampling period) needed to prevent aliasing
sampled at a frequency of 1000 Hz
sampled at a period of 25 mS
sampled at a period of 10 mS
sampled at a frequency of 800 Hz

## Slide 6
sampled at a frequency of 1000 Hz
300 Hz signal
rewrite equation
minimum sampling frequency to prevent aliasing is 600 Hz
The signal is being sampled at a rate higher than the minimum sampling frequency
No aliasing will occur

## Slide 7
sampled at a period of 25 mS
25 Hz signal
rewrite equation
T
The signal is being sampled at less than the minimum sampling frequency
50 Hz minimum sampling frequency
Aliasing will occur
(k = -1)
signal will appear at 15 Hz

## Slide 8
100 Hz signal
rewrite equation
T
The signal is being sampled at less than the minimum sampling frequency
200 Hz minimum sampling frequency
Aliasing will occur
(k = -1)
signal will appear at DC
sampled at a period of 10 mS
(0 Hz)
Chart: 100 Hz Signal and Sampling

## Slide 9
500 Hz signal
rewrite equation
The signal is being sampled at less than the minimum sampling frequency
1000 Hz minimum sampling frequency
Aliasing will occur
(k = -1)
signal will appear at 300 Hz
sampled at a frequency of 800 Hz