## Slide 1: Digital Signal Processing
Fall 2025
Signal Flow Graphs
Part 2

## Slide 2
Practice Problems

## Slide 3
Make a signal flow graph for the system described by the equation
y[n] = 2 x[n] – 6 x[n-1] + 2 x[n-3] – 4 y[ n – 2] + y[ n -3]
Practice Problem 1
Last session we learned how to make a ladder type arrangement to implement a linear constant coefficient difference equation
This is called the direct form 1 method
We will use that same method to solve this problem

## Slide 4
Signal Flow Graph Practice Problem
0
2
X[z]
Y[z]
-4
-6
0
y[n] = 2 x[n] – 6 x[n-1] + 2 x[n-3] – 4 y[ n – 2] + y[ n -3]
2
1
node a
𝑋[𝑧]
node b
node c

## Slide 5
General direct form 1 signal flow graph
X[z]
Y[z]
b0
b1
b2
b3
a1
a2
a3
Linear Constant Coefficient Difference Equations in z domain
rearrange
transfer function

## Slide 6
General direct form 1 signal flow graph
X[z]
Y[z]
b0
b1
b2
b3
a1
a2
a3
transfer function
cascaded transfer functions
For linear systems, cascaded transfer functions can be put in any order

## Slide 7
Does this really work?
X[z]
Y[z]
b0
b1
b2
b3
a1
a2
a3
node m
node n
p
q
r
s
t
u
c
d
e
f
Wp = Wm ∙ z-1
Wr = Wm ∙ z-2
Wt = Wm ∙ z-3
Wc = a3 ∙ Wm ∙ z-3
Wd = a2 ∙ Wm ∙ z-2 + a3 ∙ Wm ∙ z-3
We = a1 ∙ Wm ∙ z-1 + a2 ∙ Wm ∙ z-2 + a3 ∙ Wm ∙ z-3
Wf = a1 ∙ Wm ∙ z-1 + a2 ∙ Wm ∙ z-2 + a3 ∙ Wm ∙ z-3 + X[z]
Wm = a1 ∙ Wm ∙ z-1 + a2 ∙ Wm ∙ z-2 + a3 ∙ Wm ∙ z-3 + X[z]
Wm - a1 ∙ Wm ∙ z-1 - a2 ∙ Wm ∙ z-2 - a3 ∙ Wm ∙ z-3 = X[z]
Wm (1 - a1 ∙ z-1 - a2 ∙ z-2 - a3 ∙ z-3 ) = X[z]

## Slide 8
What is the advantage of this arrangement?
X[z]
Y[z]
b0
b1
b2
b3
a1
a2
a3
node m
node n
Wm = Wn
p
q
Wp = Wq = z-1 Wm
r
s
Wr = Ws = z-2 Wm
t
u
Wt = Wu = z-3 Wm
We now have two branches doing the same thing
We can combine them and simplify the circuit

## Slide 9
Simplified Signal Flow Diagram
X[z]
Y[z]
b0
b1
b2
b3
a1
a2
a3
This is called the direct form 2 method
This is also called a canonic direct form implementation
“direct form” means that the branch gains can be read directly from the difference equation
“canonic” means that it uses the minimum number of delays

## Slide 10
Other cascaded forms
transfer function
both the numerator and the denominator are polynomials in (z-1)
These can be factored
The factors can be used to make sections which can be cascaded together

## Slide 11
Example
transfer function

## Slide 12
1/3
1/2
-1/6
1/4
30
-1
-1/5
X[z]
Y[z]

## Slide 13
X[z]
Y[z]
zeros at gk
poles at ck
feed forward loop for each zero
feed back loop for each zero
General form for first order cascaded sections

## Slide 14
It is still possible to implement using complex arithmetic
(But no one wants to do that)
What if there are complex zeros or poles?
If our original coefficients were all real, then any complex zeros or poles will occur in complex conjugate pairs
The product of complex conjugate pairs has real coefficients

## Slide 15
Let’s look at what a second order stage looks like
Alternative

## Slide 16
Second Order Sections
X[z]
Y[z]
b0
b1
b2
a1
a2
X[z]
Y[z]
A
b1
b2
a1
a2
Both of these use the canonical direct form 2 method

## Slide 17
Second order sections are often used even if there are not complex zeros or poles
Three second order sections used to make a sixth order filter
X[z]
A
b11
b21
a11
a21
b12
b22
a12
a22
Y[z]
b13
b23
a13
a23
section 1
section 2
section 3
If there were only five zeros, then one of the “a” coefficients would equal zero

## Slide 18
Parallel forms
Once the polynomials have been factored, partial fraction expansion can be used to separate the transfer function into a series of fractions
If the order of the numerator is less than or equal to the order of the denominator, then this can take the form:
zeros at gk
poles at ck
Again, this can lead to complex poles and complex math.
The poles are usually combined in twos to make second order subsystems
The second order subsystems operate in parallel with the outputs added together

## Slide 19
Parallel forms
X[z]
A
b11
b21
a11
a21
b12
b22
a12
a22
Y[z]
b13
b23
a13
a23

## Slide 20
Parallel forms
e11
e01
a11
a21
Y[z]
X[z]
e11
e01
a11
a21
e11
e01
a11
a21

## Slide 24
b0
b1
b2
b3
a1
a2
a3